## Slide 1: Enabling AP power save – Follow Up
Date: 2024-01-12
Authors:
January 2024
Notes: September 2012

## Slide 2: Introduction
Nowadays mainstream APs are expected to be always in Active mode
  Operate using the highest bandwidths (BW) and # of spatial streams (NSS) so that
    Associated STAs can get the highest throughput and fastest service possible
And reducing AP power consumption has not gained sufficient traction
  Mainly because the APs are traditionally wall powered
However, the power consumed by APs is significant (tens of watts)
  And this energy needs to be generated somewhere which:
    Increases the maintenance costs of the network,
    Reduces the battery life of the device (if battery operated)
    Increased the ecological footprint of deployed networks
And is even more emphasized for multi link and multi-AP networks
  Since power consumption increases with the number of links/APs
January 2024

## Slide 3: Summary of existing AP power save modes
BW/NSS reduction: Advertised by any AP via operation (mode) IEs in beacons
  AP can reduce the max BW/NSS that associated STAs can use when exchanging frames
    Similarly, the AP can modify the MCS set as well
  Associated STAs are required to use the most recent BW/NSS/MCS sets advertised by the AP
Link Disablement: AP MLD temporarily disables the link of an affiliated EHT AP
  STAs on the disabled link either move to another BSS or suspend operation on that link (if multi-link)
  Requires the AP MLD to keep at least one enabled link to serve all associated STAs
Scheduled AP PS modes (available and advertised by an S1G AP)
  AP sets the Responder PM bit to 1 if the AP intends to go to doze state outside of TWT SPs
  AP explicitly indicates during which beacon interval (BI) it may go to doze state outside of SPs
    By setting the PM bit to 1 in the Beacon frame that precedes that BI
  The SPs can be the negotiated TWT SPs or certain restricted access windows (RAWs)
      STAS are expected to not transmit outside of these SPs
January 2024

## Slide 4: Limitations of existing AP PS modes
BW/NSS reduction (for 11n APs and beyond):
  Long term change that impact all associated STAs operating on that link
    Transition duration is in the order of several DTIM periods
    Reduced throughput and/or increased latency during reduced BW/NSSs period
      Which is also in the order of DTIM periods
Link Disablement (for 11be APs and beyond):
  Long term changes that impact all STAs operating on that link
    Transition duration is in the order of several DTIM periods
    No throughput and no service (“infinite latency”) during the disabled period
      Which is also in the order of DTIM periods
      Some consequential impact on the enabled links of that AP MLD as well
        E.g., increased loads on enabled links due to traffic steering from disabled links
Scheduled AP PS modes (for 11ah APs):
  Medium term changes that impact all STAs operating on that link
    Transition duration is in the order of beacon intervals
    No throughput and no service outside of the service periods
      Which is in the order of tens of milliseconds
January 2024

## Slide 5: Candidate AP PS modes for UHR
Scheduled AP PS
  E.g., TWT-based ON-OFF duty cycling of AP’s operation
  Medium term changes that impact all STAs operating on that link
    E.g., based on scheduled doze service periods within beacon intervals
Dynamic AP PS
  E.g., based on dynamic SM PS/eMLSR enablement at the AP side
  Short term changes that impact all STAs operating on that link
    E.g., initial control frame usage to enable higher BW/NSS modes
The focus of this presentation is to provide context for an SP for the scheduled AP PS case
  More details for dynamic AP PS provided in another contribution
January 2024

## Slide 6: Overall Summary
Qualitative overview of the different AP PS modes
An AP MLD could use a combination of different AP PS modes
  To minimize the overall power consumption of the system while
  Minimizing the impact to the KPIs of the associated STAs
Next, we provide additional insights on two candidate AP PS modes
  First covering scheduled AP PS,
  Then covering dynamic AP PS
AP PS modes | Status | Inactive Periods | Active Periods | Inactive/Active Duration | PS benefits | KPI1 impact
BW/NSS-based | Baseline | None | All | None/All | Medium | Medium
Link Disablement | Baseline | In Disabled Links | In Enabled Links (At least one link) | ~ Seconds or more (order of DTIM interval) | High2 | Higher
Scheduled AP PS | UHR Candidate | Outside Wake SPs | Within Wake SPs | ~ Tens of ms. or more | Medium3 | Medium3
Dynamic AP PS | UHR Candidate | None | All | None/All | Medium | Minimal
Key performance indicator (KPI) refers to one of throughput, latency or reliability. AP power save is the highest on the disabled links, with no power save on the enabled link. There is a trade-off between AP PS and KPI impact which depends on the on-off duty cycle. | Key performance indicator (KPI) refers to one of throughput, latency or reliability. AP PS is the highest on the disabled links, and no AP PS on the enabled link. There is a trade-off between AP PS and KPI impact which depends on the on-off duty cycle |  |  |  |  | 
January 2024

## Slide 7: Scheduled AP PS for UHR
Requirements at the AP:
  Generate Beacons, and certain MGMT frames in non-HT PPDUs (baseline)
  Generate DL PPDUs (subject to assoc. STAs’ caps., and op. modes (baseline))
  RX of UL PPDUs is subject to the AP being in Awake state (new requirement)
    I.e., new rules are needed to avoid STAs sending frames to an AP that is in Doze state
  Mode enabled by AP only if all associated STAs support the AP entering this mode
Target:
  Enable AP to save power outside of awake SPs
    The longer inter-SP separation the lower the power consumption
  Simplicity and predictability from a protocol perspective
    STAs either negotiate or know in advance the periods during which the AP is expected to be in doze state
    Use existing mechanisms (e.g., use TWT-based AP PS & set dot11APPowerSaveImplemented to true)
January 2024

## Slide 8: Scheduled AP PS for UHR (cont.)
Issues that need careful consideration:
  Opportunities for AP to save power are highly dependent on the STAs associated to it (whether they support it)
  Active scanning is not possible during periods when AP is in doze state
  Sleep patterns of the AP need to consider the QoS parameters of the associated STAs
    Trade-off between STAs’ traffic requirement and AP’s power consumption
Could be addressable by using scheduled AP PS with MLO
  Require one link to be always enabled (in AM mode) while the other links use scheduled AP PS
    Legacy STAs and STAs that don’t support scheduled AP PS operate on the AM link (which provides active discovery as well)
January 2024

## Slide 9: Dynamic AP PS for UHR
Requirements at the AP:
  DL and beacon generation are the same as baseline (see previous slide)
  RX UL PPDUs subject to initiating frames that precedes them satisfying strict requirements
    These initiating frames will cause the AP to transition from Listen State to Awake State
    Need to define rules to enable this (dynamic SMPS/eMLSR-like) functionality at AP side
      E.g., by requiring initiating frames (e.g.. RTS frame) be carried in non-HT (dup) PPDU format, etc.
  Mode enabled by AP only if all associated STAs support the AP entering this mode
Target:
  AP to save power (e.g., stay in Listen State) most of the time, unless solicited to Awake
    Listen State: AP is capable of RX PPDUs of a certain configuration (e.g., non-HT (dup) PPDUs, etc.)
    Awake State: AP is awake & capable of RX PPDUs with highest BW/NSS (e.g., advertised in Beacons)
  Simplicity and predictability from a protocol perspective
    Require that every exchange is initiated with a frame exchange that causes transition from listen to awake
      E.g., define dynamic SMPS/eMLSR-like protocols at the AP side
Issue that needs careful consideration (see next slide)
  Use of dynamic AP PS is highly dependent on what STAs are associated to it
January 2024

## Slide 10: Dynamic AP PS for UHR (cont.)
An AP in dynamic AP PS is expected to natively support active & passive scanning
  Pre-association UL frames are expected to be exchanged in non-HT PPDU format
  And AP can decide what format to use for DL frames, but generally
    Uses non-HT PPDU format for Beacons, Probe Responses, and so on
To avoid missing UL frames being sent by associated STAs, either of these rules need to apply:
  An AP may go to Listen State only when all associated STAs are (capable of) initiating their exchanges with non-HT (dup) PPDU
    E.g., the AP must disable dynamic AP PS if there is at least one associated STA that does not support it
  An AP MLD must keep at least one link where dynamic AP PS mode is disabled
    If there is at least one STA that does not support dynamic AP PS, then they must operate on that link
January 2024

## Slide 11: Conclusions
We have discussed candidate power save protocols for the AP aiming at
  Minimizing power consumption while ensuring that STAs continue to be serviced without disruptions
  Accounting for the necessary trade-offs/constraints
    Which arise due to use cases/scenarios and/or device configurations
We covered both
  Scheduled AP PS: medium term PS mode that enables deep sleep in the form of
    Doze state (DS): AP enters doze state (i.e., powered off) and is
      Capable of storing association states but has no RX/TX functionalities
  Dynamic AP PS: short term PS mode that enables light sleep in the form of
    Listen state (LS): AP has limited operation (e.g., RX/TX@High BW/NSS are off) and is
      Capable of maintaining minimal RX functionality (e.g., RX non-HT PPDU only)
January 2024

## Slide 12: Straw Poll 1
Do you support to enable a mechanism that allows a STA to advertise (and eventually update) periodic unavailability time intervals to its peer STA(s)?
  Expectation is to use existing mechanism
  Mechanism can be enabled only if it is supported by the peer STA(s)
January 2024