## Slide 1: TGbi Epoch proposal
Date: 2023-10-28
Authors:

## Slide 2: Abstract
Define an epoch for when a client should change the Over The Air (OTA) MAC address that is being used.

## Slide 3: Epoch Partitioning Idea
Partition time into epochs based on network trust*:​
Fully Untrusted – Open/OWE – Rotate every 5 mins ​
Semi Untrusted – PSK – Rotate every 10 mins. ​
Trusted - 802.1X - Rotate every 10 mins – optional​ (enabled if using IRM)
  Passpoint treated as Fully Untrusted
By defining epochs based on association duration, both the AP STA and non-AP STA will know when they should rotate to the new IRM​, calculation could happen anytime during the current epoch
This allows for a dynamic approach as not all non-AP STA will rotate at the same time, making it more difficult for an eavesdropper to know a rotation happened vs STA joining/leaving
*non-AP STA can override the default network type in the supplicant configuration

## Slide 4: Update/Sunset
Announce time – Tell AP-STA when we will start to use new IRM – sent in a protected frame​
e.g. in 1 minute STA will use new IRM​
Once announce time has elapsed, Sunset timer starts.​
Sunset timer – DTIM period * 5​
Frames in the queue should still be transmitted during the Sunset period
Old mac shall not respond and AP shall not forward packets for old IRM once Sunset timer has elapsed.