## Slide 1: Multiple Channel Access in Preemption Sequence
Date: 2023-11-13
Authors:

## Slide 2: Abstract
The tail of latency reduction is one of 11bn’s objectives.
To improve latency performance, preemption methods were discussed.
The preemption methods, in which an AP coordinates preemption, were discussed[1, 2].
  STAs transmit pre-emption request frames within an inter-PPDU spacing.
  Contention resolution phase follows pre-emption request phase.
The preemption methods with random access between STAs were also discussed [3].
  STAs contend for medium for latency sensitive frame within an inter-PPDU spacing.
  Once a STA succeed in channel contention, the STA transmits the latency sensitive frame immediately.
This submission

## Slide 3: Recap: Coordinated preemption method (Coordinate)
The discussed preemption method uses AP’s coordination
  This method can reserve transmit slots for STAs
    Collision probability can be decresed
  However, coordination overhead may occur
[1]: 23/1229r1, Juan Fang
Coordination

## Slide 4: Recap: Random Channel Access for Preemption (Random)
[3] discussed the necessity of random channel access within an inter-frame spacing
There are some candidates of random channel access schemes:
  E.g., DCF-like operation

## Slide 5: Example: DCF-like Backoff Scheme
This example is showing one of the random access method for preemption.
STAs perform short-term backoff within inter-PPDU spacing (XIFS)
  XIFS should be long enough to perform backoff operations.

## Slide 6: Comparison between Coordinate and Random Methods
1. Small number of STAs which perform preemption:
  When only a small number of STAs perform preemption, the random method is advantageous for quick transmission as it does not require separate coordination.
  However, an overhead of the coordinate method may occur inefficiency when only a small number of STAs perform preemption.
2. Large number of STAs which perform preemption:
  When a large number of STAs perform preemption, the coordination method has the advantage of a lower probability of collision and better resource management.
  However, as the number of STAs performing preemption increases, the probability of collision also rises in the random method. Therefore, inefficiency can occur when using the random method.

## Slide 7: Summary
In this submission, the two channel access methods for UL SU preemption was discussed
  1. Coordinated Method
  2. Random Access Method
In the coordinated method,
  STAs can access channel without collisions
  Overheads for coordinating STAs will be occurred
In the random-access method,
  STAs can access channel without coordination overheads
  Collisions may occur between STAs

## Slide 8: References
[1] 11-23/1229r1: Preemption for low latency application (Follow up), https://mentor.ieee.org/802.11/dcn/23/11-23-1229-01-0uhr-preemption-for-low-latency-application-follow-up.pptx
[2] 11-23/1174r0: TXOP preemption follow up, https://mentor.ieee.org/802.11/dcn/23/11-23-1174-00-0uhr-txop-preemption-follow-up.pptx
[3] 11-23/1242r1: Considerations on Inter-PPDU based Preemption Scheme, https://mentor.ieee.org/802.11/dcn/23/11-23-1242-01-0uhr-considerations-on-inter-ppdu-based-preemption-scheme.pptx