## Slide 1: Coex Enhancement for XR Use Cases
Date: 2023-11-07
Authors:
Name | Affiliations | Address | Phone | email
Guoqing Li Kumail Haider Carlos Aldana Claudio De Silva Davide Magrin Connor Kennedy Dong Zheng | Meta |  |  | guoqingli@meta.com

## Slide 2: Problem Statement
XR devices may use multiple radios such as Wi-Fi and Bluetooth and need to coex well
Device constraint issue
  Due to size and cost, these radios may share RF components and have to time share the RF resources
  Due to possible low isolation, one radio’s Tx may destroy another radio’s Rx
  In addition, Tx+Tx or Rx+Rx may not be possible depending on device’s architecture design and cannot be assumed as default
AP rate adaptation issue
  BT traffic interval may be at a few ms (<10ms) and Wi-Fi may not have sufficient time to notify AP its unavailability using power save signaligns (e.g., PM) when switching to BT activity
  As a result, downlink throughput/latency may be greatly degraded from AP’s fast rate scaling down due to lack of response from STA
Wi-Fi packet duration issue
  BT typically has periodic traffic and need to Tx/Rx at predicted time slot
  However, AP/STA may continue Tx tinto BT’s Tx/RX slot, leading to either Wi-Fi packet loss or BT packet loss

## Slide 3: Coex Enhancement
A client (STA) device may be aware of its co-located BT traffic profile and traffic interval and may shape its Wi-Fi Tx/Rx trafic to fit into BT gaps
STA may be able to control its uplink Tx activity, but has not mechanism to control AP’s DL activity
Proposal
  Define a mechanism that allows STA to request AP to control the following
    Max DL packet duration
    Min Tx interval
    Slow DL rate control when lack of UL BA
  BT activity usually will last a few seconds to minutes, thus these parameters can negotiated through management frames