## Slide 1: AIML Report and Next Steps for AIML Related Work
Date: 2023-11-10
Authors:

## Slide 2
Authors (continued):

## Slide 3: Abstract
This contribution provides a summary of the AIML TIG Technical Report
The technical report includes:
  Identified AIML Use case for IEEE 802.11
    Use case that enables AIML in WLANs (hence making IEEE 802.11 deployment-ready for AIML)
    Use cases that leverage AIML for performance enhancement for WLANs
  Feasibilities, KPIs and requirements for IEEE 802.11 features required to address these use cases.
  Standard impact to the IEEE 802.11 specifications
Discussion of the next steps for AIML related work in IEEE 802.11.

## Slide 4
Background (1/2)
AIML has seen tremendous progress in the past decade and has been used in many areas of technologies
  Medical diagnosis
  Speech recognition
  Computer vision
  Wireless communications
  Much of the AIML related traffic (including traffic for model distribution) is expected to be carried by WLANs
In addition, IEEE 802.11 networks and devices may benefit from utilization of AIML algorithms to improve performances and user experience
Various wireless communications technologies are developing/have developed specifications work for AIML, e.g.,
  3GPP has introduced AIML-based network functionality in Rel-15 (5G, initial release in 2017) and it is further enhanced in Rel-16 and Rel-17
  AIML-related technology for air interface has been a study item for Rel-18 and is very likely becoming a work item in Rel-19 starting in 2024
November 2023
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 4

## Slide 5
Background (2/2)
The AIML TIG started working in July 2022 to:
  (a) describe use cases for Artificial Intelligence/Machine Learning (AI/ML) applicability in 802.11 systems and
  (b) investigate the technical feasibility of features enabling support of AI/ML.
The current version of the AIML TIG report can be found in [2]
November 2023
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 5

## Slide 6
Summary of the the AIML TIG Technical Report (1/3)
The AIML TIG has studied two categories of AIML use cases for WLANs
One use case that enables AIML deployment in WLANs:
  Efficient AIML model sharing [5]: including
    1) models that are used for enhancing WLAN performances
    2) models used for other AIML applications that are carried by the WLAN networks
Four use cases that that leverage AIML techniques to enhance the performance of WLANs
  AIML-based CSI feedback compression/enhancement [3]
  Deep-learning based distributed channel access [4]
  Efficient AIML model sharing [5]
  AIML-based roaming enhancement [6]
  AIML-based multi-AP coordination [7]
For each use case, the following aspects are being defined:
  Standards impact to the IEEE 802.11 specifications: to provide an estimate of scope of work needed
  KPIs
  Requirements
  Technical feasibility
* Please see appendix for the details for each of the use cases
November 2023
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 6

## Slide 7
Conclusions
In order to enable and support AIML algorithms in IEEE 802.11 network and devices and in order to leverage AIML techniques to enhance IEEE 802.11 network performance, features that are needed to address the AIML use cases identified in this technical report can be achieved with a reasonable amount of work within the scope of the IEEE 802.11 WG.
In order to support generic AIML algorithms in IEEE 802.11 networks and devices, general management and support features, such as capability indication, control and model distribution of AIML technology deployment are needed in the IEEE 802.11 specifications for all AIML-based use cases.
November 2023
Summary of the the AIML TIG Technical Report (2/3)
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 7

## Slide 8
Recommendations
IEEE 802.11 should commence further study and work related to AIML technologies. In particular, efforts and standards changes to make the IEEE 802.11 standards deployment-ready (i.e., general support and management) for AIML techniques should be defined.
IEEE 802.11 should also consider defining features and capabilities in which AIML techniques are leveraged to enhance network performance and user experience when using IEEE 802.11 networks and devices. Privacy considerations should also be studied during further AIML related work.
November 2023
Summary of the the AIML TIG Technical Report (3/3)
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 8

## Slide 9
Based on the recommendations
Make the IEEE 802.11 standards deployment-ready (i.e., general support and management) for AIML techniques.
  AIML technology and traffic are coming to IEEE 802.11 networks and devices
  Other wireless communication specifications are progressing rapidly, e.g., 3GPP is expected to define AIML related specifications for air interface starting in 2024
    Operators may expect similar manageability of AIML techniques for IEEE 802.11, particularly for WiFi offloading and WiFi calling
IEEE 802.11 should consider defining features and capabilities in which AIML techniques are leveraged to enhance network performance and user experience when using IEEE 802.11 networks and devices.
Such work may be in the form of a SG aiming to provide specification changes
  Identified standards impact to the IEEE 802.11 standards for features targeting the various AIML use cases can be achieved with a reasonable scope of work
November 2023
Next Steps for AIML related work in IEEE 802.11
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 9

## Slide 10: References
[1] 11-22/597r3: May 2022 Working Group Motions, May 18, 2022
[2] 11-22/987r24: AIML TIG Technical Report Draft, Nov 2023
[3] 11-22/1934r5: Proposed AIML TIG Technical Report Text for the CSI Feedback Compression Use Case
[4]11-22/2119r1: Proposed AIML TIG Technical Report Text for the Distributed Channel Access Use Case
[5] 11-23/0050r2: Proposed AIML TIG Technical Report Text for the AIML Model Sharing Use Case
[6] 11-23/475r4: Proposed IEEE 802.11 AIML TIG Technical Report Text for the AIML-based Roaming Enhancements Use Case
[7] 11-23/227r4: Proposed IEEE 802.11 AIML TIG Technical Report Text for the Multi-AP Coordination Use Case
[8] 11-23/1072r0: AIML methodology for dynamic spectrum sharing and coexistence

## Slide 11: Appendix

## Slide 12
Highlights of AIML Use Cases Identified for WLANs (1)
We highlight in this report AIML use cases that have already been motioned into the AIML TIG Technical Report [2]
  AIML-based CSI feedback compression/enhancement [3]
  Deep-learning based distributed channel access [4]
  Efficient AIML model sharing [5]
  AIML-based roaming enhancement [6]
  AIML-based multi-AP coordination [7]
November 2023
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 12

## Slide 13
Highlights of AIML Use Cases Identified for WLANs (2)
Efficient AIML model sharing/distribution [5]
Efficient AIML model distribution is essential for many AIML-based operations in WLANs and for performance of WLANs
  In centralized learning/federated learning, large amount of traffic are used to distribute AIML models/training data among participating devices (STAs and APs), in UL, DL and P2P links
  Efficient AIML model distribution protocols are needed to enable support AIML operations
    Including sharing of all AIML models (e.g., for other applications; these model sharing is expected to be carried by WLANs anyway), not just for models used to improve WLAN performance (such as NN models)
Feasibility: Efficient AIML model distribution can leverage the broadcast nature of WLANs
  802.11bc defines UL/DL broadcast services for both associated and unassociated STAs/APs, providing a good set of baseline tools for AIML model distribution
Standards impact to the IEEE 802.11 specifications:
  Architecture that enables AIML model sharing on the MAC layer
  Signaling and protocols related to AIML model sharing support/capability indication and management
KPI: medium occupation time saving compared to model sharing using application layer data
November 2023
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 13

## Slide 14
Highlights of AIML Use Cases Identified for WLANs (3)
AIML-based CSI Feedback Compression/enhancement [3]
Sounding procedures in WLANs represent large overhead particularly with potential new features:
  Higher number of spatial streams, e.g., 16
  Multi-AP features such as joint transmissions
Studies show that AIML algorithms may efficiently reduce CSI feedback/improve system throughput
  using unsupervised learning algorithms to significantly reduce CSI feedback into clusters while maintaining similar PER performance
  E.g., AIML-aided dual CSI compression combines codebook and Givens Rotation which leverage K-means ML algorithm
  E.g., AIML algorithm may be used to reduce the computation complexity for CSI feedback, such as quantization of the right singular matrix using an autoencoding-based algorithm
Standards impact to the IEEE 802.11 specifications :
  Additional signaling (or new signaling design) between AP an STAs required by AIML process to provide (e.g., newly designed) feedback and/or cluster information
  AIML model sharing (also see AIML Model Sharing Use case)
KPIs:
  CSI airtime reduction/additional AIML process overhead
  PER
  Computation complexity/latency
  Storage needed for AIML models
November 2023
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 14

## Slide 15
Highlights of AIML Use Cases Identified for WLANs (4)
Deep-learning based distributed channel access [4]
Performances of traditional WLAN channel access designs such as DCF degrade in dense deployment, unable to support stringent QoS requirements such as
  Ever increasing throughput
  Low latency
Study has shown that deep learning algorithms can efficiently increase throughput and reduce latency and jitter while maintain fairness to other devices
  E.g., using Deep reinforcement learning for contention window optimization
  E.g., AIML algorithm selects whether to transmit after the channel has been idle for DIFS
Standards impact to the IEEE 802.11 specifications :
  Signaling and protocols related to parameter exchange between AP and non-AP STAs, e.g., capability indication, data report to facilitate training, neural networks parameters distribution, etc.
KPIs:
  Throughput improvement
  Latency and jitter reduction
  Additional complexity
November 2023
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 15

## Slide 16
Highlights of AIML Use Cases Identified for WLANs (5)
AIML Enhanced Roaming [6]
Roaming may occur frequently in dense AP deployments, affecting device battery lifetime and user experience
  Multi-AP networks commonly see a high level of roaming events
  A large number of roaming candidate APs/channels in use can cause STA scanning process to take a long time
  Candidate APs in 802.11k neighbor report are useful, however, not all RF neighbor APs are equally relevant for roaming
Efficient AIML techniques may be applied to
  Augment 802.11k neighbor report with weight for each candidate AP for prioritization of scanning
  Assist the STA to find the optimal mid-point between APs to start scanning and roam
Standards impact to the IEEE 802.11 specifications :
  Enhanced 802.11k neighbor report with weight of roaming neighbor AP candidates
  Triggering STAs to scan at mid-point between APs may require enhancement of BTM request frame
  Feedback for roaming recommendation by using enhanced BTM response frame
KPI:
  Scanning/Roaming time
  Roaming failure rate
  MCS distribution/Retry rate during a BSS transition
  RSSI at reattach time
November 2023
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 16

## Slide 17
Highlights of AIML Use Cases Identified for WLANs (6)
AIML based Multi-AP Transmission [7]
In OBSS scenarios, multi-AP coordinated transmissions can improve network performance
  Multi-AP coordinated transmission is expected to be a feature of UHR SG/802.11bn
  Configuring such transmissions is challenging due to varying network and radio conditions and outside interference (neighboring, non-coordinating BSS)
AIML models can be learnt and help make decisions/predict
  Find AP-STA pairs, select multi-AP transmission schemes and associated parameters, select when to transmit, etc.
  Exact multi-AP schemes depend on work in UHR/802.11bn but may include C-TDMA, C-OFDMA, C-SR, C-BF and JT
Standards impact to the IEEE 802.11 specifications :
  Additional signaling for exchanging training data/measurement reports/model sharing
KPI:
  Network performance metrics (throughput, latency and jitter, power efficiency) – measured at the BSS level but also aggregated over the whole multi-AP network
  Fairness – to ensure that all users are fairly served
  AIML overhead – additional signaling, computational complexity, and learning latency
November 2023
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 17