## Slide 1: WBA E2E QoS – QoS over Wi-Fi Links
Date: 2023-07-07
Authors:

## Slide 2: Abstract
Document 23/1206 was presented in the July 23 Plenary where we described the WBA E2E QoS project Phase-1. We also mentioned a Phase-2 of the project where E2E QoS (optimizing QoS end-to-end over links that are not exclusively IEEE802.11 links).
This presentation is a follow up, identifying higher layer protocols for latency optimization, and intends to start a discussion to determine
What information needs to be exchanged between the IEEE802.11 MAC layer and higher layers to facilitate higher layer protocols over IEEE802.11 MAC?
Is there a need for over-the-air signaling between IEEE802.11 MAC peers? And if so, what are they?
Is there any implementation requirements in the IEEE802.11 MAC layer to support the higher layer functions/features?

## Slide 3: General Approach to mitigating latency issues
At each node in the path between the Talker and the Listener, keep buffering small enough to meet latency requirements
Proactively signal congestion conditions and
  Leverage drop-eligibility, if available
  Provide feedback to the Talker to take corrective action(s)
    E.g., adapt to congestion conditions by reducing requirements (drop to a lower video resolution, more aggressive compression, etc.)
  Other IEEE802.1 techniques like Congestion Avoidance, Congestion Isolation (IEEE802.1Q-2022 and IEEE802.1Qcz-2023)
Some implementation-specific strategies
  Distinct queues for latency-bound and non-latency-bound traffic (in some cases DSCP-agnostic)

## Slide 4: End-to-End QoS Enablement in Wired/Wireless (IEEE802.11) deployments
Leveraging .1Qcz mechanisms (IEEE802.1Qcz-2023 Cl. 49) and IEEE802.1Q-2022 Clause 30 (Principles of Congestion Notification)
Low Latency Low Loss Scalable Throughput (L4S)
  a fast and explicit feedback loop from the network node managing the queue latency to the end systems and applications

## Slide 5: What is needed?
Decision on supported topologies – Is Wi-Fi Mesh (not .11s) a candidate?
Support for ECN – IP Headers, LLDP TLV (Access Points)
  IEEE802.11 STAs need to be .1Q compliant – does this mean support for .11ak?
Support for Network Congestion Notification – above the IP layer (e.g., RTP over UDP or TCP headers)
L2 Signaling in 802.1 for support (in higher layers)?

## Slide 6: References
https://mentor.ieee.org/802.11/dcn/23/11-23-2065-00-0wng-l4s-and-implications-for-wi-fi.pptx Greg White (CableLabs)
L4S Architecture: https://www.ietf.org/archive/id/draft-ietf-tsvwg-l4s-arch-19.html
Discussion on considerations prior to deploying L4S over Wi-Fi: domos.no/blog/an-introduction-to-l4s

## Slide 7: Backup