## Slide 1: UHR MLD Mobility Improvement
Date: 2024-04-16
Authors:
Name | Affiliation | Address | Phone | Email
Yonggang Fang | MediaTek |  |  | yonggang.fang@mediatek.com
James Yee | MediaTek |  |  | 
Gabor Bajko | MediaTek |  |  | 
Kaiying Lu | MediaTek |  |  | 
Li-Hsiang Sun | MediaTek |  |  | 
Frank Hsu | MediaTek |  |  | 

## Slide 2: Introduction
This contribution discusses mobility improvement in in UHR MLD networks.

## Slide 3: Motivation
Mobility Issues
  In a typical home or enterprise WLAN, multiple access points (APs) are used to improve the radio coverage of a single AP.
  A STA may experience issues of roaming among APs:
    Transition Reliability: Failure to establish a stable connection to a target AP
    Transition Delay: (1) re-authentication (2) re-association with a target AP, causing tens to a hundred of milliseconds of delay of access service
    Transmission Delay/Lost: the buffered data may be delayed beyond QoS requirement or lost due to transition delay
    Link Quality: the new connection to the target AP may not have sufficient QoS for the roaming STA.
  Service Impacts
  Roaming can cause a service interruption of application in upper layers
  Degrade QoS and QoE, especially for time sensitive applications.

## Slide 4: Motivation
Objectives and Possible Solutions
  Define a measurement for roaming performance
  Verify a target AP reachability to improve roaming transition reliability
  Improve roaming stability

## Slide 5: Roaming Performance Measurement
    Roaming failures
  failure to setup the connection to a target AP
  the transition delay beyond the QoS delay bound of MSDUs
  transmission reliability less than the QoS reliability requirement during roaming
Roaming success ratio
  (1 – (the total number of roaming failures / the total number of roaming at a given period) ) x 100%

## Slide 6: UHR MLD Roaming Procedure
  An Example of Roaming Stages
  Stage 1: non-AP MLD gets neighbor AP(s) information, including traffic load, traffic latency (DL/UL), link reliability ratio.
  Stage 2: non-AP MLD selects best reachable AP(s), re-configure and enable the link of target AP(s).
  Stage 3: non-AP MLD performs data frame exchanges with the source and/or the target AP(s).
  Stage 4: non-AP MLD disables the link to the source AP(s) when it is not reachable or reliable.
Non-AP MLD
AP2 (Target)
AP1 (Source)
Stage 1
Discovery of
target APs
Stage 2
(1) Select the best target AP(s)
(2) Reconfigure and enable the link(s) to the target AP(s)
Stage 3
Communicate with the source AP and/or target AP
Stage 4
Disable the link to the source AP when it is not reachable or reliable

## Slide 7: Roaming Transition Reachability & Reliability Improvement
  Reachability & Reliability in Transition
  Reachability: a target AP on same/different channel is reachable.
  Reliability: the transmission on a link is reliable especially in OBSS case.
  Target link quality: has sufficient QoS for applications on the roaming STA.
AP MLD0
AP MLD2
AP MLD1
AP MLD3
AP MLD4
AP MLD6
AP MLD5
  Stage 1:
  An AP may have multiple neighbor APs.
  A neighbor AP of the serving AP to the STA may not be a candidate AP that the STA to roam to
  A serving AP needs to provide more information of potential candidate APs to the STA to assist the roaming procedure
  Proposal
  Provides candidate neighbor AP(s) information, including traffic load, traffic latency (DL/UL), reliability ratio
    In unicast management frames, or
    In Beacon frames
AP MLD0 has 6 neighbors.
2 candidate neighbors for the non-AP MLD

## Slide 8: Roaming Transition Reachability & Reliability Improvement
  Stage 2 & 3
  A roaming STA performs frame exchanges with the source AP(s) to setup a connection to the target AP on same or different channel.
  The roaming transition to the target AP may happen at the time different from the time of target link setup
  High possibility of roaming failure may be caused by radio condition, like interference, lower RSSI/SNR, busy on target AP, etc.
  Proposal
  Roaming STA performs control frame exchange with target AP(s) to verify the link reachability and reliability to the target AP before data frame exchanges with the target AP in the roaming transition.
Source AP
Target AP
Frame exchange to verify the reachability & reliability
Setup a connection to target AP

## Slide 9: Roaming Transition Stability Improvement
  Roaming Stability
  A roaming non-AP MLD may frequently roam-in & roam-out among APs. This may cause transmission performance degradation and network congestion.
  Proposal
  Define roam-in and roam-out thresholds to control frequent link reconfiguration or update, and frequent roaming transitions.
  The roaming thresholds are sent through APs to a non-AP MLD.
  A non-AP MLD performs ML Reconfiguration/Update, and transition accordingly.
AP2
AP1
Non-AP MLD
AP2
AP1
Non-AP MLD
AP2
AP1
Non-AP MLD
Frequent Roaming-In & Roaming-Out
Before Roaming-In
After Roaming-Out

## Slide 10: Summary
This contribution discusses UHR mobility improvement
  Define roaming performance measurement
  Improve roaming success via checking reachability and reliability
  Reduce frequent roam-in and roam-out among AP MLDs