## Slide 1: TXOP bandwidth expansion
Date: 2023-12-20
Authors:
Name | Affiliations | Address | Phone | email
Shawn (Sanghyun) Kim | WILUS Inc. | 216 Hwangsaeul-ro, Seongnam-si, Gyeonggi-do, Korea | +82-31-712-0523 | shawn.kim@wilusgroup.com
John (Ju-Hyung) Son |  |  |  | john.son@wilusgroup.com
Jin Sam Kwak |  |  |  | jinsam.kwak@wilusgroup.com
Greg Geonjung Ko |  |  |  | greg.ko@wilusgroup.com
December 2023
Sanghyun Kim (WILUS), et al.

## Slide 2: Abstract
Several contributions have been submitted to improve the utilization of the secondary channel for 11bn
  Non-primary(secondary) channel access [1-5]
  Dynamic subband operation [6][7]
  Subchannel selective transmission [8]
The above contributions aim to acquire a TXOP through the secondary channel or enhance the utilization of a TXOP by allocating STAs to secondary channels
In this contribution, we present a method to expand the bandwidth of the acquired TXOP, improving accessibility to the secondary channels while ensuring fast channel access
December 2023
Sanghyun Kim (WILUS), et al.

## Slide 3: Wide bandwidth channel access (baseline)
When a STA is accessing a wide channel and encounters insufficient available bandwidth, it can opt for one of the following two alternatives:
  Option 1: Initiate Tx only using available subchannels
  Option 2: Invoke the backoff procedure again (choose not to Tx)
December 2023
Sanghyun Kim (WILUS), et al.
3
2
1
0
IDLE
Frame exchange (40 MHz)
TXOP
OBSS TXOP
BUSY
BUSY
P20
S20
S40
3
2
1
0
IDLE
OBSS TXOP
2
1
0
5
4
3
2
1
0
4
3
2
1
BUSY
BUSY
Chose not to transmit (invoke BO procedure)
IDLE
IDLE
IDLE
Frame exchange (80 MHz)
…
P20
S20
S40
TXOP

## Slide 4: Problems
A STA may select the previous:
  Option 1 when it has a Low Latency (LL) traffic
  Option 2 when it has a substantial volume of queued traffic
However, for a STA managing a significant amount of traffic including LL traffic, neither of the two options proves to be optimal
  Option 1 results in underutilization of the secondary channel
  Option 2 leads to channel access delays and the potential failure to obtain a TXOP
December 2023
Sanghyun Kim (WILUS), et al.
3
2
1
0
OBSS1 TXOP
5
4
3
2
Chose not to transmit
OBSS2 TXOP
(Failed to access the medium)
P20
S20
S40
3
2
1
0
Frame exchange (40 MHz)
TXOP
OBSS TXOP
IDLE subchannels
Unused available resources
P20
S20
S40
Option 1
Option 2

## Slide 5: Goal
To mitigate delays in channel access, one potential approach is to first secure a TXOP for the available channels, and then subsequently obtain additional access rights to idle secondary channels
  The TXOP holder can consider expanding the bandwidth of its TXOP after transmitting Low Latency (LL) traffic
December 2023
Sanghyun Kim (WILUS), et al.
3
2
1
0
IDLE
Frame exchange (40 MHz)
TXOP (<= TXOP limit)
OBSS TXOP
BUSY
BUSY
Frame exchange (80 MHz)
P20
S20
S40
Obtaining
TXOP
Expanding
BW

## Slide 6: Design Principles
Ensuring fairness for STAs operating on secondary channels
  Should adopt TBD channel access mechanism for occupying additional secondary channels considering fairness to OBSS
Minimize the cost associated with the BW expansion procedure
  The TXOP holder should ascertain in advance whether it can acquire additional bandwidth before initiating the BW expansion procedure during its TXOP
Need to be simple
  Should avoid introducing additional complexity to the channel access procedure
December 2023
Sanghyun Kim (WILUS), et al.

## Slide 7: Proposal
When a STA intends to expand its TXOP BW, it checks whether secondary subchannel(s) are available
  The STA exchanges short PPDUs to perform short CCA on the secondary subchannels
    The STA may perform CCA before transmitting its PPDU during the TXOP
    The STA may use XIFS duration for CCA
The STA transmits an initial frame, such as a MU-RTS frame, on the IDLE secondary subchannels to expand BW of its TXOP
The STA recognizes the successful expansion of its TXOP bandwidth upon the successful reception of a response frame on the secondary subchannels
  The STA can only utilize the subchannels that the response frame has received
December 2023
Sanghyun Kim (WILUS), et al.
(40MHz)
Tx short PPDU1
Rx resp frame
(40MHz)
Tx short PPDU2
Rx resp frame
S40 CH
BUSY
S40 CH
IDLE
3
2
1
0
AIFS
XIFS
(for CCA)
SIFS
XIFS
(for CCA)
SIFS
3
2
1
0
B
U
S
Y
I
D
L
E
SIFS
Tx
MU-RTS
Tx
MU-RTS
Tx
MU-RTS
Tx
MU-RTS
Rx
CTS
Rx
CTS
Rx
CTS
Rx
CTS
SIFS
Tx
80 MHz PPDU

## Slide 8: Discussions
The expanded BW TXOP is considered as a continuation of the previous TXOP
  Therefore, the TXOP holder performing BW expansion cannot extend its TXNAV timer value
For channel access during BW expansion, following two options can be considered:
    Option 1: Invoke backoff procedure
      Performing a new backoff procedure achieves the same level of protection for the secondary channel as when acquiring a new TXOP
      It's worth noting that initiating a new backoff procedure during TXOP is already allowed in the baseline for TXOP recovery procedures
    Option 2(may have regulation issues): PIFS access (PIFS CCA)
      For the initial TXOP acquisition, access to the secondary channels is determined based on the PIFS CCA results upon completion of the backoff procedure on the primary channel. In other words, the backoff procedure on the primary channel may not have a significant correlation with the protection level of the secondary channel
      For the BW expansion during TXOP, it can be inferred that an equivalent level of protection is applied to the secondary channel by relying solely on PIFS without incorporating the backoff procedure
      To further enhance protection for the secondary channel and minimize the impact to OBSS on the secondary channels, utilizing DIFS (instead of PIFS) can be considered
December 2023
Sanghyun Kim (WILUS), et al.

## Slide 9: Summary
Among the channel access options provided by the baseline, there is no suitable option for a STA with a significant amount of traffic with low-latency traffic
We proposed a mechanism for expanding the bandwidth of the already acquired TXOP, allowing a STA to initiate transmission as early as possible and to utilize available secondary channels later during the TXOP
December 2023
Sanghyun Kim (WILUS), et al.

## Slide 10: Straw Poll
Do you agree to define a mechanism for expanding bandwidth of the obtained TXOP to increase secondary channel utilization in TGbn?
  NOTE: Specific channel access mechanism to be used for the BW expansion is TBD.
December 2023
Sanghyun Kim (WILUS), et al.

## Slide 11: References
[1] 11-23/0034 Non-primary Channel Utilization (Sindhu Verma, Broadcom)
[2] 11-23/0631 secondary channel usage and secondary 20MHz channel backoff (Liwen Chu, NXP)
[3] 11-23/0797 Non-primary channel access (Yongho Seok, MediaTek)
[4] 11-23/0961 UHR secondary channel access (Minyoung Parl, Intel)
[5] 11-23/1365 Discussions on Non-primary Channel Access (Sanghyun Kim, WILUS)
[6] 11-22/2204 Dynamic Subchannel Operation (Sindhu Verma, Broadcom)
[7] 11-23/1496 EMLSR Dynamic Subband Operation (Yongho Seok, MediaTek)
[8] 11-23/1865 Discussion on SST and A-PPDU (Ross Jian Yu, Huawei)
December 2023
Sanghyun Kim (WILUS), et al.