## Slide 1: Coordinated Spatial Reuse Types
Date: 2024-01-09
Authors:

## Slide 2: Abstract
This contribution presents different types of coordinated spatial reuse, based on the direction (i.e., uplink or downlink) of involved PPDU transmissions, as well as the requirements for each coordinated spatial reuse type, in terms of interference measurement and transmit power control

## Slide 3: Backgrounds
The term ‘spatial reuse’ is introduced in the IEEE 802.11ax amendment:
  Spatial reuse (SR): The transmission of a physical layer (PHY) protocol data unit (PPDU) on the medium under certain conditions when a PPDU has been detected that would otherwise have prevented the transmission
‘Coordinated’ SR (Co-SR) is a proposed UHR feature that has been presented and evaluated in different UHR SG and TGbn contributions, where the ‘coordination’ of SR is performed by a sharing AP, i.e., a TXOP owner AP [1]-[14]
The ‘coordination’ of SR by a sharing AP may include a specification of the maximum transmit power for a transmitting STA, which depends on the interference that the transmitting STA introduces to other PPDU transmissions during a specified Co-SR duration
The requirements for transmit power control and interference measurement/report mainly depend on the Co-SR type, in terms of the direction of PPDU transmissions [i.e., uplink (UL) or downlink (DL)] in the sharing AP and shared AP BSSs

## Slide 4: Co-SR Types and Requirements
SIFS
time
Co-trigger
Sharing AP
DL PPDU
SIFS
ACK
SIFS
time
Shared AP
DL PPDU
ACK
SIFS
time
Co-trigger
Sharing AP
UL PPDU
SIFS
ACK
SIFS
time
Shared AP
UL PPDU
ACK
SIFS
Trigger
Trigger
SIFS
time
Co-trigger
Sharing AP
UL PPDU
SIFS
ACK
SIFS
time
Shared AP
DL PPDU
ACK
SIFS
Trigger
SIFS
time
Co-trigger
Sharing AP
DL PPDU
SIFS
ACK
SIFS
time
Shared AP
UL PPDU
ACK
SIFS
Trigger
SIFS
STA1
STA2
AP1
(Sharing AP)
AP2
(Shared AP)
STA1
STA2
AP1
(Sharing AP)
AP2
(Shared AP)
STA1
STA2
AP1
(Sharing AP)
AP2
(Shared AP)
STA1
STA2
AP1
(Sharing AP)
AP2
(Shared AP)
Type 1
Type 2
Type 3
Type 4
 | Interference measurement/report |  | Transmit power control |  | Additional requirements
 | Sharing AP | Shared AP | Shared AP | STAs triggered by the shared AP | 
Type 1 | Shared AP  sharing AP destinations | Sharing AP  shared AP destinations |  |  | -
Type 2 | Shared AP  sharing AP trigger frame destinations STAs triggered by the shared AP  sharing AP | Sharing AP  shared AP trigger frame destinations STAs triggered by the sharing AP  shared AP |  |  | Trigger frame alignment Knowledge by the sharing AP of the STAs that the shared AP will trigger
Type 3 | Shared AP  sharing AP | STAs triggered by the sharing AP  shared AP destinations |  |  | -
Type 4 | STAs triggered by the shared AP  sharing AP destinations | Sharing AP  shared AP |  |  | Knowledge by the sharing AP of the STAs that the shared AP will trigger
 | Interference measurement/report |  | Transmit power control |  | Additional requirements
 | Sharing AP | Shared AP | Shared AP | STAs triggered by the shared AP | 
Type 1 | Shared AP  sharing AP destinations | Sharing AP  shared AP destinations |  |  | -
Type 2 | Shared AP  sharing AP trigger frame destinations STAs triggered by the shared AP  sharing AP | Sharing AP  shared AP trigger frame destinations STAs triggered by the sharing AP  shared AP |  |  | Trigger frame alignment Knowledge by the sharing AP of the STAs that the shared AP will trigger
Type 3 | Shared AP  sharing AP | STAs triggered by the sharing AP  shared AP destinations |  |  | -
Type 4 | STAs triggered by the shared AP  sharing AP destinations | Sharing AP  shared AP |  |  | Knowledge by the sharing AP of the STAs that the shared AP will trigger
Co-SR Types
Requirements
 Required
 Not required
* Required for successful deliveries of trigger frames
^ May be required for successful deliveries of ACK frames
X  Y Interference from X to Y
Desired signal
Interference signal
Can be optionally avoided

## Slide 5: Discussion
Among the discussed Co-SR types, Type 1:
  requires transmit power control only for a shared AP (not for any non-AP STA in the shared AP’s BSS),
  allows the employment of current standard measurement/report schemes (e.g., Beacon request/report) to collect all the interference information required by a sharing AP or shared AP, and
  is the Co-SR type that have been evaluated in most (if not all) of the previous UHR SG and TGbn contributions on Co-SR
We refer to Type 1 Co-SR as ‘downlink Co-SR’, since the SR allows for concurrent downlink transmissions by the sharing AP and shared AP

## Slide 6: UHR SG Co-SR Contributions
[1] 11-22-1822-00-0uhr-recap-on-coordinated-spatial-reuse-operation
[2] 11-23-0616-00-0uhr-overhead-analysis-of-coordinated-spatial-reuse
[3] 11-23-0668-02-0uhr-coordinated-measurement
[4] 11-23-0058-00-0uhr-spatial-reuse-in-coordinated-m-ap-for-uhr
[5] 11-23-0325-00-0uhr-coordinated-spatial-reuse-for-uhr
[6] 11-23-0776-01-0uhr-performance-of-c-bf-and-c-sr
[7] 11-23-1023-02-0uhr-coordinated-spatial-reuse-in-a-4-ap-topoplogy
[8] 11-23-1037-00-0uhr-performance-of-coordinated-spatial-reuse
[9] 11-23-0420-01-0uhr-spatial-reuse-improvements-for-uhr

## Slide 7: TGbn Co-SR Contributions
[10] 11-23-1832-00-00bn-multi-ap-coordinated-spatial-reuse
[11] 11-23-1868-01-00bn-coordinated-spatial-reuse-design
[12] 11-23-1917-00-00bn-coordinated-spatial-reuse
[13] 11-23-1975-00-00bn-coordinated-spatial-re-use-for-uhr
[14] 11-23-2012-00-00bn-location-dependent-performance-of-c-sr