## Slide 1: Seamless Roaming Details
Date: 2023-11
Authors:

## Slide 2: Introduction
In this presentation, we discuss a few detailed call flows to show how seamless roaming works
All assume no data forwarding but with context transfer between APs (unless otherwise stated)
  However, even with data forwarding, the same signaling should also apply
All STA-initiated (can easily be extended to AP-initiated)

## Slide 3: Case 1 (dual links)
The non-AP MLD is capable of communicating with multiple non-colocated APs during roaming
Examples:
  MLMR non-AP MLDs
  eMLSR non-AP MLDs and if both the source AP and target AP are operating on the same channel

## Slide 4: Example Call Flow
RAI: roaming announcement indicator
RAR: roaming announcement response

## Slide 5: Highlights
Assumptions:
  Source AP, target AP, and the Controller communicate via the backhaul
  Context can be transferred from source AP to target AP via the backhaul
  No data forwarding between APs
  AP1 and AP2 could be generalized to AP MLD1 and AP MLD2 in the call flow
  STA and non-AP MLD are synonymous in the call flow
Context transfer
  Information about SN (per-TID)
  Information about PN
Non-AP MLD receives DL from BOTH APs staring at step 8
  i.e., receiving buffered DL packets from AP1 (to avoid data loss) and fresh packets from AP2
Properties:
  Lossless
  Leverage multi-links to deliver DL packets concurrently during roaming
  Minimizes delays in both UL and DL directions

## Slide 6: Case 2 (single link)
The non-AP MLD can only communicate with one AP MLD at a time during roaming
Examples:
  MLSR non-AP MLDs
  eMLSR non-AP MLDs and if the source AP and target AP are operating on different channels

## Slide 7: Example Call Flow 2
RAI: roaming announcement indicator
RAR: roaming announcement response

## Slide 8: Highlights
The non-AP MLD communicates with one AP at a time
  UL resumes at step 9
  DL reception from AP1 until step 9, then DL reception only from AP2
Minimal context transfer
  SN (per-TID) can start at 0 at AP2
  PN at AP2 can start at a value higher than the last PN value used at AP1
Properties:
  Longer UL interruption compared to Case 1
  Longer DL interruption compared to Case 1: serialized DL packet delivery prevents parallel DL packet delivery from two APs (lost opportunities)

## Slide 9: Case 3 (just jump w/o context transfer)
Same as Case 2 except the STA just switches to the target AP immediately after RAI
No context transfer performed

## Slide 10: Example Call Flow 3
RAI: roaming announcement indicator
RAR: roaming announcement response

## Slide 11: Highlights
The non-AP MLD communicates with one AP at a time
  UL resumes at step 7
  DL receives from AP2
Properties:
  DL packet loss: buffered DL packets discarded at the source AP
  However, no context transfer needed

## Slide 12: Conclusion
In this presentation, we presented a few detailed call flows to show how seamless roaming works without data forwarding between APs
As shown in the call flows, the signaling (both over-the-air and between the APs and the Controller) is very similar between the different cases
Case 1 (dual-link) offers best performance, followed by Case 2 (single-link), followed by Case 3 (just switch)
=> We can reuse/extend the 11be ML Reconfig framework and use the same set of management signaling framework to handle all the different cases (i.e., Add link/Link disable and RAI/RAR)