## Slide 1: Some Details about Non-Primary Channel Access
Date: 2023-07-21
Authors:
Name | Affiliations | Address | Phone | Email
Yunbo Li | Huawei | Shenzhen, China |  | liyunbo@Huawei.com
Yuchen Guo |  |  |  | 
Guogang Huang |  |  |  | 
Yue Zhao |  |  |  | 
Maolin Zhang |  |  |  | 
Ming Gan |  |  |  | 
Notes: September 2012

## Slide 2: Introduction
For >20MHz operation, any PPDU must be transmitted on a channel that include the primary 20MHz sub-channel;
When the primary 20MHz sub-channel is busy, secondary sub-channels can not be used for PPDU transmission even they are in idle status, which cause inefficiency for large bandwidth;
The concept of utilize secondary channel was discussed in several UHR presentations;
Opinions of following topics will be shared in this presentation:
  Bandwidth for basic NAV
  CCA on anchor channel
  Backoff counter on anchor channel
  Non-primary channel contention on/off

## Slide 3: Design Principle
No major additional transmit and receive capability for AP and STA;
Minimum or no affect on channel access on primary channel;
Reuse current channel access mechanism as much as possible.

## Slide 4: High Level concepts
A STA do channel access on primary channel;
After the STA set basic NAV based on a received inter-BSS PPDU, it may switch to an anchor channel
  The anchor channel is predefined or announced by AP
  The anchor channel is common for all STAs within a BSS
  The anchor channel is one 20MHz sub-channel in secondary channel
The STA may do channel access and frame exchanges on the anchor channel;
The STA switches back to primary channel before the basic NAV expired.

## Slide 5: Bandwidth for Basic NAV
Currently, a STA doesn’t need to record the BW when setting the Basic NAV;
Before a STA initiates channel access on the anchor channel, it needs to identify which secondary sub-channels are not occupied by the OBSS transmission on primary channel;
If there are multiple anchor channels, the STA also needs to identify which secondary sub-channels are neither occupied by the OBSS transmission on primary channel, nor occupied by the OBSS transmission on the anchor channel with higher priority.
  Assume each anchor channels with different priorities.

## Slide 6: CCA on Anchor Channel
When a STA switches to the anchor channel, it lacks of NAV info on anchor channel;
  It is similar as blindness that happens in NSTR/EMLSR/EMLMR operation;
We can leverage some designs of channel access in blindness for anchor channel operation, which include below main points
  MediumSyncDelay timer = aPPDUMaxTime
  ED threshold (default) = -72dBm
  Max # of RTS
Since the STA will switch back to primary channel before basic NAV expires, a timer (i.e. MediumSyncDelay timer) for channel access on anchor channel is not required;
It would be nice to have a lower ED threshold to respect the OBSS transmission on anchor channel.
The STA is required to initiate transmission using (MU-)RTS to reduce the probability of Data frame collisions, but a maximum number is not needed;

## Slide 7: Backoff Counter
The CW and BO counter of a STA closely related to the channel contention history on primary channel.
To keep the fairness among the STAs on primary channel, a STA’s CW and BO counter on primary channel shall not be affected by the channel access on anchor channel;
A separate backoff is needed for the anchor channel;
The STA only opportunistically operate on anchor channel, how to maintain the CW and BO counter on anchor channel?
  Record the CW and BO counter when the STA operated on anchor channel last time, Or,
  Make is simpler, e.g. always initiate from a random number within [0, CW_min]

## Slide 8: Anchor Channel ON/OFF
AP and associated STAs, in a scenario with little hidden nodes, will coordinate the switch between operating on the primary channel and anchor channel;
In a scenario that AP and associated STAs cannot coordinated the switch between primary channel and anchor channel, a mechanism to suspend the channel access on Anchor channel is required;
The anchor channel ON/OFF is BSS level or per STA based can be discussed
  For BSS level based, AP will broadcast a signaling to enable/disable channel access on anchor channel
  For per STA based, each STA could inform anchor channel ON/OFF individually to AP. It will be much flexible but also more complex for AP to manage.

## Slide 9: Conclusion
Some further discussion on non-primary channel access
  A STA needs to record the BW when set Basic NAV, in order to understand which secondary sub-channels are available now;
  Reuse part of CCA design for blindness
  A separate backoff counter is suggested for anchor channel
  It is good to suspend the channel access on anchor channel under some cases (e.g. hidden nodes scenario)