## Slide 1: Some Details about Non-Primary Channel Access
Date: 2023-07-21
Authors:
Name | Affiliations | Address | Phone | Email
Yunbo Li | Huawei | Shenzhen, China |  | liyunbo@Huawei.com
Yuchen Guo |  |  |  | 
Guogang Huang |  |  |  | 
Yue Zhao |  |  |  | 
Maolin Zhang |  |  |  | 
Ming Gan |  |  |  | 
Notes: September 2012

## Slide 2: Introduction
For >20MHz operation, any PPDU must be transmitted on a channel that include the primary 20MHz sub-channel;
When the primary 20MHz sub-channel is busy, secondary sub-channels can not be used for PPDU transmission even they are in idle status, which cause inefficiency for large bandwidth;
The concept of utilize secondary channel was discussed in several UHR presentations;
Opinions of following topics will be shared in this presentation:
  Bandwidth for basic NAV
  CCA on anchor channel
  Backoff counter on anchor channel
  Time threshold for channel switch
  Non-primary channel contention on/off

## Slide 3: Design Principle
No major additional transmit and receive capability for AP and STA;
Minimum or no affect on channel access on primary channel;
Reuse current channel access mechanism as much as possible.

## Slide 4: High Level concepts
A STA do channel access on primary channel;
After the STA set basic NAV based on a received inter-BSS PPDU, it may switch to an anchor channel
  The anchor channel is predefined or announced by AP
  The anchor channel is common for all STAs within a BSS
  The anchor channel is one 20MHz sub-channel in secondary channel
The STA may do channel access and frame exchanges on the anchor channel;
The STA switches back to primary channel before the basic NAV expired.

## Slide 5: Bandwidth for Basic NAV
Currently, a STA doesn’t need to record the BW when setting the Basic NAV;
Before a STA initiates channel access on the anchor channel, it needs to identify which secondary sub-channels are not occupied by the OBSS transmission on primary channel;
If there are multiple anchor channels, the STA also needs to identify which secondary sub-channels are neither occupied by the OBSS transmission on primary channel, nor occupied by the OBSS transmission on the anchor channel with higher priority.
  Assume each anchor channels with different priorities.

## Slide 6: CCA on Anchor Channel
When a STA switches to the anchor channel, it lacks of NAV info on anchor channel;
  It is similar as blindness that happens in NSTR/EMLSR/EMLMR operation;
We can leverage some designs of channel access in blindness for anchor channel operation, which include below main points
  MediumSyncDelay timer = aPPDUMaxTime
  ED threshold (default) = -72dBm
  Max # of RTS
Since the STA will switch back to primary channel before basic NAV expires, a timer (i.e. MediumSyncDelay timer) for channel access on anchor channel is not required;
It would be nice to have a lower ED threshold to respect the OBSS transmission on anchor channel.
The STA is required to initiate transmission using (MU-)RTS to reduce the probability of Data frame collisions, but a maximum number is not needed;

## Slide 7: Backoff Counter
The CW and BO counter of a STA closely related to the channel contention history on primary channel.
To keep the fairness among the STAs on primary channel, a STA’s CW and BO counter on primary channel shall not be affected by the channel access on anchor channel;
A separate backoff is needed for the anchor channel;
The STA only opportunistically operate on anchor channel, how to maintain the CW and BO counter on anchor channel?
  Record the CW and BO counter when the STA operated on anchor channel last time, Or,
  Make is simpler, e.g. always initiate from a random number within [0, CW_min]

## Slide 8: Time threshold for channel switch
There are some fixed overhead after switch to the anchor channel.
  Channel switch delay
  Time for channel contention
  Initial control frame
If the basic NAV on primary channel is short, it doesn’t make sense for a STA to do channel switch;
No channel switch for a short NAV period will benefit for STA’s power save;
The value of this time threshold can be further discussed.

## Slide 9: Anchor Channel ON/OFF
AP and associated STAs, in a scenario with little hidden nodes, will coordinate the switch between operating on the primary channel and anchor channel;
In a scenario that AP and associated STAs cannot coordinated the switch between primary channel and anchor channel, a mechanism to suspend the channel access on Anchor channel is required;
The anchor channel ON/OFF is BSS level or per STA based can be discussed
  For BSS level based, AP will broadcast a signaling to enable/disable channel access on anchor channel
  For per STA based, each STA could inform anchor channel ON/OFF individually to AP. It will be much flexible but also more complex for AP to manage.

## Slide 10: Conclusion
Some further discussion on non-primary channel access
  A STA needs to record the BW when set Basic NAV, in order to understand which secondary sub-channels are available now;
  Reuse part of CCA design for blindness
  A separate backoff counter is suggested for anchor channel
  A time threshold for channel switch will benefits for power save
  It is good to suspend the channel access on anchor channel under some cases (e.g. hidden nodes scenario)

## Slide 11: SP 1
Do you agree that, when a STA that support non-primary channel access transmits on non-primary channel, its transmitting channel shall follows below requirements?
  The transmitting channel is within the STA’s operating channel;
  The transmitting channel is not overlapping with the transmitting channel of OBSS PPDU on the primary channel

## Slide 12: SP 2
Do you agree that, when a STA that support non-primary channel access intend to transmit on non-primary channel, it shall follows below requirements?
  The CCA ED threshold shall less than -62 dBm;
  The transmission shall initiate with a control frame (e.g. RTS).

## Slide 13: SP 3
Do you agree that, when a STA that support non-primary channel access do channel access on secondary channel, it shall use another set of parameters which is separate from EDCA parameters on primary channel?

## Slide 14: SP 4
Do you agree that, when a STA that support non-primary channel access shall not switch to secondary channel if the Basic NAV on primary channel is less than a time threshold?
  The value of the time threshold is TBD

## Slide 15: SP 5
Do you agree that, when a STA that support non-primary channel access may enable or disable its non-primary channel access operation?
  The conditions of enable or disable non-primary channel assess operation are TBD