## Slide 1: Maximizing channel bandwidth in dense AP deployments
16 January 2024
Authors:
Name | Affiliation | Phone | email
Malcolm Smith | Cisco Systems |  | mmsmith@cisco.com
Brian Hart | Cisco Systems |  | 
Jerome Henry | Cisco Systems |  | 

## Slide 2: 160+MHz channels unlikely to be deployed in Enterprise*
20MHz (13-25ch@5GHz) | 40MHz (6-12ch@5GHz) | 80MHz (3-5ch@5GHz) (14@6GHz) | 160MHz (1-2ch(160) + 1ch(80M) @5GHz) (7@6GHz) | 320 MHz in 6GHz
5GHz Manual | Q2 | 5GHz Manual | Q4 | 
25% | 64% | 11% | 0.02% | N/A
5GHz Auto |  | 5GHz Auto |  | 
23% | 59% | 17% | 0.02% | N/A
6GHz Estimate |  |  |  | 
5% | 10% | 60% | 25% | 0.02%
*Anonymous data from >30k configs and >900k 160MHz capable APs across 6 countries
% of customers at different channel widths

## Slide 3: RRM (non-real-time) not always suitable for wide channels
  Radio Resource Management (RRM) favors WLAN stability
    long-term KPIs (e.g. hours/days) used for general operation
    worst-case co-channel-interference (CCI) often used for cell/channel planning
    conservative frequency re-use targets (e.g. 10+) are typically used
  Expansion via legacy channel-change mechanisms not a great solution
    (E)CSA delay (0.5s) can cause STA to disassoc and impacts real-time
    (E)CSA can’t support 320MHz or higher
    11v BTM is disruptive to connections (especially to real-time traffic)
  Opportunities for maximum bandwidth usage are being squandered

## Slide 4
Real-time Dynamic Bandwidth Selection (RT-DBS)

## Slide 5: MAPC enables real-time BW selection (“RT-DBS”)
MAPC introduces AP-to-AP control signaling:
  BSS channel usage/load can be exchanged in TBTT time-frame
  Per-subchannel OBSS CCI could be readily estimated and opportunities for selective BW expansion identified (e.g., 80MHz operating BW to 320MHz PPDU Bandwidth)
  APs can negotiate and activate immediately (or at a later time) the new channel sizing for a moderate future duration
Triggers and AP control messages can help ensure AP and STAs change BW at the same time:
Low or possibly no disruption in existing services
Subset of eligible/capable STA can be explicitly targeted for BW expansion
et al (Cisco Systems)

## Slide 6: Phase-based RT-DBS implementation
  Expanded BW (E-BW) activated for eligible STAs over long duration (e.g., seconds)
    Starts at te and ends at ts
  Low overhead (measurement exchange amortized over 100s of TXOPs)
  Adaptive to load but not fading channel (esp. with mobility)
t
BW (MHz)
320
80
CCI Estimation
Shared/sharing AP coordination
(not shown)
Shared AP E-BW
Activation/confirmation
ts=TSF+n te=T
n
BSS prepares
for E-BW PPDU
BSS uses E-BW
PPDUs until at most t = te
Shared AP E-BW
De-activation
e.g. te=TSF+m
m
CCI Estimation
Shared/sharing AP coordination
(not shown)
Shared AP
BSS CCI Query
e.g. off-channel scan results
STA=1,2,… N
STA=1,2,5,10

## Slide 7: TXOP-based RT-DBS implementation
TXOP
  On demand expansion (e.g., 1-4ms) can be highly adaptive to load & channel*
  Selected STA(s) can change each TXOP (i.e., QoS control)
  High overhead (in-TXOP activation trigger & more frequent CCI query)
BW (MHz)
320
80
Shared AP queries BSS CCI e.g. triggered off-channel Beacon Report
Shared AP Activation/confirmation E-BW for certain STA within TXOP
CCI Estimation
Shared/sharing AP discovery
(not shown)
STA=1,2,…N
STA=1,3,5,…
SIFS
CCI Estimation
Shared/sharing AP discovery
(not shown)
SIFS
SIFS
SIFS
Data transfer
e.g. DL OFDMA
UL TB PPDU
SIFS
*dependent on timing of latest CCI query (scan) relative to TXOP e.g. to adhere to Tc=150ms

## Slide 8: RT-DBS Summary
  Enterprise and similar environments can’t leverage wide channels routinely but could leverage wider channels under controlled circumstances
  802.11bn MAPC, triggers and AP messages can dynamically and seamlessly expand BW for a subset of the BSS
  The user will experience the best possible speeds when conditions allow

## Slide 9
Backup