## Slide 1: Protected Low Latency Communications for MLO
Date: 2024-01-12
Authors:

## Slide 2: Introduction
“Enabling at least one mode of operation capable of improving the tail of the latency distribution and jitter compared to EHT MAC/PHY operation, with mobility between BSSs” has been one of the main objectives within the scope of P802.11bn [1].
Low latency has already been considered for 11bn from various aspects [2-6].
  E.g., preemption, scheduling, multi-AP operation, PPDU design, frame overhead reduction
Most devices in IEEE 802.11bn are expected to support multi-link operation (MLO), and thus, the operation of multi-link devices (MLDs) should be considered for handling low latency traffic.
In this contribution, we consider the operation of MLDs to support low latency traffic in 11bn, while protecting the data via RTS/CTS exchange.

## Slide 3: LL Data via Single Link
According to the existing behavior, when LL data for a stream becomes available for transmission at an AP with multi-link capabilities (e.g., AP MLD), the AP may try to transmit the LL data over a single link.
If the link is busy for a period of time, the transmission completion time may be reached. The transmission of the LL data may be delayed. The STA may discard the received LL data.
LL data arrives
Transmission completion time
RTS repetitions
Transmission may be delayed

## Slide 4: LL Data via Multiple Links (1)
As one approach, AP may transmit to the STA (non-AP MLD) an RTS frame via one of the links (e.g., Link-1) for transmitting LL data.
If the AP does not receive a CTS frame within a time period (e.g., CTSTimeout), AP may calculate the remaining time for transmission and may transmit to the STA an RTS frame from another link (e.g., Link-2).
On receiving a CTS frame via Link-2, AP may transmit to the STA the LL data.
LL data arrives
Transmission completion time
Calculation of remaining time for transmission

## Slide 5: LL Data via Multiple Links (2)
As another approach, by leveraging multi link capabilities, AP may transmit multiple RTS frames to the STA via multiple links.
If the AP receives a single CTS frame from one of the links, AP may transmit the LL data via the link that it received the CTS frame from.
LL data arrives
Transmission completion time

## Slide 6: LL Data via Multiple Links (3)
When AP transmits multiple RTS frames to the STA via multiple links (e.g., Links 1&2), both links may be available.
If both links are available, STA may transmit CTS frames to the AP via Links 1&2.
Option-1: AP may transmit to STA the LL data in part via both of the links.
In case the LL data is not long, AP may not need to transmit LL data in part (i.e., MSDUs of LL data in separate PPDUs) in multiple links.
LL data arrives
Transmission completion time

## Slide 7: LL Data via Multiple Links (4)
When AP transmits multiple RTS frames to the STA via multiple links (e.g., Links 1&2), both links may be available.
If both links are available, STA may transmit CTS frames to the AP via Links 1&2.
Option-2: AP may transmit to STA the LL data via one of the links (e.g., Link-2), and may also send an indication of single link transmission via the other link.
On receiving indication, STA may transmit a CF-end frame for the unused link.
LL data arrives
Transmission completion time
Unused link can be used by OBSS STA

## Slide 8: LL Data via Multiple Links (5)
Unused link can be used by OBSS STA
As another option (Option-3), AP may transmit RTS frames (or MU-RTS TFs) to the STA for transmitting LL data via either Link-1 or Link-2. RTS frames may indicate a request for transmission of the data via either link.
If both links are available, as a response to RTS frames, STA may transmit only one CTS frame via one of the links (e.g., Link-2).
On receiving CTS frame via Link-2, AP may transmit to STA the LL data via Link-2.
LL data arrives
Transmission completion time

## Slide 9: Conclusion
Operation of MLDs to support low latency traffic has been considered, while protecting the LL data frame via RTS/CTS exchange.
AP MLD may not know the availability of one or more links for transmitting LL data to a non-AP MLD due to an active OBSS STA out of its communication range.
Various options have been considered for the transmission of LL data within the transmission completion time, including the options that are not preventing an OBSS STA from communicating in an unused link.

## Slide 10: References
[1] 23/0480r0, UHR Proposed PAR
[2] 22/1556r1, Multi-AP Coordination for Low Latency Traffic Delivery
[3] 22/1939r0, PPDU Design for Short Frames
[4] 22/1923r1, Enhanced Trigger-Based Uplink Transmission
[5] 23/0045r1, Urgency-based Delivery of Latency Sensitive Traffic
[6] 23/0378r0, Enhanced Scheduling Method for Low Latency Traffic

## Slide 11: Straw Poll
Do you agree to define a procedure for multi-link devices to transmit RTS frames on multiple links to transmit a low latency frame?
  Yes
  No
  Abstain
  Y/N/A: