## Slide 1: C-TDMA Follow-up
Date: 2024-01-13
Authors:

## Slide 2: Introduction
There has been several contributions on C-TDMA including one from us.
The main idea is to allocate time for one shared AP at a time similar to the TXS procedure in 11be.
Here, we focus on the problem of NAV protection rules and fairness:
  How to allocate time to a shared AP without inadvertently setting NAV for that AP’s BSS ?
  How to make the scheme fairer to other STAs esp. legacy ones which cant be allocated resources ?

## Slide 3: NAV protection rules in C-TDMA
Based on the discussions in wifi-7 and some proposals in wifi-8, for C-TDMA there are two somewhat contradictory issues:
  (Issue 1) To allow legacy STAs associated to coordinated APs to be able to a) respond to a Basic TF sent from coordinated APs during the allocated time, b) respond to an RTS sent by the coordinated AP in the same way as it would if the coordinated AP obtained TXOP doing EDCA => need to ensure that NAV set by frame transmissions from Coordinator AP does not prevent this.
  (Issue 2) To increase probability of the coordinator AP not losing its obtained TXOP during the allocated time because a STA hidden to the coordinated AP’s BSS observes medium to be idle and obtains TXOP.
Any solution for issue 2 likely to be more complex and introduce a bit unfairness as the sharing AP will set NAV beyond its immediate BSS and block the medium.
So, prefer to just focus on issue 1 for simplicity.

## Slide 4: NAV protection rules in C-TDMA (contd.)
Proposal: The M-AP TF from sharing AP (AP-0) sets basic NAV for any STA only till the duration of that TF + SIFS+ duration of an immediate response frame + {a small time needed for the shared AP to initiate own transmission}.
After the allocation ends, the sharing AP performs CS check (similar to TXS) to determine if it can continue the TXOP
In congested environments where the sharing AP will likely find medium busy at end of allocation, the sharing AP will
  finish its own transmissions before allocating to another AP,
  guarantee time allocation to one shared AP

## Slide 5: NAV protection rules in C-TDMA (contd.)
Max TXOP length
Sharing AP-0
Shared AP 1
M-AP TF (Duration = TNAV )
Frame exchanges within BSS of AP-1
CTS
New frame
TNAV
TALLOC
CS check:
medium idle
In-BSS transmissions
Max TXOP length
SharingAP-0
Shared AP 1
M-AP TF (Duration = TNAV )
Frame exchanges within BSS of AP-1
CTS
TNAV
TALLOC
CS check:
medium busy => abort TXOP
In-BSS transmissions
EDCA

## Slide 6: Fairness issues for C-TDMA
The concern is a given AP might get additional airtime through C-TDMA in addition to baseline EDCA mechanisms which in turn reduces airtime for legacy STAs.
AP1
AP2
AP3
STA/legacy AP
Time shared to AP1
Time shared to AP1
Even though all STAs are contending simultaneously, the 4th STA has to wait a very long time.
Note: if the green and red blocks are zero above, then its an even worse scenario as the 4th STA effectively loses Tx opportunity from 50% to 25% on average.

## Slide 7: Fairness issues for C-TDMA (contd.)
Since the problem mainly comes from sharing AP giving up time beyond its own need to another STA, a simple solution could be to bound this time allocation.
We therefore propose to limit the aggregate time allocation by a sharing AP in any TXOP to other shared AP(s) to X % of the time used by that AP for transmission within own BSS.
  Prefer X = 100, i.e., each shared AP’s allocation doesn’t exceed the time used by sharing AP for own transmissions in a TXOP.
AP1
AP2
AP3
STA/legacy AP
Time shared to AP1
Time
shared to AP1
4th STA wins contention sooner
Notes: This is not perfect but we expect it to reduce the unintentional fairness impact from C-TDMA.

## Slide 8: Summary
Provided some solutions to resolve any potential unfairness issue to legacy STAs created by C-TDMA.