## Slide 1: MLD Roaming scenarios
Date: 2024-01-12
Authors:

## Slide 2: Abstract
This contribution discusses MLD roaming scenarios with enabling seamless roaming for non-AP MLD STAs
  Make before break
  Eliminate the packet loss
STA assists in the roaming to reduce packet loss and latency

## Slide 3: Scenario 1. “Intra V-MLD” Roaming
Roaming/Virtual MLD:
Non-Link specific management frame endpoint
STA MLD associates with V-MLD MAC address
Reordering buffer is in the MLDs only (no buffer in the V-MLD)
V-MLD does not have access to the DS
Virtual MLD
Purpose:
Extend the EHT architecture to allow APs/MLDs to be not co-located
Optimize data path to DS to reduce latency
Provide lossless roaming
Each MLD may consist of one or more Affiliated APs
MLD2
DS
MLD1
Management path (proprietary)
Data path
STA MLD
ETH switch
Virtual MLD

## Slide 4
Initial phase:
AP MLD1
AP MLD2
2.4GHz
5GHz
5GHz
2.4GHz
STA MLD
Ethernet Switch
Router
DL Data
UL Data
DL Data & UL DATA
DL Ethernet frame
UL Ethernet frame

## Slide 5: Transition step 1
STA sends ML reconfig to MLD1 to set up link(s) with MLD2. This step can be
  STA initiated
  MLD triggered
Add link to MLD2
V-MLD

## Slide 6
Transition Step 2a
AP MLD1
AP MLD2
2.4GHz
5GHz
5GHz
2.4GHz
STA MLD
Ethernet Switch
Router
1. MLD Roaming Indication
STA initiates roaming by sending a Roaming Indication frame to MLD1

## Slide 7
Transition Step 2b
AP MLD1
AP MLD2
2.4GHz
5GHz
5GHz
2.4GHz
STA MLD
Ethernet Switch
Router
UL Data
UL Ethernet frame
2a. Flush UL Data frames received from STA MLD
MLD1 flushes UL data to DS
2b. V-MLD coordination (context sync)

## Slide 8
Transition Step 3
  STA Requests DS Map Update to MLD2 (DS stops sending DL data through MLD1)
    STA sending UL data (if any) through MLD2 does DS Map update automatically
    STA may request MLD2 to buffer its DL data until ready to receive
AP MLD1
AP MLD2
2.4GHz
5GHz
5GHz
2.4GHz
STA MLD
Ethernet Switch
Router
DS Map update Req
DS Mapping update
DL data for STA MLD

## Slide 9
During transition
    Depending on STA capabilities, DL data is retrieved by the STA either sequentially or in parallel from the MLDs
      If sequential, STA requests MLD2 to buffer DL data for STA until STA receives all DL from MLD1
AP MLD1
AP MLD2
2.4GHz
5GHz
5GHz
2.4GHz
STA MLD
Ethernet Switch
Router
DL Data
DL Data
DL Ethernet frame
UL Data
UL Ethernet frame
UL Data
MLD2 to buffer DL Data frames until STA ready to receive DL from MLD2

## Slide 10
Transition Step 4a
STA releases its links with MLD1
Requests the DL data from MLD2

## Slide 11
Transition Step 4b
    STA request for DL Data (if buffering was requested)
AP MLD1
AP MLD2
2.4GHz
5GHz
5GHz
2.4GHz
STA MLD
Ethernet Switch
Router
UL/DL data with MLD2

## Slide 12
Roaming complete
AP MLD1
AP MLD2
2.4GHz
5GHz
5GHz
2.4GHz
STA MLD
Ethernet Switch
Pack
Router
DL Data
UL Data
DL Data & UL DATA
DL Ethernet frame
UL Ethernet frame

## Slide 13: What is proposed to enable this roaming scenario
Define procedures which allows
  MLDs to indicate they belong to a V-MLD
  STA to indicate roaming intent and MLD buffer flush request
  STA to request DS Map Update
  STA to request DL data buffering for the roaming transition period

## Slide 14: Submissions on roaming topic
11-23-1884
11-23-1897
11-23-1907
11-23-1908
11-23-1937
11-23-1971
11-23-1976
11-23-1996
11-23-2157
. . .

## Slide 15: 3 distinct characteristics for the proposals
Require context transfer directly between MLDs
Require context sync through a V-MLD
Reuse and extend the existing FT architecture

## Slide 16: Main differences between proposals 1/2
Context Sync/Transfer on the backend
  Only for control msgs vs control msgs & buffered data forwarding
    Buffered data forwarding only practical when source and target APs can have a direct connection
  Reuse the FT architecture vs sharing the PTK among APs
    STAs use 2 keys and DL from 2 APs during the roaming period
    STAs use only one key at a time and forward buffered data from source MLD to target MLD
  Sync/transfer happens between AP MLDs or between AP MLDs and a V-MLD

## Slide 17: Main differences between proposals 2/2
Frontend:
  Reusing FT architecture requires STA to re-associate
    2 PTKs for a temporary period
      Complicates STA implementations
    1 PTK and data forwarding
      delay and data loss impact
  Sharing the PTK among APs (either directly between APs or through a V-MLD) removes the requirement from the STA to reassociate
Is the aspect of requiring STA to re-associate important/crucial in the 11bn seamless roaming design?
    Crucial part is the 2 keys vs 1 key usage at the STA during the roaming transition period

## Slide 18: Context Sync/Transfer between MLDs
Directly between AP MLDs
  Requires APs to create a mesh among themselves (n(n-1)/2 connections)
Through a V-MLD
  Each AP requires only one connection to the V-MLD
  V-MLD would not require any inter-AP communication definition in the spec

## Slide 19: Way forward
Decide on the roaming architecture
transfer the context (SN, PN, SCS, rTWT, BA …) between the AP MLDs vs. reuse of the FT architecture
transfer PTK between AP MLDs (to enable reuse of the same key) vs. reuse of FT architecture and require STAs to use 2 keys during the roaming transition
  If former, then rekey after roaming
enable data forwarding for MSDU transfer between source and target AP, when practical:
    AP MLDs have direct connection
    ‘raw’ MSDU transfer possible
context sync/transfer done directly or through a V-MLD

## Slide 20: SP
To enable seamless roaming, do you agree to:
transfer the context (SN, PN, SCS, rTWT, BA …) between the AP MLDs instead of reusing the FT architecture
transfer PTK between AP MLDs instead of reusing the FT architecture and require STAs to use 2 keys during the roaming transition
enable data forwarding for MSDU transfer between source and target AP, for deployments when practical
define a framework for V-MLD