## Slide 1: Discussion on Bandwidth Issue in IMMW
Date: 2024-01-XX
Authors:
Name | Affiliations | Address | Phone | Email
Yue Xu | Huawei | Huawei Nanjing R&D Institute, Nanjing, Jiangsu, China, 210012 |  | xuyue57@Huawei.com
Chenhe Ji |  |  |  | 
Chun Pan |  |  |  | 
Xiaofei Bai |  |  |  | 
Yizhan Ni |  |  |  | 

## Slide 2: Introduction
In the last meeting, various aspects of IMMW have been discussed from diverse perspectives. Notably, bandwidth has emerged as a highlight concern, warranting a more in-depth analysis.
This contribution provides a brief summary of the main points made in the last meeting about bandwidth, analyzing potential choices.
Furthermore, we introduce a noteworthy consideration: IMMW SG is able to provide supplementary benefits for WIFI sensing, thereby contributing to the expansion of WIFI practical applications.

## Slide 3: Recap: Proposed Bandwidth
Contributions | Bandwidth
[1] | A limited set of bandwidths (a set of BWs between 160 and 1280MHz)
[2] | Support one or two bandwidth modes (320MHz, 640MHz are proposed)
[3] | Recommend 80/160 MHz as minimum bandwidth
[4] | Opening new bandwidth modes (160MHz, 320MHz, 640MHz are proposed)
[5] | Base bandwidth >= 320MHz Support multiple channel bandwidths (320MHz, 640MHz, 1280MHz, 2560MHz are proposed)
From the above table, it can be found that the current bandwidth is mainly selected as follows: 160MHz, 320MHz, 640MHz, or 1280MHz.Therefore, in the following slide, we compare these different bandwidths from multiple dimensions.

## Slide 4: Comparison of Proposed Bandwidth
Optional Bandwidth | Data Rate | NSS and QAM | Spectral efficiency | Technical Challenges & Costs
160MHz | 3.4Gbps | 2, 64QAM (up to 256QAM) | Same Level | Low & Low
320MHz | 6.8Gbps | 2, 64QAM (up to 256QAM) |  | Medium & Low
640MHz | 13.7Gbps | 2, 64QAM (up to 256QAM) |  | Medium & Medium
1280MHz | 20.4Gbps | 2, 64QAM |  | High & High
The proposed bandwidths are analyzed from multiple aspects:
Data Rate: The theoretical data rate
NSS and QAM: Matched Spatial Flow and QAM Settings
Spectral Efficiency: (#valid data subcarriers) divided by (#total subcarriers).
The absence of an accurate efficiency value is due to the different utilization strategy of non-data subcarriers. As per the HE standard (see the Appendices), we currently assess that the efficiency remains within a similar range.
The rate associated with the bandwidth is influenced by spectral efficiency. Consequently, the actual rate could potentially exceed the value presented in the table.
Technical Challenges and Costs: Provide a logical comparison based on the AD/DA sampling rate, non-ideal factor controller, baseband processing capability, etc. The resource consumption of these factors increases exponentially.
(Length of Data symbol is 0.4us, GI is 0.1us )

## Slide 5: Further Consideration
In [1], Sensing, as one potential feature of IMMW, has been mentioned. And, it should be noted that there are some advantages to the bandwidth that can be provided in IMMW SG, such as 11bf:
WIFI sensing has been widely discussed and has applications in various fields (there are more than 20 uses case in [6]).
One of the reasons that limits sensing performance is the insufficient bandwidth in the 5G and sub-7G bands.
A larger bandwidth can provide higher resolution for sensing to obtain more information.
Currently, there are commercial products that employ WIFI sensing without any standardization. Therefore, making the appropriate selection of bandwidth and expanding the ecosystem of IMMW SG, contributes to the overall development of IMMW SG.
Bandwidth | 80MHz | 160MHz | 320MHz | 640MHz | 1280MHz
Distance Resolution (m) | 1.875 | 0.9375 | 0.4688 | 0.2344 | 0.1172
(This is the theoretical resolution. The actual resolution is determined by the bandwidth of the main lobe. The resolution decreases to different degrees.)
Example:
Object Existence Detection
Object Counting
Motion recognition

## Slide 6: Summary
In this contribution, we present potential options related to bandwidth.
Moreover, IMMW demonstrates the capability to offer substantial bandwidth, addressing some challenges encountered in WIFI sensing. The significance of this aspect need to be further discussed.
In conclusion, the selection of bandwidth for IMMW SG requires more details and thorough deliberation.

## Slide 7: References
[1] 11-23-2004-00-immw-technical-scope-proposal
[2] 11-23-1905-00-immw-high-level-thoughts-on-immw
[3] 11-23-1968-00-immw-discussion-on-general-direction-of-integrated-mmwave
[4] 11-23-1819-00-immw-integrated-mmwave-design-considerations
[5] 11-23-1878-00-immw-high-level-design-considerations-of-immw
[7] 11-20-1712-02-00bf-wifi-sensing-use-cases

## Slide 8: Appendices
Partial context of HE standard
Bandwidth | HE-20M | HE-20M | HE-20M | HE-20M
#total subcarriers | 256 | 512 | 1024 | 2048
#valid subcarriers | 242 | 484 | 996 | 1992
#valid data subcarriers | 234 | 468 | 980 | 1960
#Pilots | 8 | 16 | 16 | 32
#DC | 3 | 5 | 5 | 23
#Null | 11 | 23 | 23 | 5+5+23
Spectral efficiency | 0.9140625 | 0.9140625 | 0.95703125 | 0.95703125