## Slide 1: TGbn Motions List - Part 1
Date: 2024-01-18
Authors:

## Slide 2: IEEE 802.11 TGbn: Enhancements for Ultra High Reliability (UHR) WLAN Task Group
Motions List from January 2024
Chair: Alfred Asterjadhi (Qualcomm Inc.)
Vice Chairs: Laurent Cariou (Intel), Jianhan Liu (Mediatek), Kiseon Ryu (NXP)
Secretary: Yusuke Asai (NTT)
Technical Editor: Ross Jian Yu (Huawei)
PHY Ad-hoc chairs: Dongguk Lim (LGE), Sigurd Schelstraete (MaxLinear), Tianyu Wu (Apple)
MAC Ad-hoc chairs: Srinivas Kandala (Samsung), Jeongki Kim (Ofinno), Xiaofei Wang (Interdigital)

## Slide 3: Motions on January 18th

## Slide 4: Motion 1 (PHY)
Move to add the following text to the TGbn SFD
11bn supports a distributed-tone RU (DRU) for a TB PPDU transmission
  The DRU means an RU which consists of subcarriers spreading across a certain bandwidth
Move: Eunsung Park Second: Jianhan Liu
Discussion: Some discussion.
Preliminary Result: 116Y, 6N, 48A (pass)
Result: 113Y, 6N, 47A (pass)
Note: Discussed in one of the PHY ad-hoc sessions (ref: 11-23/1919r1) during which a similar SP was run. The SP did not receive any objections.

## Slide 5: Motion 2 (MAC)
Move to add the following text to the TGbn SFD
  11bn defines a mechanism that enables a non-AP MLD to roam from one AP MLD to another AP MLD and the non-AP MLD remains in state 4 (see 11.3) during and after roaming to the other AP MLD
Move: Po-Kai Huang Second: Binita Gupta
Discussion: None.
Result: Approved with unanimous consent.
Note: Discussed in one of the MAC ad-hoc sessions (several submissions were discussing similar concept, ref: 23/1884r2, 23/1898r1, 23/1908r2, 23/1937r1, 23/1971r2, 23/1996r0, 23/2157r2) during which a similar SP was run. The SP result was 83Y, 22N, 22A.

## Slide 6: Motions on March 14th

## Slide 7: Motion 3 (PHY)
Move to add the following text to the TGbn SFD
  11bn will define distributed tone RU (“DRU”) transmission
Move: Bin Tian Second: Lin Yang
Discussion: Some.
Preliminary Result: 136Y, 37N, 46A.
Result: 133Y, 36N, 43A (pass).
Note: Discussed in one of the PHY ad-hoc sessions of the January Interim, (ref: 11-23/1988r2) during which a similar SP was run. The SP did not receive any objections.

## Slide 8: Motion 4 (PHY)
Move to include the following into the 11bn SFD
DRU is allowed in a punctured UHR TB transmission.
Move: Ross J. Yu Second: Eunsung Park
Discussion: None.
Result: Approved with unanimous consent.
Note: Discussed in one of the PHY ad-hoc sessions of the March plenary, (ref: 11-23/2200r3) during which a similar SP was run. The SP did not receive any objections.

## Slide 9: Motion 5 (PHY)
Move to add the following text to the TGbn SFD:
11bn supports hierarchical pilot structure for DRU
  Pilot locations of a larger DRU is a subset of pilot locations of smaller component DRUs within the same PPDU BW
Move: Lin Yang Second: Eunsung Park
Discussion: None.
Result: Approved with unanimous consent.
Note: Discussed in one of the PHY ad-hoc sessions of the March plenary, (ref: 11-24/0501r2) during which a similar SP was run. The SP did not receive any objection.

## Slide 10: Motion 6 (PHY)
Move to add the following text to the TGbn SFD
The number of pilot tones for the same size DRU and RRU (regular RU) is the same
  The RRU means the existing RU defined in 11ax and 11be
Move: Eunsung Park Second: Stephen Palm
Discussion: Some.
Preliminary Result: 133Y, 23N, 49A
Result: 129Y, 23N, 47A (pass)
Note: Discussed in one of the PHY ad-hoc sessions of the March plenary, (ref: 11-24/0402r1) during which a similar SP was run. The SP did not receive any objection.

## Slide 11: Motion 7 (PHY)
Move to add the following text to the 11bn SFD:
11bn supports the hybrid mode with DRUs (Distributed tone RU) and RRUs (Regular RU as existing RU defined in 11ax/be) in UHR UL TB OFDMA transmissions
  Minimum PPDU BW for hybrid mode is TBD
Move: Shengquan Hu Second: Ross J. Yu
Discussion: None.
Result: Approved with unanimous consent.
Note: Discussed in one of the PHY ad-hoc sessions of the March plenary, (ref: 11-24/477r2) during which a similar SP was run. The SP did not receive any objection.

## Slide 12: Motion 8 (MAC)
Move to add the following text to the TGbn SFD
11bn defines a mechanism that when a non-AP MLD roams from one AP MLD to another AP MLD, the context related to the non-AP MLD is transferred from the one AP MLD to the other AP MLD such that it preserves the data exchange context for the non-AP MLD.
  Details of the context (e.g., security association context) that can be transferred are TBD
  Framework to transfer the context is TBD.
Move: Po-Kai Huang Second: Gaurav Patwardhan
Discussion: Some.
Preliminary Result: 122Y, 71N, 34A
Result: 121Y, 71N, 34A (fails)
Note: Discussed in one of the MAC ad-hoc sessions (several submissions were discussing similar concept, ref: 23/0322r0, 23/1884r2, 23/1897r0, 23/1908r2, 23/1937r1, 23/1971r2, 23/1996r0, 23/2157r2) during which a similar SP was run. SP result was 100Y, 28N, 18A.

## Slide 13: Motion 9 (MAC)
Move to add to the TGbn SFD:
TGbn defines a power save mode for a STA that is a UHR Mobile AP or a UHR non-AP STA wherein the STA may transition from a lower capability mode to a higher capability mode upon reception of an initial control frame
  Lower capability mode (e.g., 20 MHz BW, one SS, limited data rates, PPDU format)
  Higher capability mode (e.g., operating BW, NSS and MCSs, with at least one higher capability than that in the lower power capability mode)
  Initial Control frame is TBD
  Whether that applies for a non-mobile AP is TBD
Move: Laurent Cariou Second: Ming Gan
Discussion: None.
Result: Approved with unanimous consent.
Note: Discussed in one of the MAC ad-hoc sessions (several submissions were discussing similar concept, ref: 23/10, 23/1875, 23/1936, 23/1965, 23/2003). SP result was: 101Y/11N/23A.

## Slide 14: Motion 10 (MAC)
Move to add to the TGbn SFD:
TGbn defines cross link power save signaling mechanism
  Allowing a non-AP MLD to indicate to its associated AP MLD that supports the mechanism, in a frame sent on one enabled link, the power management mode for one or more of its affiliated non-AP STAs
  Whether support for the mechanism is mandatory or optional is TBD
Move: Laurent Cariou Second: Rakesh Taori
Discussion: None.
Result: Approved with unanimous consent.
Note: Discussed in one of the MAC ad-hoc sessions (several submissions were discussing similar concept, ref:11-23/2003, 11-24/0602). SP result was: 122Y/23N/32A

## Slide 15: Motions on May 16th

## Slide 16: Motion 11 (MAC)
Move to add the following text to the TGbn SFD:
TGbn defines a mode of operation that enables a STA to access the secondary channel while the primary channel is known to be busy due to OBSS traffic or other TBD conditions.
  The mode of operation shall not assume that the STA is capable to detect or decode a frame and obtain NAV information of the secondary channel concurrently with the primary channel.
  A BSS shall only have a single NPCA primary channel (name TBD) on which the STA contends while the primary channel of the BSS is known to be busy due to OBSS traffic or other TBD conditions.
Move: Minyoung Park Second: Yunbo Li
Discussion: Some discussion. Recorded vote requested.
Preliminary Result: 209 (+1)Y, 7N, 31A.
Result: 199(+1)Y, 7N, 28A (pass).
Note: Discussed in several sessions and several submissions discuss similar concept, ref: [23/1911r0, 23/1913r2, 23/1935r1, 23/2005r1, 23/2023r1, 24/0070r1, 24/458r0, 24/486r0, 24/538r0, 24/670]. No objection to the SP.

## Slide 17: Motion 12 (MAC)
Move to add the following text to the TGbn SFD:
Define a way in 11bn to include in an initial control frame an intermediate FCS for UHR STA(s) that precedes padding and the FCS field
Move: Laurent Cariou Second: Ming Gan
Discussion: None.
Result: Approved with unanimous consent.
Note: Reference documents are [11-23/1873, 11-23/2003] No objection to the SP.

## Slide 18: Motion 13 (MAC)
Move to add the following text to the TGbn SFD:
TGbn enables per-TID buffer size reporting of a larger queue in UHR
  Note: It is an optional feature.
  Note: In the baseline, the maximum approximate per-TID queue size to report is 2,147,328 octets
Move: Frank Hsu Second: Bruce Kang
Discussion: Some clarificatory discussion.
Result: Approved with unanimous consent.
Note: Reference document is 11-23/2007r2. No objection to the SP.

## Slide 19: Motion 14 (PHY)
Move to add the following text to the TGbn SFD:
DRUs tone plan design on distribution BW 20MHz and 40MHz is 26-tone RU based DRU method (using 26-tone DRUs as basic building blocks).
  DRUs tone plan design on other distribution BWs is TBD.
Move: Shengquan Hu Second: Jianhan Liu
Discussion: None.
Result: Approved with unanimous consent.
Note: Reference document is 11-24/468r2. No objection to the SP.

## Slide 20: Motion 15 (PHY)
Move to add the following text to the TGbn SFD:
Global CSD is used for DRU UHR-STF transmission to solve unintentional beamforming issue
Global CSD is applied in each distribution BW
Move: Lin Yang Second: Sameer Vermani
Discussion: Some clarificatory questions.
Result: Approved with unanimous consent.
Note: Reference document is 11-24/752r2. No objection to the SP.

## Slide 21: Motion 16 (PHY)
Move to add the following text to the TGbn SFD:
DRU transmission reuses the 8 CSD table/values in 11ax/be for global CSD allocation
Move: Lin Yang Second: Bo Gong
Discussion: None.
Result: Approved with unanimous consent.
Note: Reference document is 11-24/752r2. No objection to the SP.

## Slide 22: Motion 17 (PHY)
Move to add the following text to the TGbn SFD:
11bn defines frequency domain aggregation of PPDUs. A frequency domain aggregated PPDU consists of multiple PPDUs.
  The PPDU format combinations are TBD.
  The number of PPDUs is TBD.
Move: Ross J. Yu Second: Yan Xin
Discussion: Some discussion. Recorded vote requested.
Preliminary Result: 120Y, 75N, 57A.
Result: 115Y, 72N, 55A (fails).
Note: Reference document is 11-24/224r2. SP result: 68Y/20N/8A.

## Slide 23: Motion 18 (PHY)
Move to add the following text to the TGbn SFD:
The UHR-STF for DRU in a TB PPDU uses 11ax/11be trigger based STF sequences.
Move: Bo Gong Second: Lin Yang
Discussion: None.
Result: Approved with unanimous consent.
Note: Reference document is 11-24/749r2. No objection to the SP.

## Slide 24: Motion 19 (PHY)
Move to add the following text to the TGbn SFD:
For UHR-STF corresponding to distribution bandwidth for DRU,
  STF sequence depends on PPDU BW.
  Occupied STF tones are the same as that of the largest RRU corresponding to the distribution BW within PPDU BW.
Move: Bo Gong Second: Lin Yang
Discussion: None.
Result: Approved with unanimous consent.
Note: Reference document is 11-24/749r2. No objection to the SP.

## Slide 25: Motion 20 (PHY)
Move to add the following text to the TGbn SFD:
In a non-punctured 80 MHz PPDU, the following distribution bandwidth modes are allowed for DRU
  80 MHz
  20 MHz + 20 MHz + 40 MHz (or 40 MHz + 20 MHz + 20 MHz)
Move: Eunsung Park Second: Dongguk Lim
Discussion: None.
Result: Approved with unanimous consent.
Note: Reference document is 11-24/766r2. No objection to the SP.

## Slide 26: Motions on July 18th

## Slide 27: Motion 21 (PHY)
Move to add the following text to the TGbn SFD:
If a DRU for a PPDU occupies more than one 20 MHz channel, then the L-STF, L-LTF, L-SIG, and RL-SIG fields are duplicated over all the 20 MHz channels which are occupied by the DRU.
Move: Second:
Discussion:
Result:
Reference documents: [24/0736r1]. SP result: 51Y, 2N, 15A.

## Slide 28: Motion 22 (PHY)
Move to add the following text to the TGbn SFD :
“PHY version identifier” is set to 1 in U-SIG for UHR PPDUs?
Move: Second:
Discussion:
Result:
Reference documents: [24/0876r0]. SP result: 112Y, 4N, 17A.

## Slide 29: Motion 23 (PHY)
Move to add the following text to the TGbn SFD:
Define unequal modulation over different spatial streams
Move: Second:
Discussion:
Result:
Reference documents: [24/0474r2]. SP result: 116Y, 4N, 9A.

## Slide 30: Motion 24 (PHY)
Move to include the following in the 11bn SFD:
Define Enhanced Long Range (ELR) PPDU and potentially other Range Extension mechanisms.
Move: Second:
Discussion:
Result:
Reference documents: [24/0873r2]. SP result: 118Y, 7N, 16A.

## Slide 31: Motion 25 (PHY)
Move to include the following in the 11bn SFD:
Define LDPC codeword length larger than 1944, including 2x1944
Move: Second:
Discussion:
Result:
Reference documents: [24/1985r5]. SP result: 113Y, 3N, 20A.

## Slide 32: Motion 26 (MAC)
Move to add the following text to the TGbn SFD:
Define in 11bn that when a non-AP MLD is in the process of roaming from the current AP MLD to a target AP MLD, the context related to the non-AP MLD is transferred to the target AP MLD such that it preserves the data exchange context for the non-AP MLD or the context can be renegotiated with the target AP MLD?
  Details on what context can be transferred and what context can be renegotiated are TBD
  How to transfer the context is TBD.
Move: Second:
Discussion:
Result:
Note: Reference documents:[23/1971, 23/1996, 24/0052, 24/0083, 24/0101, 24/0396, 24/0412, 24/0679]. SP result: 153Y, 22N, 37A.

## Slide 33: Motion 27 (MAC)
Move to add the following text to the TGbn SFD:
As part of the seamless roaming procedure, during roaming,
  after the request/response exchange that initiates notification of the DS mapping change from the current AP MLD to the target AP MLD,
    The current AP MLD may deliver buffered DL data frames for a TBD period of time.
    The non-AP MLD may retrieve buffered DL data frames from the current AP MLD
    The non-AP MLD may send UL data to target AP MLD.
    It is assumed that the target AP MLD is able to deliver data frames to non-AP MLD after the DS mapping change
  The current AP MLD may forward DL data to the target AP MLD.
    When and how to initiate the forwarding of DL data is TBD
Move: Second:
Discussion:
Result:
Reference documents:[23/1971, 23/1996, 24/0052, 24/0083, 24/0101, 24/0396, 24/0412, 24/0679]]. SP result: Y:136, N:11, and A:32.

## Slide 34: Motion 28 (MAC)
Move to add the following text to the TGbn SFD:
Define in 11bn that a non-AP MLD can gather information on candidate AP MLD(s) over the DS via the current AP MLD
Move: Second:
Discussion:
Result:
Reference documents:[24/0349r3, 24/0679r1]. SP result: 125Y, 34N, 38A.

## Slide 35: Motion 29 (MAC)
Move to add the following text to the TGbn SFD:
• Define a multi-AP Coordinated Spatial Reuse at TxOP-level with power control
• Define multi-AP Coordinated Beamforming
• Other multi-AP coordination modes are TBD
Move: Second:
Discussion:
Result:
Reference documents:[22/1822r0, 23/0325r0, 23/0776r1, 23/1023r2, 23/1037r0, 23/1832r0, 23/1917r0, 24/0529r0, 24/0577r0, 24/0635r0, 24/0639r0, 24/0839r1, 24/0880r0, 24/1204r0, 24/1211r1]. SP result: 173Y, 27N, 28A.

## Slide 36: Motion 30 (MAC)
Move to include in the 11bn SFD:
  define a mechanism for a non-AP STA to report unavailability at TxOP level and define or reuse/update existing mechanism for a non-AP STA to report long term (periodic) unavailability?
Move: Second:
Discussion:
Result:
Reference documents:[23/0816, 24/0831, 23/1934, 23/2002, 23/2078, 24/0420,
24/0856]. SP result: 164Y, 24N, 33A.