## Slide 1: Coordinated Transmission ID
Date: 2024-02-01
Authors:
Name | Affiliations | Address | Phone | email
Yanchun Li | Huawei | Huawei Industrial Base, Bantian, Longgang District, Shenzhen 518129 P.R. China. | (+86)13127744874 | liyanchun@huawei.com
Ming Gan |  |  |  | 

## Slide 2: Introduction
BSS color has been introduced to IEEE 802.11 in 11ax.
BSS color allows the PHY to infer the relevant BSS/source/destination of the PPDU
  If a home AP is not involved in any current transmission, the home AP or STA is able to reuse the channel.
  BSS color collision detection allows each of the nearby APs to have an unique BSS color locally.
However, coordinated transmission such as JT, Coordinated BF, Coordinated OFDMA, etc, involves aligned transmission from multiple APs. It causes a problem over the air. This contribution discussed the problem.

## Slide 3: Recap BSS color in 802.11ax
Usage of BSS color
  allows power saving at mobile STAs.
    Ignore irrelevant PPDU over air (if BSS color does not match).
  allows the efficient spatial reuse of spectrum (Fig. 1).
AP1:
AP2:
STA1
STA2
AP1:
AP2:
Preamble (BSS color =A)
Payload
Payload
(BSS color =B)
Fig. 1 AP2’s BSS reuses spectrum after identifying transmission with BSS Color =A
(BSS color =A)

## Slide 4: Recap multi-AP transmissions
Considering that AP1 and AP2 serve STA1 and STA2, they transmit their preambles simultaneously on overlapping 20MHz channel(s).
STA2
AP1:
AP2:
STA1
Case 1: Joint transmission
Case 2: Coordinated BF
STA2
AP1:
AP2:
STA1
e.g.
With nulling to suppress inter-BSS interference

## Slide 5: When BSS coloring meets multi-AP transmissions
STA2
BSS coloring in multi-AP transmission which allows spatial reuse can be beneficial for throughput, e.g.
AP1:
AP2:
Preamble from AP1 and AP2
Payload
AP3:
STA1
STA3
(2) STA2 hears Preamble from AP1 and AP2. It understands AP3 is idle and initiate EDCA uplink transmission to AP3.
(1) AP1 and AP2 have coordinated BF/joint transmission etc. to STA1/2 with PPDU:
multi-AP
transmission
spatial reuse

## Slide 6: The issue when BSS coloring meets multi-AP transmissions
For coordinated transmissions with multi-AP concurrent Tx:
  Case A: Each AP uses different BSS color leads to preamble collision.
AP1:
AP2:
(adjacent to AP1)
Payload
Payload
STA2
AP1:
AP2:
STA1
U-SIG
Preamble
NAV,
BSS color =B, etc.
NAV,
BSS color =A, etc.
Preamble
L-LTF
L-LTF
① L-LTFs are aligned, the estimated channel will be h1+h2, due to pilot contamination effect.
② However, the channel which AP1’s U-SIG signal pass through is not h1+h2 but h1, with superposed interference from AP2 (coded waveform with BSS color=B). The mismatch will dramatically increase PER for U-SIG.
These preambles have different waveform in U-SIG (due to BSS color difference).
Assume AP1 uses BSS color A
AP2 uses BSS color B

## Slide 7: The issue when BSS coloring meets coordinated multi-AP transmissions (conti.)
  Case B: AP can also use BSS color =0, besides each AP’s unique BSS color. However, it will disallow spatial reuse.
It is important to allow successful transmission of BSS color and also indicate relevant BSS information clearly.
Preamble (NAV,
BSS color =0)
Payload
CCA busy

## Slide 8: Comparison of various coloring schemes
 |  | Case A | Case B | Case C | Case D
Uncoordinated Transmission | Schemes | AP1: BSS color1 AP2: BSS color2 | AP1: BSS color1 AP2: BSS color2 | AP1: BSS color1+ partial bits(=1) in aid AP2: BSS color1+ partial bits(=2) in aid | AP1: BSS color1 AP2: BSS color2
 | Results | √ | √ | √ for 11bn STA √ for OBSS legacy STA Limit SR for legacy STA within AP1+2 | √
Coordinated Transmission | Schemes | AP1: BSS color1 AP2: BSS color2 | AP1+AP2: BSS color0 | AP1+AP2: BSS color1+partial bits(=3) in aid | AP1+AP2: BSS color3
 | Results | X | X, disabled SR | √ | X: legacy STA causes intra-BSS collision

## Slide 9: Summary
We discussed the issue of BSS coloring for coordinated transmissions.
A coloring scheme without ambiguity can allow coordinated multi-AP transmission while also allow spatial reuses.

## Slide 10: Straw Poll
Do you agree that in 11bn should support to use UHR preamble for indicating of the APs involving multi-AP transmissions?
  Y
  N
  A

## Slide 11: References
[1] https://mentor.ieee.org/802.11/dcn/22/11-22-1394-01-0uhr-virtual-bss-and-multi-ap-transmissions.pptx