## Slide 1: A Uniform Procedure for Preemption
Date: 2024-02-08
Authors:
Name | Affiliations | Address | Phone | Email
Yunbo Li | Huawei | Shenzhen, China |  | liyunbo@Huawei.com
Yuchen Guo |  |  |  | 
Guogang Huang |  |  |  | 
Yue Zhao |  |  |  | 
Maolin Zhang |  |  |  | 
Ming Gan |  |  |  | 
Notes: September 2012

## Slide 2: Introduction
Many presentations in UHR SG and 11bn are discussing the procedure of preemption;
A TXOP holder preempts its own TXOP to send low latency (LL) traffic can be easily handled by the TXOP holder itself;
There are different cases for a STA to preempt another STA’s TXOP to transmit LL traffic
  Case 1: Preempt a DL TXOP to send UL LL traffic
  Case 2: Preempt a UL TXOP to send DL LL traffic
  Case 3: Preempt a UL TXOP to send UL LL traffic
Different procedures are discussed based on different cases;
A uniform procedure is proposed for all cases to simplify the design and implementation.

## Slide 3: A Uniform Procedure
PR: preemption request frame
TF: Trigger frame
TFR: Trigger frame with UORA
UORA: uplink OFDMA random access
LL: low latency
Preempting STA: a STA (not the TXOP holder) that buffers LL traffic
This step is not needed if AP is the TXOP holder
In this presentation, assuming all the preempting STAs are associated STAs. Whether and how to support OBSS STA to do preemption is open for further discussion.

## Slide 4: Case 1: Preempt DL TXOP to send UL LL
The AP may transmit PPDU2 before transmit a BSRP if the LL traffic is carried in PPDU2;
AP must be able to solicit LL BSR from preempting STAs, a simple way is to mandate UORA support for preempting STAs;
When the AP sends BSRP frame with UORA, it is better only allow BSR of LL traffic be reported by non-AP STAs;
  E.g. a new type of random access RU that only for LL traffic
The BSRP with UORA frame is optional to transmit, AP may choose other ways to know which non-AP STAs are buffering LL traffic, e.g.
  Use a NFRP Trigger frame
  Do the prediction based on historical statistics
Note: The contents of PR frames from STA2 and STA3 are exactly the same, so STA1 and AP can correctly decode them. It is similar as simultaneous CTSs follow MU-RTS sent by multiple STAs

## Slide 5: Case 2: Preempt UL TXOP to send DL LL
Case 2a: DL LL to TXOP holder
Case 2b: DL LL to other non-AP STA
Case 2a and Case 2b can happen in one preemption;
The PR frame is needed when considering a uniform procedure for different cases;
The TXOP holder will stop transmitting following PPDU after receiving a PR frame;
The contents of PR frame from the AP and the non-AP STAs are same;
A signaling in PPDU3 informs STA1 continues to transmit PPDU in the remaining TXOP
  The detail of the signaling is TBD, e.g. carried in A-Control field.

## Slide 6: Case 3: Preempt UL TXOP to send UL LL
After receiving a PR frame follows PPDU1 which is preemption enabled, the AP is allowed to ignore the intra-BSS NAV and send BSRP with UORA to solicit BSR from preempting STAs;
The benefits to allow AP to control the preemption procedure:
  Avoid contention collision from multiple STAs
  Can serve multiple STAs in one preemption
After the LL traffic transmission are finished, The AP signaling the TXOP holder continues to transmit PPDUs in the remaining TXOP.

## Slide 7: Case 2 + Case 3
Case 2 and Case 3 can happen in one preemption;
The AP that transmits PR doesn’t know whether there is one or more non-AP STAs sent PR frames. The AP may transmits BSRP with UORA to test whether there is BSR from any preempting STAs;
The AP can choose first to transmit DL LL traffic or first to solicit UL LL traffic.
First to transmit DL LL traffic
First to solicit UL LL traffic

## Slide 8: Summary
A uniform preemption procedure is proposed to cover all possible cases
  Case 1: preempt DL traffic to send UL LL traffic
  Case 2: preempt UL traffic to send DL LL traffic
  Case 3: preempt UL traffic to send UL LL traffic
The uniform procedure will facilitate the procedure design and implementation.

## Slide 9: Straw Poll 1
Do you agree a TXOP holder may indicate in a PPDU that a STA in the same BSS of the TXOP holder is allowed to send a preemption request frame SIFS after the PPDU?
  A preemption request frame informs buffering of low latency traffic frame
  The detail of indication signaling is TBD
  The detailed design of preemption request frame is TBD
  Yes:
  No:
  Abstain:

## Slide 10: Straw Poll 2
Do you agree a TXOP holder will continue PPDU transmission PIFS after a preemption enabled PPDU if no preemption request frame is received SIFS after the preemption enabled PPDU?
  Yes:
  No:
  Abstain:

## Slide 11: Straw Poll 3
Do you agree a TXOP holder that is a non-AP STA will grant the TXOP to its associated AP if a preemption request frame is received after a preemption enabled PPDU?
  A preemption enabled PPDU is a PPDU that allows preemption request frame be transmitted SIFS after the PPDU
  Yes:
  No:
  Abstain:

## Slide 12: Straw Poll 4
Do you agree an AP that is granted a TXOP by a non-AP STA TXOP holder to do preemption operation will return the TXOP to the TXOP holder after the preemption operation?
  The details of returning the TXOP is TBD
  Yes:
  No:
  Abstain: