## Slide 1: Legacy STA and OBSS Issues for Preemption
Date: 2024-02-18
Authors:
Name | Affiliations | Address | Phone | Email
Yunbo Li | Huawei | Shenzhen, China |  | liyunbo@Huawei.com
Yuchen Guo |  |  |  | 
Guogang Huang |  |  |  | 
Yue Zhao |  |  |  | 
Maolin Zhang |  |  |  | 
Ming Gan |  |  |  | 
Notes: September 2012

## Slide 2: Introduction
Many presentations in UHR SG and 11bn are discussing the procedure of preemption;
Most of the presentations are discussing how to do preemption for UHR STAs within single BSS;
Some issues about legacy STAs and OBSS need to be considered for preemption
  Issue 1: how to alleviate the affect to preemption when a legacy STA within own BSS obtains a TXOP
  Issue 2: how to alleviate the affect to preemption when a STA from preemption supported OBSS obtains a TXOP
  Issue 3: how to alleviate the affect to preemption when a STA from preemption not supported OBSS obtains a TXOP
I don’t have any idea how to solve issue 3. This presentation only focus on issue 1 and 2.

## Slide 3: Legacy STA Issue
A legacy STA can not understand preemption procedure, it will reserve a long TXOP. The long TXOP will affect the delay of low latency traffic from other STAs;
Reducing the TXOP limit can avoid legacy STA to reserve a long TXOP, but it will case new problem;
A short TXOP limit will reduce the efficiency of UHR STAs which support preemption;
We need a good balance between latency and efficiency;
Proposed solution:
  TXOP limit in EDCA parameter element (set to a smaller value) is used by legacy STAs as well as UHR STAs that don’t support preemption;
  A new TXOP limit (set to a larger value) is used for UHR STAs that support preemption;
  The UHR STAs use a larger TXOP limit will limit the PPDU length to allow preemption.

## Slide 4: OBSS Issue
An OBSS UHR STA may reserve a long TXOP. The long TXOP will affect the delay of low latency traffic from STAs of own BSS;
Potential solution 1:
  APs of multiple overlapping BSSs set TXOP limit for UHR STAs (as well as legacy STAs) to a small value；
  Cons: low efficiency for both OBSS and own BSS due to short TXOP
Potential solution 2:
  APs maintain short TXOP limit for legacy STAs, and long TXOP for UHR STAs;
  UHR STA will limit the PPDU length to allow preemption;
  STAs of own BSS can preempt a TXOP obtained by an OBSS STA.
Solution 2 is a better balance between latency and efficiency.

## Slide 5: Summary
Issues of legacy STA and OBSS are discussed in the presentation;
Propose to use short TXOP limit for legacy STAs to alleviate the affect of legacy STAs to preemption;
Propose to allow a STA from own BSS to preempt a TXOP obtained by an OBSS STA to improve the preemption performance.

## Slide 6: Straw Poll 1
Do you agree that TGbn will introduce a new TXOP limit for associated STAs support preemption?
  Yes:
  No:
  Abstain:

## Slide 7: Straw Poll 2
Do you agree to allow a STA from own BSS to preempt a TXOP obtained by a STA from OBSS?
  Yes:
  No:
  Abstain: