## Slide 1: Enhancements on Base-Channel Peer-to-peer (P2P) Communications
Date: 04-29-2024
Authors:

## Slide 2: Abstract
In this contribution, we follow up on the prior work on enhancing Peer-to-Peer communication on the base channel.

## Slide 3: Recap(1)
P2P communications, for most consumer devices, can be categorized based on types of operating channels—
  Base-channel P2P: When the P2P clients operate on the channel where the infrastructure AP operates.
  Off-channel P2P: When the P2P clients operate on the channels different from the AP’s channel.
At present, AP is essentially hands-off for any P2P communication in the network.
  In a congested network, this may inhibit the timely delivery of P2P traffic
For base-channel P2P operation, the AP should be involved in QoS provisioning for P2P communications for non-AP STAs.

## Slide 4: Recap(2)
To better facilitate the base-channel P2P operation, 802.11be introduced the TXOP sharing mode-2 procedure where an AP can allocate a portion of its TXOP to a STA for the STA’s P2P transmission.
When a TXOP is allocated to a STA for P2P, only that STA can utilize the TXOP for transmitting to its peer.
  If the TXOP-recipient STA intends to receive frames from its peer device during the TXOP allocated by the AP, then the TXOP recipient STA can transition to a role of mobile AP in order to solicit the transmission from the peer STA, which again is in a per-peer-STA basis.
Figure: AP’s TXOP usage in a P2P group using 802.11be

## Slide 5: Recap(3)
P2P devices typically operates in a group or cluster-basis
For various evolving applications such as interactive XR experiences, members of a P2P group/cluster may have the same or very similar traffic pattern (and the traffic can also be latency-sensitive).
To better support the P2P communication within the overall P2P group/cluster, the AP should be able to allocate its resources in a per-group/cluster basis.

## Slide 6: Topology of interest

## Slide 7: Resource Request
A STA that is a member of the P2P group can coordinate within the P2P group to collect the resource need (with QoS Characteristics information) for each of the STAs in the P2P group.
  For illustration purposes, the STA that collects these resource needs can be referred to as the P2P leader.
The P2P leader can inform the AP about the P2P group’s QoS requirement.
Based on the QoS request, the AP can allocate TXOP for the P2P group.

## Slide 8: Resource delivery
For resource delivery, the same MU-RTS frame can be used with the receiver address set as the P2P group address.

## Slide 9: NAV Setting

## Slide 10: References
[1] Rubayet Shafin and et al., “P2P Resource Management”, 23/1929r0, November 2023.

## Slide 11: SP
Do you support defining a mechanism in 802.11bn that would allow an AP to share a TXOP with a group of peer-to-peer (P2P) non-AP STAs?