## Slide 1: Enhancements for Off-Channel Peer-to-peer (P2P) Communications
Date: 04-29-2024
Authors:

## Slide 2: Abstract
In this contribution, we follow up on the prior work on enhancing Peer-to-Peer communication over the off-channels.

## Slide 3: Background--Advertisement of Recommended P2P Channels
Based on the recent addition to 11be, an AP can announce a set of channels in its BSS that are recommended for P2P communications
  These advertised channels would be more conducive to P2P communication.
    For example, the AP can minimize the use of those channels for its infrastructure communication.
  The AP can announce/advertise the Recommended P2P Channels in its BSS by including the related information in the Beacons and Probe Response frames it transmits.
    The AP can include Channel Usage elements for this advertisement
  The P2P channel recommendation can be updated over time.
Motivation for the AP: By incentivizing the P2P STAs to keep their P2P transmissions within the recommended set of channels, the AP can essentially reduce the uncontrolled P2P transmission on the channels that the AP uses for infrastructure BSS operation (for UL/DL communication, for example)
    This, in essence, can help the AP in ensuring infrastructure STAs’ QoS requirements.
Motivation for the P2P STAs: The guidance from the AP would enable the P2P STAs to embark on a cleaner channel (with less interference from the infrastructure) faster for their P2P communications by using the recommended channels
  Help faster setup of a P2P link (or P2P group) or faster switch of a P2P operating channel

## Slide 4: Need for Extended Support (1/2)
  A typical network topology coexisting with P2P STAs/P2P groups

## Slide 5: Need for extended support (2/2)
  The P2P STAs can follow the P2P channel resource recommendation from the AP for their P2P needs.
  This helps in parking on a channel for P2P that would have less interference from the BSS maintained by that AP.
  However, in an OBSS environment, the P2P link is still likely to face interference from the OBSS network
    P2P channel recommendation from the first AP may be independent of the recommendation from the OBSS AP.

## Slide 6: Multi-AP Coordination for Off-Channel P2P
  In OBSS environment, P2P group operation can be quite challenging
    When trying to go off-channel, it can be very hard to find a common off-channel that is clean from both infrastructure networks.
  For efficient P2P communication, it would be very beneficial if the APs corresponding to the overlapping BSS coordinate with each other. Upon coordination--
    For instance, the APs can designate a common set of channels for P2P
    Help facilitate off-channel P2P operation
  The APs can create a common schedule for P2P
    Help facilitate base-channel P2P operation

## Slide 7: Summary
Efficiently finding a suitable off-channel is important for P2P STAs
In order to ensure that the P2P off-channels also have minimum OBSS interference, the APs in the overlapping BSSs need a mechanism to coordinate with each other and jointly come up with a set of channels for off-channel P2P operation.
  Such channels are deemed to be more conducive to P2P operation.

## Slide 8: References
[1] Rubayet Shafin et al., “Follow-up on peer-to-peer (P2P) communication for UHR”, 23/1424r0, Sept 2023.
[2] Rubayet Shafin et al., “Channel Usage Enhancements for P2P in UHR”, 23/294, May 2023

## Slide 9: SP1
Do you want to define a mechanism in 802.11bn that would allow multiple APs to coordinate with each other in order to find a set of channels that would be conducive to peer-to-peer communication?