## Slide 1: Coordinated Roaming through Target AP MLD
Date: 2024-02-26
Authors:

## Slide 2: Introduction
UHR is aiming to provide improved support for roaming. Several roaming proposals have highlighted seamless roaming operation through the current serving AP MLD [1-4].
In [1] we presented a proposal for seamless roaming within a mobility domain through the current serving AP MLD.
In this presentation, we extend that proposal to achieve coordinated roaming through the target AP MLD, for the cases when roaming through the serving AP MLD may not be possible.

## Slide 3: Problem Statement
In Wi-Fi networks, there can be sudden RSSI drops (e.g. due to concrete walls, elevator metal shaft etc.), leading to connectivity disruption.
Also, a STA can be in sleep mode and not scanning, and when it comes out of the power save mode then its RSSI with serving AP has dropped significantly.
In such cases, STA can’t perform seamless roaming through its (old) serving AP MLD. STA needs to quickly roam to a target AP MLD to maintain connectivity.
For such scenarios, 11bn must define improved roaming through coordination between the target AP MLD and the serving AP MLD.
Here we propose a mechanism for coordinated roaming through the target AP MLD.

## Slide 4: Solution Considerations
Solution for coordinated roaming through a Target AP MLD should meet following considerations:
Provide data continuity and preserve context
  Similar to seamless roaming through serving AP MLD, solution should preserve data exchange context to provide data continuity and preserve other control plane context/agreements to minimize reestablishment of those context.
Feasibility across deployments
  Solution should not mandate requirements (e.g. data transfer) which may not be supported/feasible in all types of deployments. Some data loss will happen if data can’t be transferred.
Unified roaming architecture and signaling
  Solution should be built upon the same roaming architecture as used for seamless roaming through the serving AP MLD and should leverage same set of roaming signaling defined.

## Slide 5: Roaming through the Target AP MLD (1)
We assume same roaming architecture as in [1] where a non-AP MLD establishes s single secure association with an SMD (Seamless Mobility Domain) covering multiple AP MLDs
  Same keys (PMK, PTK) are shared across AP MLDs. This enables a non-AP MLD to exchange PMF protected roaming signaling with the Target AP MLD, without first requiring to establish a new PTK.
  Sharing same keys enables better roaming experience through a target AP MLD. After roaming is completed, PTK rekeying is initiated to generate a new PTK for the target AP. The old PTK is shared by the target AP MLD only for a short period of time.
We also note that:
  Roaming through serving AP MLD is strongly preferred and will provide more reliable and deterministic roaming experience - minimal interruption and zero/minimal data loss (with dual DL path during roaming).
  Decision to roam through a target AP MLD is made by the non-AP MLD based on RSSI and other factors and may not necessarily be limited to only when the RSSI suddenly drops.
We consider two cases:
  Case 1: Roaming through Target AP MLD when no roaming prep was done in advance with serving AP MLD
  Case 2: Roaming through Target AP MLD when roaming prep was done in advance with serving AP MLD

## Slide 6: Roaming through the Target AP MLD (2)
Case 1: Roaming through Target AP MLD, w/o advance roaming preparation
  STA sends Link Reconfiguration Request to target AP MLD and signals old serving AP MLD
    The frame is sent as PMF protected
  Target AP MLD fetches keys (PMK, PTK) for the non-AP MLD (if not already installed), and uses to process received Link Reconfiguration Request
  Target AP MLD requests context transfer (SN, PN, BA, agreements)
  Target AP MLD may optionally support & request data transfer from serving AP MLD
  Target AP MLD initiates DS mapping update and sends Link Reconfiguration Response
  Note: Same roaming signaling is used as for the roaming through a serving AP MLD.

## Slide 7: Roaming through the Target AP MLD (3)
Case 2: Roaming through Target AP MLD, with advance roaming preparation
  Roaming preparation phase (steps 1-4) done in advance to transfer near static contexts (e.g. agreements, capabilities) to candidate Target AP MLDs. Keys (PMK, PTK) for the non-AP MLD are fetched, if not already installed.
  STA selects one of the target AP MLDs where roaming prep was done. Roaming execution steps though the target AP MLD are same as in case 1.
  Roaming execution (steps 6-9) is much faster:
    Keys already installed; most context already transferred.
    Only dynamic context (SN, PN, BA) need to be transferred. Optionally data may be transferred.
  Note: Same roaming signaling is used as for the roaming through a serving AP MLD.

## Slide 8: Data Transfer Considerations
To minimize data loss, it would be desirable to transfer data from old serving AP MLD to target AP MLD.
However, transferring data would require high throughput connection between all AP MLDs. Based on the backhaul capability, this may or may not be supported in all deployments.
Furthermore, it is not straightforward to take out and transfer MPDUs buffered deep in the hardware queue. It is much easier to transfer buffered MSDUs/A-MSDUs.
Hence requirement for data transfer need to be optional, based on these considerations.
Selective data transfer (e.g. MSDUs/A-MSDUs for specific TIDs or SCS flows) may be done either based on the request from the non-AP MLD or determined by the AP MLDs

## Slide 9: Summary
We highlighted that a non-AP MLD may not always be able to perform seamless roaming through its serving AP MLD
We proposed a mechanism for coordinated roaming through the target AP MLD
  It provides data continuity by transferring data exchange context, and preserves other control plane context
  Roaming through target AP MLD is faster with the roaming preparation phase done (in advance)
  Data transfer can be optionally (and selectively) done to minimize data loss, if supported by AP MLDs
We noted that sharing same keys (PMK, PTK) is strongly desirable to achieve better/seamless roaming experience through a target AP MLD.
We also noted that still Roaming through the serving AP MLD is strongly preferred and will provide more reliable and deterministic roaming experience. When that is not possible, the roaming through target AP MLD can be done.

## Slide 10: SP1
Do you agree to define a mechanism in 11bn that enables a non-AP MLD to initiate roaming through a target AP MLD it roams to, where the target AP MLD initiates context transfer from the previous serving AP MLD to the target AP MLD such that the data exchange context is preserved for the non-AP MLD?

## Slide 11: References
[1] 11-23-2157 “Seamless Roaming within a Mobility Domain”
[2] 11-22-1910 “Seamless Roaming for UHR”
[3] 11-23-1996 “Improve roaming between MLDs”
[4] 11-24-0052 “Seamless Roaming Details”