## Slide 1: Improving Acknowledgment Mechanisms
Date: 2024-03-10
Authors:
Name | Affiliation | Address | Phone | Email
Sherief Helwa | Qualcomm Inc. |  |  | shelwa@qti.qualcomm.com
George Cherian |  |  |  | 
Alfred Asterjadhi |  |  |  | 
Abhishek Patil |  |  |  | 
Gaurang Naik |  |  |  | 
Duncan Ho |  |  |  | 
Sanket Kalamkar |  |  |  | 
Giovanni Chisci |  |  |  | 

## Slide 2: Introduction
Certain 11bn features benefit from improving the ack mechanisms.
One such example is Dynamic Unavailability Operation (DUO) scheme where acknowledgment information may require more context to be correctly interpreted by the AP.
For a non-AP STAs operating in DUO mode:
  Errors in received PPDUs can be caused by external reasons such as bad channel quality or internal reasons such as internal interference.
  Internal interference takes place when a received PPDU overlaps with a CoEx event going on the background.
In this contribution we propose a simple mechanism to provide error context to the AP to understand the source of error and react accordingly.
Additionally, we cover some other details regarding the formatting of feedback info a DUO STA provides to its associated AP.

## Slide 3: Dynamic Unavailability Operation (DUO)
Before a DUO STA becomes unavailable due to IDC transmission, its peer STA needs to be made aware of its unavailability.
Two mechanisms can be used to achieve that goal:
  Solicited unavailability reporting
  Unsolicited unavailability reporting

## Slide 4: Internal Interference Indication
In some scenarios, a STA’s unavailability period may overlap with some data PPDUs causing errors.
In that case, it will be useful if the STA indicates to the AP that those errors are due to internal interference.
We propose to have a 1-bit indication sent back by the STA conveying this information.

## Slide 5: Multi-STA BA Frame Format
Multi-STA BA was agreed to be used as a carrier for control feedback information where the control info is included instead of the BlockAck Bitmap in Per AID TID Info field.
Since there are different types of possible feedback info to report. Therefore, there is a need to include a “Feedback Type” field in the Per AID TID Info field to indicate the type of control info included in this field.
We propose to set the length of the “Feedback Type” field to 4 bits and include it in the last 4 bits of the “Block Ack Starting Sequence Control” field, i.e., B12 to B15.
  The rest of the “Starting Sequence Number” field will be reserved.
  For example, the “Feedback Type” field will be set to 0 to indicate DUO unavailability info.
Set to 0 to indicate DUO unavailability info

## Slide 6: Unavailability Info Format
It is agreed to report the DUO unavailability information in terms of two parameters/fields (Motion 142):
  Unavailability Target Start Time (9 bits)
  Unavailability Duration (9 bits)
We propose the following encoding for these two fields:
  Unavailability Target Start Time (9 bits):
    This subfield contains a positive unsigned integer corresponding to a partial TSF time at which the unavailability event is expected to start
    Except that this subfield is reserved (i.e., invalid and to be ignored by the recipient) if the Unavailability Duration subfield is equal to 0
  Unavailability Duration (9 bits)
    This subfield is set to the estimated duration, in units of 64 microseconds, of the unavailability event except that
      The value 0 indicates that the STA is available
      The value 511 indicates that the STA is unavailable for an indefinite duration of time
        The STA shall use the value 511 only if the unavailability duration is unknown
    After a DUO STA reports an indefinite duration of unavailability, it can later update its state by sending an unavailability report with Unavailability Duration set to 0 to indicate availability or another value that is not equal to 511 to report updated unavailability.

## Slide 7: Summary
The idea of providing error context is discussed in DUO scenarios.
Details for DUO-related signaling was discussed including:
  How to indicate the control feedback information type included in a Multi-STA BA frame and how to use that for the DUO mode.
  Internal error indication made by the DUO STAs in cases of overlap with CoEx activity.
  The encoding of unavailability information reported by a DUO STA.

## Slide 8: Straw Poll 1
Do you support to add internal errors reporting in M-BA frame
  Internal (in device) Error Occurred bit is 1 if internal (in-device) error(s) occurred during the reception of the PPDU that solicited the M-BA response
    I.e., unsuccessful RX reports in BlockAck Bitmaps in the M-BA are due to internal errors
  Internal (in device) Error Occurred bit is 0 if no internal (in-device) error(s) occurred or if the source of error is unknown
    I.e., unsuccessful RX reports (if any) in BlockAck Bitmaps in M-BA are not due to internal (in-device) errors or if the source of error is unknown
  Location of the Internal Error Occurred bit in the M-BA frame is TBD
  Note: Internal errors might be due to internal in-device coexistence or other internal limitations

## Slide 9: Straw Poll 2
Move to amend the TGbn SFD as follows:
TGbn defines a special Feedback Per AID TID Info field (name TBD) that carries control feedback in the Multi-STA BA frame
  The control feedback (i.e., unavailability indication) is carried instead of the BlockAck Bitmap in that Feedback Per AID TID Info field
  The Ack Type subfield of the Per AID TID Info field is set to 0 and the TID subfield of the Per AID TID Info field is set to the value 13
  The AID11 subfield of this Per AID TID Info field is set to 2008 if the control feedback is addressed to all STAs or to the AID11 that identifies the intended recipient STA
  The Starting Sequence Number field of this Per AID TID Info field is reserved
  A “Feedback Type” field (4-bit field – B12 to B15 of the “Block Ack Starting Sequence Control” field) which is set to 0 to indicate that this Per AID TID Info field is carrying CoEx unavailability information.
    The rest of the “Starting Sequence Number” bits are reserved.