## Slide 1: Considerations on Dynamic Subchannel Operation - Follow up
Date: 2024-03-15
Authors:
Liuming Lu (OPPO)
Name | Affiliation | Address | Phone | Email
Liuming Lu | OPPO |  |  | luliuming@oppo.com
Chaoming Luo |  |  |  | 
Liangxiao Xin |  |  |  | 
Ning Gao |  |  |  | 
Yapu Li |  |  |  | 

## Slide 2: Introduction
UHR takes efficient use of the medium for enhancement of WLAN reliability as a main Objective
at least one mode of operation capable of improving efficient use of the medium compared to IEEE P802.11be.[1]
Dynamic Subchannel Operation (DSO) that allows a 20MHz non-AP STA to be allocated resource on the secondary 20MHz channel that is outside of the STA’s operating bandwidth has been prosposed by members [2]
This contribution further analyzes the method of DSO and proposes a mechanism for the flexible management of DSO mode in UHR

## Slide 3: Recap: SST as an operation during TWT SPs
HE subchannel selective transmission（SST） operation
SST setup by negotiation of individual TWT:
An HE SST non-AP STA and an HE SST AP set up SST operation by negotiating a individual trigger-enabled TWT
TWT Channel field of the TWT element is used to indicate the secondary channel in TWT request/response.
Frame exchanges during SPs:
the HE SST AP allocates individually addressed RUs addressed to the HE SST non-AP STA that are within the subchannel(s) indicated in the TWT Channel field of the TWT response
the HE SST non-AP STA is available in the subchannel(s) indicated in the negotiated TWT Channel field at TWT SP start times.
SST teardown (i.e. the termination of the trigger-enabled TWT), caused by
The AP’s operating channel or channel width changes and
any secondary channel of a trigger-enabled TWT is not within the new operating channel or channel width

## Slide 4: DSO as a mode of operation
The benefit from DSO depends on what channel bandwidth AP can gains, the channel conditions (such as IDC issue, OBSS interference) and requirements of QoS and power save for the AP and non-AP STAs.
Enable or disabling DSO mode can be a good tool for the flexible management of DSO. STAs may disable DSO mode based on the following conditions :
The channel(s) outside of STAs’ operating channel but within their associated BSS’ bandwidth is unavailable for the STAs, such as the channels are occupied by other wireless technologies, such as Bluetooth,
The channel(s) outside of STAs’ operating channel but within their associated BSS’ bandwidth are interfered by OBSS transmissions.

## Slide 5: DSO as a mode of operation (Cont.)
DSO-capable non-AP STAs can enable or disable the DSO mode when it is associated with DSO-capable/DSO-allowed AP
Enabling the DSO mode, the STA can
operate on its current operating channel(s) when no DSO initial control frame (ICF) addressed to it is received
do frame exchanges on its DSO channel(s) followed by an DSO ICF addressed to it from its associated AP.
wherein the DSO channel(s) can be outside of the STA’s current operating channel(s) but within the operating channel(s) of its associated AP with which the STA is associated.
Disabling the DSO mode, the STA always
operate on the current operating channel

## Slide 6: DSO as a mode of operation (Cont.)
Signaling for DSO
Enabling DSO mode:
An DSO-capable non-AP STA can enable dynamically DSO mode by notifying the DSO-capable AP or by negotiating with the DSO-capable AP.
DSO operation parameters, such as DSO mode indication（enabling DSO mode）, DSO channel, DSO maximum operating bandwidth ,DSO padding delay, is carried in the DSO mode exchange frames (such as DSO mode notification frame).
Frame exchanges in DSO mode:
When obtaining a TXOP on the DSO channel, the DSO-capable AP allocates individually addressed RUs addressed to the DSO-capable non-AP STA that are within the DSO channel indicated in the DSO mode notification frame or DSO mode response frame by sending DSO initial control frame
the DSO-capable non-AP STA switch to the DSO channel when receiving DSO initial control frame addressed to it, and than exchange frames with the AP, and switch back to the operating channel after the end of the frame exchanges.
Updating parameter(s) in DSO mode.
An DSO-capable non-AP STA in DSO mode can update dynamically current operating channel and/or DSO parameters by sending a DSO mode notification frame with DSO mode indication (enabling DSO mode) and DSO parameters to be updated to the DSO-capable AP . AP responds to the DSO mode notification frame
Disabling DSO mode：
An DSO-capable non-AP STA can disable DSO mode by sending a DSO mode notification frame with DSO mode indication (disabling DSO mode) to the DSO-capable AP.

## Slide 7: Example for disabling/enabling DSO mode
Non-AP STA can disable/enable DSO mode depending on their QoS requirements and channel conditions.
At the beginning STA2 disables the DSO mode as the channel condition for the DSO channel is not well, such as OBSS interference suffered.
STA2 enables the DSO mode by sending DSO mode notification frame after some time as the channel condition for the DSO channel becomes well
AP responds to the DSO mode notification frame by sending another DSO notification frame, which causes STA2 to enter into DSO mode.

## Slide 8: Example for updating operating parameters
Non-AP STA can update the operating parameters in DSO mode depending on their requirement for QoS and power save.
At the beginning the STA communicates with the AP through primary 40MHz channel
The STA enables the DSO mode for updating the operating parameters by sending DSO mode notification frame based on the power save requirement.
AP responds to the DSO mode notification frame by sending another DSO notification frame, which causes the STA to enter into DSO mode.
The operating parameters: primary 20MHz channel (the maximum bandwidth is 20MHz)
The DSO operating parameters: primary 40MHz channel (the maximum bandwidth is 40MHz)

## Slide 9: Summary
UHR takes efficient use of the medium for enhancement of WLAN reliability as a main Objective
DSO as a mode of operation and the mechanism for the flexible management of DSO mode is suggested to be specified in UHR
Enabling/disabling the DSO mode based on the channel conditions and requirements of QoS and power save for DSO-capable non-AP STAs.
updating the operating parameters in DSO mode depending on the requirements of QoS and power save for DSO-capable non-AP STAs.

## Slide 10: Reference
[1] UHR proposed PAR, https://mentor.ieee.org/802.11/dcn/23/11-23-0480-01-0uhr-uhr-proposed-par.pdf
[2] Dynamic Subband Operation, 11-22-2204-00-0uhr-dynamic-subband-operation , https://mentor.ieee.org/802.11/dcn/22/11-22-2204-00-0uhr-dynamic-subband-operation.pptx
Liuming Lu (OPPO)

## Slide 11: SP
SP : Do you support to specify a mechanism for enabling or disabling Dynamic Subchannel Operation (DSO) mode in UHR?
DSO: a mode of operation that allows a non-AP STA to operate on its current operating channel(s) when no DSO initial control frame (ICF) addressed to it is received and to do frame exchanges on its DSO channel(s) followed by an DSO ICF addressed to it, wherein the DSO channel(s) can be outside of the STA’s current operating channel(s) but within the operating channel(s) of its associated AP with which the STA is associated.
The parameters carried in the frame(s) for enabling or disabling DSO are TBD.
Liuming Lu (OPPO)