## Slide 1: Multi-AP Sounding
Date: 2024-04-15
Authors:

## Slide 2
Abstract
In this contribution we share some thoughts on multi-AP sounding procedure that is needed for coordinated multi-AP operations.

## Slide 3: Introduction
Multi-AP has been proposed as a UHR feature, including coordinated operations such as
  Coordinated OFDMA
  Coordinated rTWT/TWT
  Coordinated spatial reuse
  Coordinated beamforming
  Joint transmission
These multi-AP operations requires participating APs and STAs to know channel conditions
  Between neighboring APs
  Between STAs and neighboring APs and STAs
Multi-AP sounding procedure can provide the needed information
  Different multi-AP operations requires different levels of details of channel conditions
  Coordinated TDMA requires the least amount of channel information (e.g., APs need to be in range)
  Coordinated TDMA/OFDMA/TWT/SR may just require SNR feedback
  Coordinated BF/JT requires more detailed channel information
In this contribution, we present some thoughts on multi-AP sounding procedures

## Slide 4: Multi-AP Sounding Procedures: leveraging C-TDMA
  C-TDMA has been discussed as an EHT/UHR feature
    C-TDMA allows a number of neighboring APs to transmit or trigger transmissions from their associated STAs to transmit consecutively
      Suitable for sounding frames transmission and for sounding feedback polling
    In addition, C-TDMA requires very limited channel information between OBSS STAs (e.g., just APs need to be within range of each other)
      Hence C-TDMA does not require multi-AP sounding results first to function
    Multi-AP sounding procedure can leverage C-TDMA procedure for efficient collection of channel information

## Slide 5: Review of C-TDMA Procedure (1)
  There are two proposals for C-TDMA
  C-TDMA Option 1: Original C-OFDMA proposal for 802.11be [2]
    If no frequency resource sharing, it becomes C-TDMA
    Sharing AP uses CTI to indicate shared TXOP
    Sharing AP uses CTAS to indicate AP TX schedule
    Shared APs to use CTLS to announce local schedule
CTI: CAP TXOP Indication frame
CTR: CAP TXOP Request frame
CTAS: CAP TXOP AP Schedule frame
CTLS: CAP TXOP Local Schedule frame

## Slide 6: Review of C-TDMA Procedure (2)
  C-TDMA Option 2: extending MU-RTS TXOP Sharing Procedure, e.g., [3][4]
    Extending MU-RTS TXOP sharing, which is currently defined between an AP and a non-AP STA, to between AP to AP

## Slide 7: Multi-AP Sounding Procedure using C-TDMA (1)
  Both approaches of C-TDMA can be used to define a multi-AP sounding procedure with sufficient modifications:
  C-TDMA Option 1: original C-OFDMA proposal for 11be [2]
    Multi-AP sounding procedure
    CTAS can also be a newly defined multi-AP NDPA
    High level directional presentation only, some details are missing (e.g., TXOP return step)

## Slide 8: Multi-AP Sounding Procedure using C-TDMA (2)
  C-TDMA Option 1: original C-OFDMA proposal for 11be [2]
    Multi-AP sounding feedback procedure
    Issues to consider
      Signaling to indicate MAP sounding/feedback: mandating shared APs’ behaviors

## Slide 9: Multi-AP Sounding Procedure using C-TDMA (3)
  C-TDMA Option 2: Extending MU-RTX TXOP Sharing to AP to AP, e.g., [3][4]
  Issues to consider:
    Additional indication of sounding: mandating shared AP’s behavior
    Using this approach is beneficial to legacy STA, but do we need to consider legacy STA in the inter-AP TXOP sharing case?
    Using CTS, it is not clear which APs responded; suitable for sharing TXOP with just 1 AP

## Slide 10: Conclusions
  We shared our thoughts on Multi-AP Sounding Procedure
    A suitable approach could be leveraging C-TDMA procedure
  Two approaches for Multi-AP sounding leveraging C-TDMA procedures were discussed (High level directional presentation only, some details are missing (e.g., TXOP return step)):
      Option 1: based on the original C-OFDMA proposal [2] but without frequency resource sharing
      Option 2: based on extending MU-RTS TXOP Sharing Procedure
  Both approaches can be used given sufficient modifications
  For Multi-AP sounding, Option 1 is easier to enable sounding for the case of more than 2 APs

## Slide 11
References
[1]11-23/0041r0, Considerations on Coordinated TDMA (C-TDMA), Yanjun Sun
[2] 11-19/1582r1, Coordinated AP Time/Frequency Sharing in a Transmit Opportunity in 11be, Lochan Verma
[3] 11-23/1895r2, Coordinated TDMA (C-TDMA) Follow-up, Abhishek Patil
[4] 11-24/411r0, TXOP Return in C-TDMA, Geonhwan Kim

## Slide 12: Related Motions from EHT [1]
Define a procedure for an AP to share its frequency/time resources of an obtained TXOP with a set of APs.
  Set of APs is TBD.
  [Motion 56]
An EHT AP which obtains a TXOP and initiates the multi-AP coordination is the sharing AP.
  An EHT AP which is coordinated for the multi-AP transmission by the sharing AP is the shared AP.
  NOTE – The name of the sharing AP and the shared AP can be modified.
  [Motion 73]
802.11be supports the following:
  Sharing AP and shared AP may not have the same primary 20 MHz channel.
  The primary 20 MHz channel of the shared AP shall be within the BSS operating channel width of the sharing AP.
  The primary 20 MHz channel of the sharing AP shall be within the BSS operating channel width of the shared AP.
  [Motion 119]
802.11be shall define an AP candidate set* as follows:
  An AP candidate set is a set of APs that can initiate or participate in multi-AP coordination.
  An AP in an AP candidate set can participate as a shared AP in multi-AP coordination initiated by a sharing AP in the same AP candidate set.
  At least one AP in an AP candidate set shall be capable of being a sharing AP.
  NOTE – The name* can be changed.
  [Motion 124]
  Source DNC: 20/1935r66

## Slide 13: SP #1
Do you agree that a Multi-AP sounding procedure should be defined for 802.11bn

## Slide 14: SP #2
Do you agree that a multi-AP sounding procedure should be defined using the C-TDMA procedure?