## Slide 1: Low Power and Long-Range Preamble Follow Up
Apr 2024
Authors:
Name | Affiliation | Phone | email
Brian Hart | Cisco Systems |  | brianh@cisco.com
Malcolm Smith | Cisco Systems |  | 
Juan Carlos Zuniga | Cisco Systems |  | 
Stephen Orr | Cisco Systems |  | 
Jerome Henry | Cisco Systems |  | 

## Slide 2: A Low Power Listening Mode was proposed in [1][2] …
Hart et al (Cisco Systems)
The initial frame provides flexibility for implementation on the listening operation.
Different implementations can choose their preferred alternative to leverage the initial frame and trade off.
Client only has its lower-power mode radio awake (low MCS-capable, 1SS)
RTS/Trigger indicates the recipient and lists many PHY parameters (NSS, bandwidth, MCS)
Based on RTS/Trigger, client can wake up and tune the resources needed for its high-power radio

## Slide 3: … yet this seems inefficient
Hart et al (Cisco Systems)
This is a Trigger frame sent before transmitting on the downlink
The NSS, MCS and BW fields are already signaled in the preamble of the main PPDU – so this is sending SIG info duplicates
Is there a more efficient option that allows for just CTS2self, or no MAC protection at all?
For context:
    RTS + SIFS + CTS + SIFS at non-HT/MCS0 is 128 usec long; then “UHR-SIG” info adds a further N*4 usec.
    CTS2self at non-HT/MCS0 is 60 usec
    Signal-able EMLSR transition delays are 0/16/32/64/128/256 usec
Observation: many EMLSR transition delays are much lower than 128 + N*4 or even 60 usec

## Slide 4: Proposal: Preamble Extension Follow-up from [3]
Hart et al (Cisco Systems)
A Preamble Extension field is inserted between:
      Signaling of recipient(s) and their NSS(s), BW(s) and MCS(s) (etc) …
      … and when that signaling is utilized
The minimum duration of the Preamble Extension field needed by the recipient is negotiated with it
An indication of the duration of the Preamble Extension field is provided in an earlier field (e.g., USIG)
LSTF
LLTF
LSIG
R-LSIG
USIG
UHR SIG
Preamble Extension
UHR STF
UHR LTF
Data
PE
Padding used to wake up hi-capability RX
Single copy of SIG parameters
Hi-capability receiver finishes processing the PPDU
Lo-capability receiver initially processes the PPDU (1SS, low MCS, BSS BW)
Signaling of Preamble Extension field duration

## Slide 5: Contents of Preamble Extension
R-USIG
Three natural options for the contents of the Preamble Extension field:
      Repeated USIG and UHR SIG
        Also enables longer range if the entire Preamble Extension is not required to wake up the hi-capability receiver
      Extended UHR STF
        Simplest, helps with any new CFO-related transients
      A mix of these options
LSTF
LLTF
LSIG
R-LSIG
USIG
UHR SIG
UHR STF
UHR LTF
Data
PE
R-UHR SIG
E-UHR STF
Assume UHR picks one of these options
E-UHR STF
R-USIG
R-UHR SIG
Preamble Extension

## Slide 6: Summary
Hart et al (Cisco Systems)
We propose an extended preamble for power savings
Especially when a hi-capability receiver can be woken up relatively quickly, the extended preamble provides greater efficiency than RTS/Trigger + CTS frames sent before transmitting data on the downlink
When the preamble is includes a repeated U-SIG and repeated UHR-SIG, and when the hi-capability receiver is always active, then the same preamble can instead provide for long range operation.
      Synergistic with DL DRU and SU UL DRU

## Slide 7: Strawpoll
Do you agree to add the following text to the 11bn SFD:
  11bn shall define a preamble that supports low power operation via early reporting of bandwidth, MCS and number of spatial streams.
  Note: TBD if this replaces/complements an RTS/Trigger frame that carries early reporting of bandwidth, MCS and number of spatial streams.
Y / N / A

## Slide 8: References
[1] 22/1414, “Low Power Listening Mode”, Xiaogang Chen (Zeku)
[2] 22/1841, “Follow up on the low power listening”, Xiaogang Chen (Zeku)
[3] 23/1100, “Low Power and Long Range Preamble”, Brian Hart (Cisco Systems)