## Slide 1: MAPC Coordinated Service Periods (MAPC SPs)
Mar 2024
Authors:
Name | Affiliation | Phone | email
Brian Hart | Cisco Systems |  | brianh@cisco.com
Malcolm Smith | Cisco Systems |  | 
Binita Gupta | Cisco Systems |  | 
Juan Carlos Zuniga | Cisco Systems |  | 
Stephen Orr | Cisco Systems |  | 
Jerome Henry | Cisco Systems |  | 

## Slide 2: Background
The Multi-AP Coordination (MAPC) topic spans many technologies from low to high complexity
For assurance that standardized MAPC is implementable, the 11bn draft should define (as a minimum) a valuable and simple MAPC technology
  Valuable:
    Provides much greater assurances of determinism than heretofore
    Does not impose hard-to-meet constraints in a multi-AP environment and/or on devices with IDC
The simplest technologies are time based: e.g., C-TDMA and C-R-TWT
In this presentation we describe a refinement that combines the best features of C-TDMA and C-R-TWT: Multi-AP Coordinated Service Periods (MAPC-SPs) akin to [3]

## Slide 3: Problem Statement We need to address all the dimensions else we run the risk of just solving niche problems that are not interesting enough to vendors/users
Goals for an IEEE-quality MAPC feature:
  Plausible that it can support overlapping networks from different administrative domains
    Meeting APs where they are: whatever position and channel
    With optimizations for APs within the same administrative domain
  Enables a multi-service network that simultaneously supports:
    Ultra-reliable, ultra-low latency channel access truly capable of supporting Time-Sensitive Networking (TSN)
      AR/VR, automated manufacturing
      And other QoS/scheduled traffic, which can start and stop
    Devices subject to irregular in-device coexistence (IDC) challenges
    Clock skew
    Legacy APs and clients, and power save
  Compliant with global regulations
  Provides:
    High system efficiency
    Implementation simplicity
    Acceptable fairness with legacy generations
Key: Circle = BSS’s coverage; green = BSSs on one channel, blue = BSSs on another channel; white = BSSs on different channels (uncolored for clarity).

## Slide 4
Multi-AP Coordination Service Periods (MAPC-SPs)
Concepts

## Slide 5: Core Concept
APs understand all traffic that is offered at periodic times in their BSS and in their 1-hop neighboring BSSes
  Secure AP2AP communication channels are assumed
APs apply policy & negotiate with peer APs to determine mutually-agreed SLAs for such periodic traffic
  Near-term: same administrative domain: common set of policies
  Behavior-based trust between admin domains: “I’ll help you if and while you help me when I need your help”
All APs seek to achieve the mutually agreed SLAs of all the mutually agreed periodic traffic in their neighborhood
  According to priority
The TXOPs of the mutually agreed periodic traffic are protected by:
  C-TDMA with SP-chaining: a TXOP holding AP leverages the NAV rules to ensure that the next TXOP holder(s) are the OBSS AP(s) with the next burst of highest priority periodic traffic, or
  Courtesy: other APs end their intra-BSS TXOPs immediately before the expected OBSS periodic traffic
The basic unit is the Multi-AP Coordination Service Period (MAPC-SP, or just SP)
  In a MAPC-SP, one AP initiates one TXOP or multiple (tightly-coupled) TXOPs for a burst of periodic traffic
  The SP has an actual start time that is the same or later than the Target SP Transmission Time (TSTT)
  The SP might be paused due to a higher priority SP, then resumed later
  The SP has a distinct, non-time-bounded end that is understood by both sides

## Slide 6: Example Problem
Consider 3 APs in range of each other, with multiple QoS flows per BSS
  NOTE - we treat Beacon + DTIM groupcast as additional periodic traffic (typically with highest priority)
In general, each instance of periodic traffic has different Start Times and Service Intervals (i.e., different TSTTs), different priorities, different Delay Bounds and unpredictable / time-varying Service Period durations
In this example, at any given time, the ideal time for the SPs of the periodic traffic overlap
  Also, due to clock drift (exaggerated for clarity), the relative timing of the TSTTs can change
Key: B = beacon (of multiple SSIDs, G = DTIM groupcast

## Slide 7: What Success Looks Like (assuming QoS flows have equal priority)
Typically, the beacon bursts have highest priority and go out in TBTT order, regardless of BSS
Then we have SPs scheduled by priority order, regardless of BSS
Like Beacons, the relationship between the TSTT and the actual start time of a SP is decoupled
  NOTE: This decoupling is also helpful for devices with IDC
  Beyond traditional R-TWT, the traffic of a SP can be attempted at any time, from its TSTT until its expiry
Key: B = beacon (of multiple SSIDs, G = DTIM groupcast; White = Target SP Transmission Time (TSTT) and actual SP duration, blue = when SP is transmitted. Tall blue rectangles are MU PPDUs

## Slide 8
Multi-AP Coordination Service Periods (MAPC-SPs)
Steps

## Slide 9: Step 1: QoS flow and QoS Flow-Set Information is Disseminated
Clients report their periodic traffic (and seek reliable delivery as described by corresponding SLAs) to their APs via SCS(QC) etc; APs apply policy; and intra-BSS negotiations converge
APs treat their periodic beacons and DTIM groupcast flows as further periodic traffic
APs might apply DPI or traffic analysis to discern other periodic traffic
  Especially for deep-legacy clients
APs aggregate like periodic traffic and create Periodic Traffic Scheduler Inputs (PTSIs)
Periodic Traffic Scheduler Input parameters are: SST, Service Interval, Delay Bound (& MSDU Delivery Ratio), Priority, Min SP Duration, (nominal SP duration), ((min data rate)), etc
  … i.e., the minimal set of parameters needed for scheduling periodic traffic across APs
    TSTT is determined as SST + n × SI
  Delay Bound and Priority information are vital for scheduling (i.e., beyond traditional R-TWT parameters)
  Scheduling is easier when SST isn’t specified (but less latency-optimal)
  Due to MLO, VBR, retries, rate adaptation, deferral for legacy Wi-Fi and non-Wi-Fi interference, there can be no expectation that SPs have any particular duration, but a Min Requested SP Duration is needed for negotiations
APs report their Periodic Traffic Scheduler Inputs to neighboring (1-hop) cochannel APs
APs apply policy & negotiate with peer APs to establish mutually agreed Periodic Traffic Scheduler Inputs
  Note that APs may not align on all their peer APs’ Periodic Traffic Scheduler Inputs , or may commit to a reduced SLA: such as lower Priority, MSDU Delivery Ratio, Min SP Duration, C-TDMA sharing (or not) etc

## Slide 10: Step 2: Each AP schedules MAPC-SPs towards meeting all the Periodic Traffic Scheduler Inputs (Priority-based)
All APs seek to achieve the SLAs described by the mutually agreed Periodic Traffic Scheduler Inputs in their neighborhood, in priority order, using distributed logic
A TXOP-holding AP uses coordination techniques (mainly C-TDMA) to offer medium time to a neighboring AP to meet that AP’s expected (current/overdue) SP(s) whenever the underlying PTSI(s) are agreed and have higher priority than the AP’s own SP(s)
This may involve the Pause+Resume of a long SP if a higher priority SP begins in the middle.
This does not always work – e.g., the AP/STA with the highest priority SP is 1-hop away but is busy due to activity in a 2-hop BSS; so later C-TDMA polling may be required

## Slide 11: Step 3: MAPC-SPs are supported by neighboring APs via C-TDMA chaining and/or Courtesy
One contention enables the transmission of back-to-back SP(s) until finished or the TXOP limit is reached
The latest C-TDMA proposals recommend TXOP chaining for setting the NAV across BSSs
  i.e., the TXOP holding AP sets the NAV for its planned PPDUs/SPs plus some extra time
  Then the next AP is assigned the medium for its planned PPDUs/SPs
MAPC-SPs leverage such C-TDMA chaining, with flexibility:
  One contention for 0.5 or 1 or M SPs at one AP; or 2 SPs across 2 APs; … or M SPs across N APs:
    AP 1 to AP 2 (trivial C-TDMA)
    AP 1 to 2 to 3 … (multi-AP C-TDMA)
    AP 1 to 2 to (3 || 4) to 2 … (fully flexible)
    … while there are back-to-back SPs, … via C-TDMA chaining and the Initial+Final Control frames
If the TXOP limit is reached, MAPC-SPs continue via Courtesy:
  Other APs do not contend while another AP has higher priority SPs
For coordination purposes, it is desirable that APs, via Initial + Final Control frames, report SP progress

## Slide 12: Step 4a: All Other Time Remains Available for CSMA/CA Subject to upcoming MAPC-SPs being protected
A typical system with have long periods of CSMA/CA interrupted by short MAPC-SPs chains
The CSMA/CA time can be consumed by aperiodic high priority traffic, deferred retries of flow-sets, BE/BK traffic, probing, PM transitions, etc etc
Still, at the next TSTT of an AP, the AP needs to begin its SP with no delay
Define the Start Time Protection Rule (STPR) (from R-TWT) as the requirement that all TXOPs end before an upcoming SP
  NOTE – in MAPC-SP, the R-TWT STPR does not require an R-TWT agreement
Several options to protect upcoming MAPC-SPs:
  Option A: APs announce upcoming TSTTs as needing the STPR (e.g., Beacons, or new fields in Initial / Final CFs). Clients that can’t honor this use options B/C instead
  Option B: APs take care of the STPR for clients proactively via triggered access: APs end each TXOP before the next TSTT (or chain their TXOP via C-TDMA). For unexpected uplink traffic, UORA (or something better) is made ubiquitously available
  Option C: APs take care of the STPR for clients reactively via TXOP truncation:
    DL: APs end their TXOPs by the next OBSS TSTT or transfer the TXOP to that AP (C-TDMA via TXOP chaining)
    UL: RTS is required at the start of UL TXOPs and the AP truncates the TXOP (e.g., via IDC signaling [1-2]) before the next TSTT.

## Slide 13: Step 4b: Example of making all other time available for CSMA/CA
The Next TSTT Announcement might use legacy R-TWT signaling or other signaling

## Slide 14: MAPC-SPs build on C-R-TWT
 | Trigger-enabled C-R-TWT | MAPC-SPs = C-RTWT, consuming Periodic Traffic Scheduler Inputs and leveraging C-TDMA
Time scale | Ongoing | Ongoing
SP start time | Nominally TSTT, but can slide right; yet no SP if the start slides past the nominal SP end | Nominally TSTT, but can slide right, only limited by the Delay Bound
Pause + Resume across BSSs | No | Yes, to avoid priority inversion
End time | End of nominal SP duration / DL EOSP / UL BSR indicates no more traffic | Positive signaling (e.g., unicast bidir EOSP) and not limited by the nominal SP duration
(O)BSS Delay Bounds known & considered | Historically no (SCS(QC) is optional) | Yes (Periodic Traffic Scheduler Inputs required)
Channel Access | STPR + EDCA | STPR + EDCA + C-TDMA
Mechanism for improving QoS | The medium is reserved for QoS flows especially at the start of periodic SPs; but behavior during SP collisions may be erratic. | SPs are scheduled at regular TSTTs but a SP is understood to slide right or be paused + resumed due to higher priority traffic
Complications | To avoid/minimize C-R-TWT SP collisions, APs must agree on SI (or something close to this); so hard to scale across administrative domains or to address variegated traffic flows. Also there are occasions when beacon traffic invariably collides with C-R-TWT SPs | Transmitting SPs at TSTT, or at least in priority order, is imperfect due to colliding SPs, or exposed nodes (respectively); so, the scheduler must continually adapt with the potential for desultory C-TDMA polling

## Slide 15: Summary
We present “Multi-AP Coordinated SPs” (MAPC-SPs) as the solution to the initial problem statement
In a nutshell:
  Requirements for periodic traffic are discovered and each AP establishes zero or more Periodic Traffic Scheduler Inputs that are then disseminated to neighboring APs
    The Periodic Traffic Scheduler Input contains the minimal info to schedule periodic traffic: SST, Service Interval, Delay Bound (& MSDU Delivery Ratio), Priority, Min SP Duration
    Beacons + DTIM groupcast are treated as periodic traffic too
  For mutually agreed Periodic Traffic Scheduler Inputs, all APs seek to achieve the SLAs of their own and their 1-hop neighboring co-channel APs’ Periodic Traffic Scheduler Inputs
  APs are always attempting to schedule MAPC-SPs in agreed priority order
  MAPC-SPs are protected from other traffic via the STPR, then MAPC-SPs are scheduled and their transmission attempted in priority order via C-TDMA (using TXOP chaining up to the TXOP limit) or Courtesy.
  All time between the MAPC-SPs is available for CSMA/CA

## Slide 16: Strawpoll 1
Do you agree to add the following text to the 11bn SFD:
  11bn shall enable the exchange, via a secure channel, between neighboring co-channel APs that support multi-AP coordination of their Periodic Traffic Scheduler Inputs including priority and delay bound
Y / N / A

## Slide 17: Strawpoll 2
Do you agree to add the following text to the 11bn SFD:
  11bn shall enable a C-TDMA mode of operation whereby a TXOP may be granted sequentially to 2 or more APs
Y / N / A

## Slide 18: References
[1] 23/1934 In-device interference mitigation follow up, Liwen Chu/NXP
[2] 23/1964 Coexistence Protocols for UHR, Sherief Helwa/Qualcomm
[3] 23/1962 Gain analysis for coordinated AP transmissions, Abhishek Patil/Qualcomm