## Slide 1: Low latency channel access Legacy impact
Date: 2024-03-28
Authors :

## Slide 2: Recap from 11-23/1065r0: solution
Proposal is to isolate STAs with prioritized access from the rest of the STAs at the beginning of a contention period
  Achieve this by allowing these STAs to transmit a Defer Signal at the beginning of a contention period to force all STAs that are not sending the Defer Signal to have CCA busy/IEFS set and not participate in the contention period
  If multiple of these STAs have prioritized access, they will transmit the same Defer Signal at the same time with the same result on other STAs (CCA busy)
And then to allow for a contention only between the STAs with prioritized access
  Only STAs that have sent a Defer Signal can participate in this immediately following contention
  More degrees of freedom for the contention parameters setting to avoid collisions without loosing priority
    don’t necessarily need to be too aggressive in order to scale to a larger number of STAs while ensuring low collision rates (contrary to AC_VO)
Example:
  A device with the traffic in AC_VO use legacy EDCA to transmit data.
  Device is eligible to send DS signal if it experience a failure after using legacy EDCA and doubled its contention window
    After successfully attempting transmission using DS STA fall back to normal EDCA operations

## Slide 3: Recap from 11-23/2126r0
High Priority EDCA (HiP EDCA) mechanism based on transmission of a dedicated signal/frame prior the start of EDCA contention allow to improve tail latency :
  90-95-99th percentiles in both isolated BSS case and multi-BSS setup
  In situations with and without hidden nodes
The repetition of DS signal (i.e. an AP reply with same DS signal) has limited affect on tail latency improvement
In terms of design
  it is better to have “Unique” DS signal rather than “Common” one, i.e. signal to be specific to a BSS
  For simplicity it is better to have it in a form of short MAC frame with duration field and TA address
Rules to send DS signal need to be discussed
  Frequency of transmission
  Eligibility for transmission
    Currently propose use to use DS for AC[X] after Y failure
      Where Y is specific for X
  AIFSN boundary for transmission

## Slide 4: New material: Impact on legacy devices
What is the effect on legacy devices when UHR device use DS
  In a BSS a set of STAs is using DS for LL frame transmission and other – don’t
  One (or more) BSS use DS and another (or more) others don’t
  A mix of above

## Slide 5: Simulation configuration
Enterprise-like layout
  1, 2 or 4 BSSes with variable number of STAs: 5,6,..,15, 16
  Out of which 2, 3 or 4 are ULL STAs
  Other STA has bidirectional full buffer BE traffic.
2x2x20Mhz @ MCS0 and @ MCS7
TXOP limit = uniform (1.5ms; 5ms)
  New TXOP limit is selected each time when STA/AP won contention
  Randomization is only to introduce “burstiness” and extra randomness into channel occupancy time
  STA Cw = 15/1023; AP Cw=15/63
  TxPower: STA = 17dBm; AP=23dBm
Location
  STAs assigned on a grid across four 4x4 cube islands, AP in the middle of the island
  Overall area size is 80x80meters
80meters
80meters
28m
31m
50m
D=9
1
2
3
4
# STAs | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
# of VO STAs | 2 | 2 | 2 | 2 | 3 | 3 | 3 | 3 | 4 | 4 | 4 | 4
% of VO STA | 40 | 33 | 29 | 25 | 33 | 30 | 27 | 25 | 31 | 29 | 27 | 25

## Slide 6: HiP EDCA for AC VO, Multi-BSS setup in 80x80 area
Traffic:
  VO traffic (LL) is bi-directional
    160 bytes every average 16ms =uniform (10ms, 22ms) ~ 96Kbps
    1600 bytes every average 16ms =uniform (10ms, 22ms) ~ 768Kbps
    16000 bytes every average 16ms =uniform (10ms, 22ms) ~ 7.6Mbps
    32000 bytes every average 16ms =uniform (10ms, 22ms) ~ 15.3Mbps
  BE traffic (legacy) is bi-directional full buffer traffic, TXOP = uniform (1.5ms, 5ms)
Three cases:
  1 BSS case with
    ULL use AC_VO legend: VO
    ULL use DS legend: DS
    Half of streams in a BSS use VO and the other one use DS legend: half-VO / half-DS
  2 and 4 BSS case
    All BSSes use AC_VO for ULL legend: VO
    All BSSes use DS for ULL legend: DS
    Half of BSSes use AC_VO and the other half – DS legend: BSS-VO / BSS-DS
    Half of streams in each BSS use VO and the other use DS legend: half-VO / half-DS
DS usage policy:
  An LL STA use regular AC_VO to deliver buffered traffic
  A STA is eligible to use DS if it experience 1 failure after obtaining EDCA TXOP
  A STA switches back to normal EDCA operation after it successfully obtained TXOP using HiP EDCA

## Slide 7: 1 BSS case, LL packet size 160bytes
VO – all ULL use legacy EDCA Half VO – half of ULL use VO
DS – all ULL use DS Half DS – half of ULL use DS
Chart: 1 BSS case, 8 STAs in BSS, 2 ULL flows
| mean | 90 | 95 | 98 | 99
VO | 0.0024122 | 0.0044449 | 0.005862 | 0.0099489 | 0.012174
DS | 0.0020167 | 0.0037092 | 0.0042231 | 0.0046312 | 0.0048523
Half DS | 0.001999 | 0.0037362 | 0.0042263 | 0.0045479 | 0.0046855
Halfs VO | 0.0023377 | 0.0042788 | 0.0056681 | 0.0088838 | 0.011546
Chart: 1 BSS case, 9 STAs in BSS, 3 ULL flows
| mean | 90 | 95 | 98 | 99
VO | 0.0029029 | 0.0063681 | 0.0090815 | 0.011655 | 0.01437
DS | 0.0020745 | 0.0038562 | 0.0043037 | 0.0046961 | 0.0049493
Half DS | 0.0020442 | 0.0038765 | 0.0042478 | 0.0047587 | 0.0051255
Halfs VO | 0.0029349 | 0.006188 | 0.0086241 | 0.012087 | 0.013776
Chart: 1 BSS case, 12 STAs in BSS, 3 ULL flows
| mean | 90 | 95 | 98 | 99
VO | 0.0031672 | 0.0073209 | 0.010102 | 0.014038 | 0.016563
DS | 0.0020829 | 0.0037916 | 0.0043122 | 0.0047853 | 0.0051285
Half DS | 0.0020451 | 0.0038723 | 0.004318 | 0.0047949 | 0.0053695
Halfs VO | 0.0032273 | 0.0072493 | 0.010008 | 0.015015 | 0.017733
Chart: 1 BSS case, 13 STAs in BSS, 4 ULL flows
| mean | 90 | 95 | 98 | 99
VO | 0.0035338 | 0.0081388 | 0.011891 | 0.015585 | 0.018725
DS | 0.0020635 | 0.0039026 | 0.0044382 | 0.0049499 | 0.0053151
Half DS | 0.0020589 | 0.0039188 | 0.0044635 | 0.0051419 | 0.0057035
Halfs VO | 0.0032747 | 0.0074549 | 0.01015 | 0.013843 | 0.016754
Chart: 1 BSS case, 16 STAs in BSS, 4 ULL flows
| mean | 90 | 95 | 98 | 99
VO | 0.0035314 | 0.0087631 | 0.011152 | 0.014561 | 0.016741
DS | 0.0020647 | 0.0039056 | 0.0044477 | 0.0050327 | 0.0054896
Half DS | 0.0020505 | 0.0038417 | 0.0043539 | 0.0048325 | 0.0053032
Halfs VO | 0.0034549 | 0.0081083 | 0.011147 | 0.014105 | 0.017101
Chart: 1 BSS case, 5 STAs in BSS, 2 ULL flows
| mean | 90 | 95 | 98 | 99
VO | 0.002234 | 0.0042061 | 0.0051508 | 0.0076859 | 0.0084733
DS | 0.0019719 | 0.0035785 | 0.0041563 | 0.0045326 | 0.004674
Half DS | 0.0019224 | 0.0036102 | 0.0040787 | 0.0045722 | 0.0047167
Halfs VO | 0.0022233 | 0.0041835 | 0.004977 | 0.0074926 | 0.0089577

## Slide 8: 2 BSS case , LL packet size 160bytes
VO – all ULL use legacy EDCA Half VO – half of ULL in a BSS use VO BSS VO – half of BSSes use VO
DS – all ULL use DS Half DS – half of ULL in a BSS use DS BSS DS – half of BSSes use DS
Chart: 2 BSS case, 5 STAs in BSS, 4 ULL flows
| mean | 90 | 95 | 98 | 99
VO | 0.0029565 | 0.0067172 | 0.0092994 | 0.012298 | 0.013878
DS | 0.002094 | 0.0039468 | 0.0045109 | 0.0053097 | 0.0060466
BSS DS | 0.0019962 | 0.0037899 | 0.0043627 | 0.0049248 | 0.0053728
BSS VO | 0.0028254 | 0.0060216 | 0.0085676 | 0.01185 | 0.014509
Half DS | 0.0020818 | 0.0038126 | 0.0043469 | 0.0050082 | 0.0058946
Halfs VO | 0.0027564 | 0.0059525 | 0.0085144 | 0.010956 | 0.013102
Chart: 2 BSS case, 8 STAs in BSS, 4 ULL flows
| mean | 90 | 95 | 98 | 99
VO | 0.0032456 | 0.0077709 | 0.010988 | 0.014218 | 0.017399
DS | 0.002127 | 0.0040605 | 0.0045758 | 0.0052111 | 0.0058299
BSS DS | 0.0020497 | 0.0038767 | 0.0044814 | 0.0050506 | 0.0056945
BSS VO | 0.0030164 | 0.0067768 | 0.0096275 | 0.012952 | 0.016068
Half DS | 0.0020492 | 0.0038704 | 0.0044467 | 0.0051925 | 0.006027
Halfs VO | 0.0030678 | 0.007474 | 0.0098093 | 0.0139 | 0.017477
Chart: 2 BSS case, 9 STAs in BSS, 6 ULL flows
| mean | 90 | 95 | 98 | 99
VO | 0.0039837 | 0.0097057 | 0.012618 | 0.017175 | 0.019819
DS | 0.0021525 | 0.0040606 | 0.0046751 | 0.0054548 | 0.0066072
BSS DS | 0.0021573 | 0.0041088 | 0.0046944 | 0.005437 | 0.0059742
BSS VO | 0.003599 | 0.0087078 | 0.011534 | 0.015407 | 0.019655
Half DS | 0.0021366 | 0.0040034 | 0.0046827 | 0.0056733 | 0.0064368
Halfs VO | 0.0038153 | 0.0090346 | 0.012363 | 0.01688 | 0.020734
Chart: 2 BSS case, 12 STAs in BSS, 6 ULL flows
| mean | 90 | 95 | 98 | 99
VO | 0.0040187 | 0.0098508 | 0.012662 | 0.017146 | 0.019816
DS | 0.0022356 | 0.0042066 | 0.0048676 | 0.0064017 | 0.0073891
BSS DS | 0.0021857 | 0.0041693 | 0.004772 | 0.0058657 | 0.0068018
BSS VO | 0.0038068 | 0.00942 | 0.012688 | 0.017109 | 0.020361
Half DS | 0.0021628 | 0.0041708 | 0.0048694 | 0.0057324 | 0.0067636
Halfs VO | 0.0037825 | 0.0092183 | 0.011841 | 0.015802 | 0.018899
Chart: 2 BSS case, 13 STAs in BSS, 8 ULL flows
| mean | 90 | 95 | 98 | 99
VO | 0.0045467 | 0.011278 | 0.014577 | 0.019471 | 0.022838
DS | 0.0022049 | 0.0042577 | 0.0049712 | 0.0061653 | 0.0070266
BSS DS | 0.0022276 | 0.0043886 | 0.0050601 | 0.0064872 | 0.0075305
BSS VO | 0.0040379 | 0.009631 | 0.013158 | 0.017034 | 0.020298
Half DS | 0.0021765 | 0.0041724 | 0.0049344 | 0.0063671 | 0.0078178
Halfs VO | 0.0042341 | 0.010125 | 0.013549 | 0.017355 | 0.020813
Chart: 2 BSS case, 16 STAs in BSS, 8 ULL flows
| mean | 90 | 95 | 98 | 99
VO | 0.0047933 | 0.011752 | 0.015977 | 0.021025 | 0.024816
DS | 0.0022076 | 0.0043184 | 0.0051239 | 0.0063911 | 0.0072899
BSS DS | 0.0022466 | 0.0043784 | 0.0051812 | 0.0060752 | 0.0072039
BSS VO | 0.0041658 | 0.010557 | 0.014063 | 0.019169 | 0.022277
Half DS | 0.002189 | 0.0042818 | 0.0051841 | 0.0068189 | 0.0082426
Halfs VO | 0.0041839 | 0.010303 | 0.013235 | 0.017081 | 0.019663

## Slide 9: 4 BSS case , LL packet size 160bytes
Chart: 4 BSS case, 5 STAs in BSS, 8 ULL flows
| mean | 90 | 95 | 98 | 99
VO | 0.0037378 | 0.0089397 | 0.012215 | 0.016514 | 0.019281
DS | 0.0024208 | 0.0047329 | 0.0060946 | 0.0083567 | 0.010527
BSS DS | 0.0022741 | 0.0044894 | 0.0055051 | 0.0072917 | 0.0085124
BSS VO | 0.0036584 | 0.0087768 | 0.011898 | 0.016031 | 0.019016
Half DS | 0.0023358 | 0.0045789 | 0.0058928 | 0.0078005 | 0.0094901
Halfs VO | 0.0033942 | 0.0080891 | 0.010873 | 0.014787 | 0.017414
Chart: 4 BSS case, 9 STAs in BSS, 12 ULL flows
| mean | 90 | 95 | 98 | 99
VO | 0.004618 | 0.011404 | 0.014828 | 0.019401 | 0.022852
DS | 0.002632 | 0.0055039 | 0.0070464 | 0.0093039 | 0.011348
BSS DS | 0.002514 | 0.0052168 | 0.0065373 | 0.0082171 | 0.0096282
BSS VO | 0.0044753 | 0.01109 | 0.014782 | 0.019932 | 0.023389
Half DS | 0.0025462 | 0.005152 | 0.0068554 | 0.0094409 | 0.011206
Halfs VO | 0.0045683 | 0.010985 | 0.01446 | 0.019752 | 0.02297
Chart: 4 BSS case, 8 STAs in BSS, 8 ULL flows
| mean | 90 | 95 | 98 | 99
VO | 0.0041162 | 0.0098462 | 0.013213 | 0.018038 | 0.022401
DS | 0.0025542 | 0.0050293 | 0.0064688 | 0.0089624 | 0.011112
BSS DS | 0.002409 | 0.0046903 | 0.0059387 | 0.0079304 | 0.0093213
BSS VO | 0.0039846 | 0.010078 | 0.013387 | 0.017762 | 0.021365
Half DS | 0.0025208 | 0.0050094 | 0.0066577 | 0.009243 | 0.010818
Halfs VO | 0.0036715 | 0.0087992 | 0.012242 | 0.016564 | 0.019461
Chart: 4 BSS case, 12 STAs in BSS, 12 ULL flows
| mean | 90 | 95 | 98 | 99
VO | 0.004962 | 0.012184 | 0.016007 | 0.021361 | 0.02611
DS | 0.0027006 | 0.0055246 | 0.0071018 | 0.0096506 | 0.011657
BSS DS | 0.0026546 | 0.005623 | 0.0073885 | 0.0094386 | 0.011303
BSS VO | 0.0047937 | 0.011969 | 0.016377 | 0.021791 | 0.025822
Half DS | 0.0027066 | 0.005651 | 0.0073584 | 0.0095351 | 0.011534
Halfs VO | 0.0047331 | 0.011758 | 0.015588 | 0.020433 | 0.024383
Chart: 4 BSS case, 13 STAs in BSS, 16 ULL flows
| mean | 90 | 95 | 98 | 99
VO | 0.0050732 | 0.012287 | 0.01631 | 0.02165 | 0.026135
DS | 0.0028472 | 0.0061299 | 0.0080833 | 0.01024 | 0.012376
BSS DS | 0.0028033 | 0.0060402 | 0.007979 | 0.010718 | 0.012697
BSS VO | 0.0051969 | 0.012826 | 0.016915 | 0.022348 | 0.025466
Half DS | 0.0028603 | 0.0063412 | 0.0082093 | 0.011135 | 0.013372
Halfs VO | 0.0052018 | 0.012876 | 0.017175 | 0.022632 | 0.026581
Chart: 4 BSS case, 16 STAs in BSS, 16 ULL flows
| mean | 90 | 95 | 98 | 99
VO | 0.0051569 | 0.012749 | 0.016999 | 0.02216 | 0.027012
DS | 0.0028706 | 0.0061538 | 0.0081113 | 0.010612 | 0.012603
BSS DS | 0.0028561 | 0.006205 | 0.0082216 | 0.010674 | 0.013063
BSS VO | 0.0054591 | 0.013387 | 0.018353 | 0.024122 | 0.028709
Half DS | 0.0028834 | 0.006508 | 0.0086981 | 0.011602 | 0.01404
Halfs VO | 0.005322 | 0.012861 | 0.017588 | 0.024083 | 0.028586
VO – all ULL use legacy EDCA Half VO – half of ULL in a BSS use VO BSS VO – half of BSSes use VO
DS – all ULL use DS Half DS – half of ULL in a BSS use DS BSS DS – half of BSSes use DS

## Slide 10: Observations
In a scenario with lightweight traffic
  160 bytes every ~16ms there is no degradation of LL traffic stream serviced using legacy EDCA in presence of traffic streams utilizing HiP EDCA

## Slide 11: 1 BSS case, various LL packet size
VO – all ULL use legacy EDCA Half VO – half of ULL use VO
DS – all ULL use DS Half DS – half of ULL use DS
Chart: 1 BSS case, 5 STAs in BSS, 2 ULL flows
| mean | 90 | 95 | 98 | 99
VO | 0.0029785 | 0.0049872 | 0.006497 | 0.0089796 | 0.010988
DS | 0.0027887 | 0.0045981 | 0.0051036 | 0.0057308 | 0.0064249
Half DS | 0.0026595 | 0.0044082 | 0.0048359 | 0.0052563 | 0.0055443
Halfs VO | 0.0030502 | 0.005114 | 0.0067717 | 0.0090928 | 0.010908
Chart: 1 BSS case, 16 STAs in BSS, 4 ULL flows
| mean | 90 | 95 | 98 | 99
VO | 0.004605 | 0.010813 | 0.013724 | 0.018706 | 0.021712
DS | 0.0030152 | 0.0052711 | 0.0060414 | 0.0070647 | 0.0078821
Half DS | 0.0028057 | 0.0046982 | 0.005408 | 0.0065114 | 0.0072492
Halfs VO | 0.0045264 | 0.009969 | 0.013124 | 0.0177 | 0.021606
Chart: 1 BSS case, 5 STAs in BSS, 2 ULL flows
| mean | 90 | 95 | 98 | 99
VO | 0.0014492 | 0.0030258 | 0.0037097 | 0.004754 | 0.0056278
DS | 0.0013524 | 0.0027986 | 0.0033218 | 0.003819 | 0.0041378
Half DS | 0.0012764 | 0.0026577 | 0.0031795 | 0.0037417 | 0.0041917
Halfs VO | 0.0014262 | 0.0028062 | 0.0035323 | 0.0046244 | 0.0057371
Chart: 1 BSS case, 16 STAs in BSS, 4 ULL flows
| mean | 90 | 95 | 98 | 99
VO | 0.0028587 | 0.0065317 | 0.0091181 | 0.012569 | 0.016381
DS | 0.0018057 | 0.0036723 | 0.0042963 | 0.004857 | 0.005284
Half DS | 0.0017717 | 0.0036424 | 0.0042521 | 0.0048764 | 0.0053774
Halfs VO | 0.0026383 | 0.0061534 | 0.0081324 | 0.010376 | 0.011921
Chart: 1 BSS case, 5 STAs in BSS, 2 ULL flows
| mean | 90 | 95 | 98 | 99
VO | 0.0037888 | 0.0062467 | 0.0078167 | 0.0094356 | 0.010841
DS | 0.0035853 | 0.0057607 | 0.0064836 | 0.0072266 | 0.0079252
Half DS | 0.0034659 | 0.0053977 | 0.0062191 | 0.0073783 | 0.0081582
Halfs VO | 0.0037787 | 0.0061214 | 0.0076412 | 0.009681 | 0.010952
Chart: 1 BSS case, 16 STAs in BSS, 4 ULL flows
| mean | 90 | 95 | 98 | 99
VO | 0.0062519 | 0.014137 | 0.01798 | 0.02332 | 0.025652
DS | 0.0043349 | 0.0076023 | 0.0088248 | 0.010472 | 0.011755
Half DS | 0.0038744 | 0.0064208 | 0.0076921 | 0.0097733 | 0.011016
Halfs VO | 0.0063102 | 0.01392 | 0.017495 | 0.023326 | 0.025445
LL size = 1600 LL size = 16000 LL size = 32000

## Slide 12: 2 BSS case, LL packet size 16000 bytes
VO – all ULL use legacy EDCA Half VO – half of ULL in a BSS use VO BSS VO – half of BSSes use VO
DS – all ULL use DS Half DS – half of ULL in a BSS use DS BSS DS – half of BSSes use DS
Chart: 2 BSS case, 5 STAs in BSS, 4 ULL flows
| mean | 90 | 95 | 98 | 99
VO | 0.0034555 | 0.0082769 | 0.010802 | 0.014496 | 0.016824
DS | 0.0022507 | 0.0041974 | 0.0047469 | 0.0056084 | 0.0066236
BSS DS | 0.0021787 | 0.0041245 | 0.0046924 | 0.0053393 | 0.0060824
BSS VO | 0.0030444 | 0.0066247 | 0.0093546 | 0.012837 | 0.014937
Half DS | 0.0021498 | 0.004111 | 0.0047142 | 0.005449 | 0.0066966
Halfs VO | 0.0031421 | 0.0071345 | 0.0095475 | 0.013166 | 0.016494
Chart: 2 BSS case, 16 STAs in BSS, 8 ULL flows
| mean | 90 | 95 | 98 | 99
VO | 0.0050788 | 0.01195 | 0.016029 | 0.02145 | 0.026019
DS | 0.0023138 | 0.0045168 | 0.0051854 | 0.0061521 | 0.0072722
BSS DS | 0.0023729 | 0.004545 | 0.0053463 | 0.0066806 | 0.0076347
BSS VO | 0.0045679 | 0.011092 | 0.014381 | 0.019814 | 0.023925
Half DS | 0.0022405 | 0.0043797 | 0.0051268 | 0.0062829 | 0.0079416
Halfs VO | 0.0044372 | 0.010738 | 0.013799 | 0.017616 | 0.021301
Chart: 2 BSS case, 5 STAs in BSS, 4 ULL flows
| mean | 90 | 95 | 98 | 99
VO | 0.0047141 | 0.010571 | 0.014061 | 0.01952 | 0.023686
DS | 0.0032066 | 0.0054741 | 0.0065465 | 0.0083979 | 0.010796
BSS DS | 0.0032011 | 0.0055226 | 0.0066587 | 0.0084156 | 0.010751
BSS VO | 0.004366 | 0.0095069 | 0.012708 | 0.018134 | 0.021296
Half DS | 0.0030991 | 0.0052596 | 0.0060995 | 0.0075478 | 0.0087836
Halfs VO | 0.0042856 | 0.0091878 | 0.012769 | 0.017179 | 0.020834
Chart: 2 BSS case, 16 STAs in BSS, 8 ULL flows
| mean | 90 | 95 | 98 | 99
VO | 0.0098242 | 0.022708 | 0.030499 | 0.044298 | 0.058925
DS | 0.0038369 | 0.0073607 | 0.0090849 | 0.011475 | 0.013613
BSS DS | 0.0038144 | 0.007508 | 0.0097113 | 0.012924 | 0.014741
BSS VO | 0.0073794 | 0.017384 | 0.023087 | 0.032528 | 0.038388
Half DS | 0.0036955 | 0.0072146 | 0.0092764 | 0.012083 | 0.014865
Halfs VO | 0.0079316 | 0.01821 | 0.024772 | 0.033576 | 0.040285
Chart: 2 BSS case, 5 STAs in BSS, 4 ULL flows
| mean | 90 | 95 | 98 | 99
VO | 0.0074984 | 0.015708 | 0.022057 | 0.033409 | 0.046934
DS | 0.0047979 | 0.0083808 | 0.010364 | 0.013962 | 0.017514
BSS DS | 0.0050023 | 0.0080658 | 0.010056 | 0.015606 | 0.024284
BSS VO | 0.0065107 | 0.013222 | 0.017401 | 0.026161 | 0.037618
Half DS | 0.0047601 | 0.0079324 | 0.0097196 | 0.014882 | 0.022227
Halfs VO | 0.006296 | 0.012905 | 0.017388 | 0.026241 | 0.034799
Chart: 2 BSS case, 16 STAs in BSS, 8 ULL flows
| mean | 90 | 95 | 98 | 99
VO | 1.3472 | 4.4146 | 4.7774 | 5.0461 | 5.1208
DS | 0.013492 | 0.029147 | 0.037918 | 0.049113 | 0.057265
BSS DS | 0.012423 | 0.026907 | 0.0357 | 0.05041 | 0.061672
BSS VO | 0.27334 | 0.65321 | 0.71765 | 0.75483 | 0.77018
Half DS | 0.013001 | 0.028218 | 0.037848 | 0.055104 | 0.069353
Halfs VO | 0.060364 | 0.1472 | 0.18349 | 0.21904 | 0.24568
LL size = 1600 LL size = 16000 LL size = 32000

## Slide 13: 4 BSS case
VO – all ULL use legacy EDCA Half VO – half of ULL in a BSS use VO BSS VO – half of BSSes use VO
DS – all ULL use DS Half DS – half of ULL in a BSS use DS BSS DS – half of BSSes use DS
Chart: 4 BSS case, 5 STAs in BSS, 8 ULL flows
| mean | 90 | 95 | 98 | 99
VO | 0.0061753 | 0.014697 | 0.019533 | 0.026175 | 0.031779
DS | 0.0028897 | 0.0056507 | 0.0074246 | 0.0096425 | 0.01181
BSS DS | 0.0028661 | 0.0056483 | 0.0073986 | 0.009807 | 0.011795
BSS VO | 0.0053826 | 0.013044 | 0.016767 | 0.02278 | 0.027287
Half DS | 0.0028108 | 0.0055483 | 0.0071927 | 0.0097793 | 0.011588
Halfs VO | 0.0050702 | 0.012002 | 0.016302 | 0.021476 | 0.025967
Chart: 4 BSS case, 16 STAs in BSS, 16 ULL flows
| mean | 90 | 95 | 98 | 99
VO | 0.0084818 | 0.019974 | 0.027249 | 0.035741 | 0.042969
DS | 0.0033335 | 0.0073302 | 0.0093215 | 0.011939 | 0.013765
BSS DS | 0.003375 | 0.0074306 | 0.0096712 | 0.012133 | 0.014156
BSS VO | 0.0075699 | 0.018161 | 0.023879 | 0.031063 | 0.03754
Half DS | 0.0034261 | 0.0077116 | 0.0099442 | 0.012997 | 0.015054
Halfs VO | 0.0073121 | 0.0172 | 0.023164 | 0.030027 | 0.034763
Chart: 4 BSS case, 5 STAs in BSS, 8 ULL flows
| mean | 90 | 95 | 98 | 99
VO | 0.11617 | 0.33755 | 0.53014 | 0.8414 | 0.97957
DS | 0.0067182 | 0.015163 | 0.019731 | 0.027106 | 0.032478
BSS DS | 0.0081518 | 0.018343 | 0.025117 | 0.035489 | 0.04385
BSS VO | 0.016551 | 0.041074 | 0.055799 | 0.07443 | 0.088723
Half DS | 0.008288 | 0.017952 | 0.026267 | 0.041264 | 0.054642
Halfs VO | 0.016139 | 0.037064 | 0.054862 | 0.083073 | 0.11395
Chart: 4 BSS case, 12 STAs in BSS, 12 ULL flows
| mean | 90 | 95 | 98 | 99
VO | 2.3535 | 8.7672 | 10.9574 | 12.9611 | 15.0709
DS | 0.24534 | 0.79499 | 0.98225 | 1.2688 | 1.3565
BSS DS | 0.050623 | 0.12047 | 0.17377 | 0.27763 | 0.3536
BSS VO | 0.89946 | 2.6037 | 3.7794 | 4.4412 | 4.4846
Half DS | 0.022311 | 0.050628 | 0.070846 | 0.10329 | 0.13308
Halfs VO | 0.12056 | 0.30306 | 0.4014 | 0.55091 | 0.78814
LL size = 1600 LL size = 16000

## Slide 14: Observations
In a scenario with lightweight LL traffic
  1600Kb every 16ms = 768Kbps there is no degradation of LL traffic stream serviced using legacy EDCA in presence of traffic streams utilizing HiP EDCA
In scenarios with moderately (7Mbps+ per LL stream) to high load LL (15Mbps+) traffic
  In isolated BSS we observe no degradation of LL traffic stream serviced using legacy EDCA mechanism
  In multi-BSS case, depending on a number of LL streams, HiP EDCA improve performance of legacy streams
  When system is near capacity, HiP EDCA provide service to LL streams while EDCA fails to do so

## Slide 15: Conclusion
We observe no negative impact on LL stream using legacy EDCA mechanism in presence of devices using HiP EDCA mechanism
HiP EDCA always provide 3-4x tail latency improvements across all analyzed scenarios
  The gain is more pronounced when system is near capacity
  The presence of HiP EDCA may improve latency for LL streams using legacy EDCA by providing additional separation between traffic streams