## Slide 1: Re-thinking latency: the missing pieces
Date: 2022-xx-xx
Authors:

## Slide 2: Problem space for UHR
The UHR SG objectives is :
The Study Group will investigate technology which may improve reliability of WLAN connectivity, reduce latencies, increase manageability, increase throughput including at different SNR levels and reduce device level power consumption.
There are at least two aspects of transmission over wireless medium that directly contribute to the latency KPI
  Channel occupancy
    An ongoing transmission (long PPDU) or series of frame exchanges (within TXOP) prevent a STA from even attempting to access the medium
    The longer the medium occupancy period, the larger the delay is
  Channel access
    To transmit, a STA or an AP shall obtain a TXOP through contention with other WiFi devices
    A failed contention (in a combination with TXOP duration), especially multiple consecutive failures, lead to latency increase
A combination of the two lead to large delay values even for traffic streams with AC_VO priority

## Slide 3: Latency problem
EDCA channel access
  In general OK for LL traffic as it provide traffic prioritization
  Cover the need for most LL apps that can tolerate waiting for completion of an ongoing TXOP or even few TXOPs
  Generally, work for all scenarios and traffics: UL, DL , in presence of OBSS, etc.
  In general cover latency needs for as low as 10th of milliseconds (10-20-30ms or so)
  Bottleneck :
    EDCA does not guarantee a transmit opportunity. It is by the nature a source of latency spikes / long tail latency
    Even higher priority AC may have difficulties obtaining a medium at a right time
    Harder to achieve sub 10th ms latency
    For latency needs of 10th of milliseconds, just need to cut the tail
Prolonged medium usage.
  Is a barrier for latency in the order of single digit milliseconds, i.e. latency needs may not tolerate waiting for completion of ongoing TXOP or previously missed TX opportunity
  Legacy solution for that is to limit TXOP to a small value including for both BSS and OBSS
    But in any case, that force to fallback to wining the medium through EDCA
    Limiting TXOP lead to inefficient use of airtime and TXOP level preemption help to reduce the impact on throughput
    STAs may not be able to flush TX buffers quickly, so they should be active for a longer time and contribute to increased collision rate
  We can utilize already discussed TXOP level preemption for that, but
    With OBSS, if we want TXOP level preemption to be used in a way to allow longer TXOP while allowing quicker access to the medium for LL streams, the only way for that to work is to allow preemption of every DL and UL TXOP by every STA including OBSS.

## Slide 4: TXOP Preemption for channel occupancy
Preemption* seems to be a perfect solution for the prolonged medium occupancy problem
  We already converg(ed)ing on many aspects of it:
    Use origin of a latency sensitive traffic or “LL-stream” and TXOP ownership for classification
    TXOP fragmentation into a sequence of short xIFS separated frame exchanges
    Indication of preemption enablement, i.e. “this can be preempted”
    Indication of preemption indication, i.e. “I need preemption”
  Seems to be a good alternative vs. setting aggressive TXOP limits
    Let to keep overall system throughput degradation at acceptable 5-15% level
    Provide sufficient level of control over TXOP for TXOP owner
Sounds good, but.. what about aspects other than “long PPDU”?
  What about OBSS or P2P? Should we be able to preempt those and how?
  What if there is no long PPDU or TXOP? No “prolonged medium occupancy” – no preemption
  What if TXOP or PPDU are not preemption enabled? i.e. legacy TXOP?
  What if only DL TXOP can be preempted or if UL TXOP cannot be preempted by other STA?
What else is missing?
*without losing generality we can say that preemption is a mechanism to access the medium by interrupting a rightful transmission sequence by an EDCAF that did not obtain the TXOP

## Slide 5: EDCA preemption - “before the opportunity is offered to others”
Too short TXOP or too short TX sequence or non-preemptable TXOP or OBSS TXOP or TX sequence require a LL stream owner to obtain medium using EDCA mechanism
  Which does not provide sufficient traffic separation and does not guarantee acquisition of TXOP even for high access categories
  May be hard to achieve 1ms-like latencies without substantial system performance degradation
We should consider a mechanism(s) that address the channel access of the latency KPI as well.
  A TXOP preemption provide to the LL-stream originator almost guaranteed opportunity for transmission as it have a chance to transmit when access to the medium is already obtained by someone
  When LL stream owner is required to compete for the medium it should have guaranteed opportunity to win the medium during first available contention window

## Slide 6: Another missing link – low latency stream
What is exactly meant under “to reduce latency” ?
  Below some target X ms (i.e. <10ms? <5ms? <1ms? ); Should 10ms stream use preemption?
  Decrease number of latency spikes? (i.e. improve 95-99%)
  Reduce latency for certain traffic? For “low latency applications”? A generic “latencies”?
Who need “low latency” and what is “low latency” or “ultra-low latency” ?
  any traffic in AC_VO ? or may be some with new UP/TID/AC? i.e. static LL stream definition
  buffered frames of a stream for which certain “delivery delay” timer is expiring? i.e. dynamic LL definition
    this potentially may let any packet to qualify as latency sensitive
  is it a predictable stream (i.e. CBR-like) or unpredictable (event-based or CBR with large frame arrival jitter)?
  Essentially the question is - WHAT IS LL STREAM. The IEEE 802.11 has no such definition. We operate with AC and TID/UP
What are the target applications?
  Voice: goes into AC_VO. Latency bounds – 30ms. Is it so critical ?
  Video: goes into AC_VI. Latency bounds – 200ms. Some packets more important that others? Can it be critical?
  XR: Latency (and jitter) numbers directly impact user experience. Defined by user input and video stream (FPS). Various reports say <2-5-8<10<16<20<40ms.
  A TCP/ AC_BE traffic: a mouse click on a web link / web page load time.
    It is best effort, so nothing to expect , BUT! “my internet is slow – I just clicked and nothing happened, WiFi is bad” – user experience define importance of the traffic
We need to be specific on who is going to use preemption and what is the scale of the solution?

## Slide 7: Conclusion
TXOP level preemption is a necessary step towards achieving latencies below 10 ms
  A possibility to enter someone's TXOP is one of the missing features in WiFi.
  Must be enabled for all/almost all TXOPs to work properly
Contention preemption / enhancements to EDCA for LL traffic is needed in UHR
  EDCA mechanism is one of the main reasons of latency spikes for all traffic types as it does not guarantee channel access.
  A LL stream with stringent requirements would benefit from prioritized, guaranteed channel access opportunity even before regular EDCA start
  Enhancements to EDCA would satisfy latency bounds in the 10th of ms
A definition/description of “LL stream” would be necessary to
  Help to narrow down the scope of “Preemption” operations
  Develop set of rules to limit possible abuse and to keep fairness to other streams

## Slide 8: Backup

## Slide 9: Preemption: definition
from Oxford Languages Dictionary
  1. the purchase of goods or shares by one person or party before the opportunity is offered to others.
  2. US: the interruption or replacement of a scheduled radio or television program.
Definitions from Oxford Languages · Learn more