## Slide 1: Considerations on Power Consumption
Date: 2024-03-11
Authors:
Name | Affiliation | Address | Phone | Email
Sang G. Kim | LG Electronics | 10680 Treena St 550, San Diego CA 92131 |  | sanggook.kim@lge.com
Eunsung Park |  | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | esung.park@lge.com
Insun Jang |  |  |  | insun.jang@lge.com
Insik Jung |  |  |  | insik0618.jung@lge.com
Dongju Cha |  |  |  | dongju.cha@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com

## Slide 2: Introduction
Integrated mmWave operation is being considered in UHR to improve [1-8]
  Peak data rate
  Latency
  Average throughput
Due to inherent propagation characteristics, the operation in mmWave requires more power consumption
In sub 7 GHz operation, the discussion on client-side power saving has been active [9-10]
Recently, low power listening mode (LPLM) in sub 7 GHz was proposed based on the measurements on power consumption [11]
In this contribution, we discuss the need of power saving feature in IMMW and consider one similar to LPLM

## Slide 3: Power Saving Operation in mmWave
A radio can be in one of two power states:
  Awake: the radio is constantly powered and able to receive and transmit
  Doze: the radio is not able to receive and transmit and consumes low power
In Power Save (PS) mode, STA can transition between awake and doze states
A STA can be one of two Power Management modes:
  Active mode: the STA is awake all the time
  Power Save mode: the STA is mostly in doze power state, but can also be awake to transmit and receive from time to time
In EDMG, dynamic spatial multiplexing (SM) power save is also defined in addition to power save mode:
  EDMG STA enables its multiple receive chains only when the frame it receives indicates that the following transmission required the activation of multiple receive chains. The EDMG STA switches back immediately when the frame exchange sequence ends

## Slide 4: Low Power Listening Mode (LPLM)
In [11], it was shown through measurements of various application usages that power consumption in listening mode is considerable mainly due to
  PLL for supporting high order modulation, e.g., 4K QAM and ADC for supporting wider bandwidth, e.g., 320 MHz
Power consumption in listening mode in mmWave band will be further aggravated:
  Stringent Rx EVM requirements for higher order modulation, e.g., 256 QAM, prone to phase noise, will increase the power consumption of PLL compared to sub 7 GHz operation
  Larger bandwidth considered in IMMW discussion, e.g., 640 MHz or 1280 MHz will also increase ADC power consumption
Thus, power consumption in IMMW operation should be placed as one of the most important design considerations

## Slide 5: Extension of LPLM to mmWave
To further reduce the power consumption in mmWave band operation, we need to consider listening mode with similar consideration in sub 7 GHz discussion. For example, during the listening mode
  Reduced bandwidth reception, e.g., 80 MHz
  Low order modulation, e.g., BPSK
  1 spatial stream
  Quasi-omni or sector level reception (since power consumption due to BF can be significant, we consider quasi-omni or sector level reception, not beam refinement and tracking in LPLM)
  Beam refinement may be executed before data PPDU reception
During initial frame exchange, more information for the reception of upcoming PPDU can be provided:
  MCS
  Number of spatial streams
  Bandwidth
  Configurable padding [9-10]
  Etc.

## Slide 6: Conclusion
Power consumption in IMMW operation should be considered from the beginning due to:
  Susceptible to phase noise
  Higher bandwidth considered
In this contribution, we emphasize that power consumption consideration in IMMW operation is important and introduces low power listening mode (LPLM) similar to the one being considered in sub 7 GHz by also considering antenna configuration

## Slide 7: References
[1] 11-24-0066-00-immw-discussion-on-target-objectives-for-immw
[2] 11-23-1819-01-immw-integrated-mmwave-design-considerations
[3] 11-23-1878-01-immw-high-level-design-considerations-of-immw
[4] 11-23-1905-00-immw-high-level-thoughts-on-immw
[5] 11-23-1968-00-immw-discussion-on-general-direction-of-integrated-mmwave
[6] 11-23-2004-00-immw-technical-scope-proposal
[7] 11-22-0046-01-0wng-next-generation-after-802-11be
[8] 11-22-0685-00-0wng-discussion-on-next-generation-wi-fi
[9] 11-23-2003-01-00bn-client-power-save
[10] 11-23-1875-01-00bn-power-save-proposal-for-non-ap-mobile-ap
[11] 11-22-1414-01-0uhr-low-power-listening-mode