## Slide 1: High Level Perspective on DRU-Follow Up
Date: 2024-03-08
Authors:
Name | Affiliations | Address | Phone | Email
Shengquan Hu | Mediatek | 2840 Junction Ave. San Jose, CA, 95134 |  | shengquan.hu@mediatek.com
Jianhan Liu |  |  |  | jianhan.liu@mediatek.com
Thomas Pare |  |  |  | 

## Slide 2: Introduction
In last January IEEE meeting, motion was passed to support Distributed tone RU (DRU) for a UHR TB PPDU transmission
We have shared our thoughts on DRU from high level perspectives [1]:
  dRU can boost transmission power up to 11dB, significantly enhance the spectrum efficiency of 6GHz LPI and improve the coverage range
  Support of distribution bandwidth 20/40/80MHz would be a good choices considering the harvest of maximum power boost gains, use cases, flexibility and complexity
  DRU should keep the same set of RU sizes as RRU, and each distribution BW may support different DRU sets such as 26/52/106-tone DRU for BW20, 26/52/106/242-tone DRU for BW40, 52/106/242/484-tone DRU for BW80
  Hybrid mode with DRU or RRU in each 80MHz subblock can be operated for wider BW160/320
  DRU with distribution BW20/40 should be allowed either in punctured 80MHz subblock or 20/40MHz subblock in BW80/160/320
In this contribution, we would like to follow up the previous discussions and seek for alignments

## Slide 3: Reference
Shengquan Hu, Mediatek Inc.
Slide 3
  [1]. 11-23-2020-01-00bn-high-level-perspective-on-distributed-tone-ru-for-11bn

## Slide 4: Straw Poll #1
Shengquan Hu, Mediatek Inc.
Slide 4
Do you agree to include the following text to the 11bn SFD?
  Allowed distribution BWs of an DRU in 11bn are 20MHz, 40MHz, 80MHz

## Slide 5: Straw Poll #2
Shengquan Hu, Mediatek Inc.
Slide 5
Do you agree to include the following text to the 11bn SFD?
  the allowed DRU sizes in 11bn are 26-tone, 52-tone, and 106-tone in distribution BW 20MHz

## Slide 6: Straw Poll #3
Shengquan Hu, Mediatek Inc.
Slide 6
Do you agree to include the following text to the 11bn SFD?
  the allowed DRU sizes in 11bn are 26-tone, 52-tone, 106-tone and 242-tone in distribution BW 40MHz

## Slide 7: Straw Poll #4
Shengquan Hu, Mediatek Inc.
Slide 7
Do you agree to include the following text to the 11bn SFD?
  the allowed DRU sizes in 11bn are 52-tone, 106-tone, 242-tone and 484-tone in distribution BW 80MHz

## Slide 8: Straw Poll #5
Shengquan Hu, Mediatek Inc.
Slide 8
Do you agree to include the following text to the 11bn SFD?
  11bn supports the hybrid mode with DRUs and RRUs (regular RU) in an OFDMA transmissions if UHR TB PPDU bandwidth is larger than 80MHz
    No mixing DRU and RRU in one 80MHz frequency subblock
    Minimum size of RRU in hybrid mode in 160MHz and 320MHz is 242

## Slide 9: Straw Poll #6
Shengquan Hu, Mediatek Inc.
Slide 9
Do you agree to include the following text to the 11bn SFD?
  in a punctured 80MHz frequency subblock, the only allowed distribution BWs are 20MHz and 40MHz in 11bn