## Slide 1: Non-Primary Channel Access (NPCA) – Follow Up
Date: 2024-05-10
Authors:

## Slide 2: NPCA primary channel
In 11-24/2005, to manage the complexity of the NPCA operation, we proposed to limit the number of secondary channels on which the non-primary channel access can take place while the primary channel is busy to one
Define one NPCA primary channel
  One of the secondary channels of the BSS on which channel access is performed while the primary channel is busy
  AP announces the location of the NPCA primary channel
  Any available secondary channels of the BSS can be used for the NPCA operation
  Accessing the secondary channels of NPCA follows the same PIFS rules defined in the baseline
BSS Primary channel (P1)
NPCA primary channel (P2)
Secondary channels of BSS
Secondary channels of NPCA
Potential NPCA operation
frequency
time

## Slide 3: Switching to NPCA primary channel and operating on NPCA primary/secondary channels
BSS Primary(P1)
NPCA Primary(P2)
Secondary for P1
Secondary for P2
NAV set by RTS
RTS
or MU-RTS
CTS
Data
BA
aRxPHYStartDelay
(20 usec)
Switch delay
ICF
IR
Data
BA
NAV set by CTS
(AIFS+RBO)
Switch to NPCA primary
OBSS frames
My BSS frames
Switch back to BSS primary before NAV expires
BSS Primary(P1)
NPCA Primary(P2)
Data
BA
HE PPDU: HE-SIG-A EHT/UHR PPDU: U-SIG
Switch delay
ICF
IR
Data
BA
(AIFS+RBO)
Switch to NPCA primary
OBSS frames
My BSS frames
Switch back to BSS primary before NAV expires or before the end of PPDU
TXOP field
TXOP field
128 usec granularity if TXOP_Duration >= 512 usec
Switching to the NPCA primary channel after a Control frame exchange of an OBSS is detected
Switching to the NPCA primary channel after detecting an OBSS HE/EHT/UHR PPDU (i.e., after detecting inter-BSS PPDU)
ICF: initial control frame
IR: immediate response
Secondary for P2
Secondary for P1
Secondary for P2
Secondary for P2
PIFS
PIFS

## Slide 4: Switching to NPCA primary channel
Switching after a control frame exchange (e.g., (MU-)RTS/CTS)
  Simple but may miss opportunities when TXOP doesn’t start with a control frame exchange
Switching based on the PHY header information of a PPDU
  This can cover the frame exchanges that don’t start with a control frame exchange (e.g., (MU-)RTS/CTS) but needs to define rules for different types of PPDU as follows:
  HE PPDU:
    HE-SIG-A field carries: BSS Color, Bandwidth, TXOP fields
    BSS Color used to detect inter-BSS PPDU
    Bandwidth field: the bandwidth of the PPDU
    TXOP field used to set the duration of the duration of the NPCA operation on the NPCA primary/secondary channels (TXOP duration value is 128 usec granularity for TXOP Duration >=512 usec)
  EHT/UHR PPDU:
    U-SIG field carries: BSS Color, Bandwidth, TXOP fields
    Usage is same as the HE PPDU case
  VHT PPDU:
    VHT-SIG-A field carries: BW, Group ID, Partial AID fields
    Group ID and Partial AID fields can be used to detect inter-BSS PPDU (i.e., OBSS PPDU)
    BW field: the bandwidth of the PPDU
    LENGTH field of L-SIG field may be used to set the duration of the NPCA operation on the NPCA primary/secondary channels but doesn’t provide TXOP information
  Non-HT or HT PPDU:
    Doesn’t have the information in the PHY preamble to detect inter-BSS PPDU and the duration, thus only way is to decode the MAC header, but this is a problem since the timing of when the MAC header information is available is implementation dependent and has to check FCS at the end of the PPDU.
  When switching is based on the PHY preamble of an OBSS PPDU, we suggest to include HE/EHT/UHR PPDUs that contain necessary information (OBSS, BW, TXOP) for the NPCA operation

## Slide 5: EDCA parameters on the NPCA primary channel
For simplicity, same EDCA parameters (CWmin/max/TXOP limit…) defined in (MU) EDCA Parameter Set are applied on the BSS primary channel and the NPCA primary channel

## Slide 6: Summary
Define one NPCA primary channel
  One of the secondary channels of the BSS on which channel access is performed while the primary channel is busy
The event that triggers switching to the NPCA primary channel
  An OBSS control frame exchange (e.g., (MU-)RTS/CTS)
  OBSS HE/EHT/UHR PPDU
Upon switching to the NPCA primary channel
  Same EDCA parameters of the BSS primary channel apply to the NPCA primary channel

## Slide 7: SP1
Do you support the following in the NPCA operation?
In 802.11bn, the event that triggers switching to the NPCA primary channel shall be
  OBSS Control frame exchange (e.g., (MU-)RTS/CTS) or
  OBSS HE/EHT/UHR PPDU

## Slide 8: SP2
Do you support the following in the NPCA operation?
In 802.11bn, the NPCA operation shall use the same EDCA parameters ((MU) EDCA Parameter Set, EPCS EDCA Parameters), on both the BSS primary channel and the NPCA primary channel.