## Slide 1: Secondary Channel Usage Follow Up
Date: 2024-03-06
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Kiseon Ryu Huizhao Wang Hongyuan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Recap
We discussed the secondary channel usage in several presentations:
  The RU index, BW negotiation in secondary channel
  Secondary channel combination by treating the anchor channel as primary channel.
  Secondary channel usage under Multiple BSSID or co-hosted APs.
  Secondary channel usage and Beacon Tx.
  Secondary channel usage and R-TWT.
  Secondary channel usage and NAV operation.

## Slide 3: Time to Switch to Secondary Backoff Channel and Switch back to Primary Channel
The rule about allowing the AP and STAs roughly do the subchannel switch at the same time should be defined, e.g.
  When an AP or a STA associated with the AP detects an OBSS PPDU whose PPDU length is longer than a length threshold announce by the AP in Beacon or the other management frame, the AP or the STA switches to the secondary backoff channel (anchor channel) announced by the AP through Beacon etc. to do the backoff for the frame exchanges by using the secondary channels.
The rule to for STAs/AP to switch back to the primary channel
  At the end of the OBSS PPDU, the AP and STA switch back to the primary channel.
Compared with TXOP-based channel switch, the PPDU-based channel switch is kind of simpler:
  Work well with incremental TXOP protection.
  Guaranteed channel switch at the same time.
  No medium synchronization issue when switch back to primary channel

## Slide 4: Time to Switch to Secondary Backoff Channel and Switch back to Primary Channel
With PPDU-based channel switch, the backoff procedure that uses the basic NAV timer on anchor channel may flush the TXOP information of the primary channel in the basic NAV Timer.
  The AP/STA that switches back to the primary channel may lose the medium synchronization information of the primary channel.
One solution could be that an AP/STA needs to maintain/resume the basic NAV timer of the primary channel after the STA/AP finishes the frame exchanges on anchor channel and switches to the anchor channel for the frame exchanges.
  The resumption operation has the same result as if the AP/STA didn’t do the channel switch.

## Slide 5: Synchronization on Secondary Channel
Medium synchronization on the anchor channel
  If a STA/AP can’t do the CCA on the anchor channel for more than 72us (aMediumSyncThreshold) until finishing the switch to the anchor channel, the STA/AP loses the medium synchronization when switching to the anchor channel. Otherwise, the STA/AP does not lose the medium synchronization when switching to the anchor channel.
    During the transmission/detection of a PPDU that cover the anchor channel, the CCA of the anchor channel is done with the result of medium busy.
    During the time switching from the primary channel to the anchor channel, the STA/AP can’t do the CCA on the anchor channel.

## Slide 6: RU Index Coding
The primary channel is used as the reference for the RU index coding of DL MU PPDU and UL TB PPDU.
When an UHR TB PPDU has BW more than 160MHz, two backoff channels are covered by the UHR TB PPDU.
280MHz UHR TB PPDU
Primary channel
Anchor channel

## Slide 7: RU Index Coding with Secondary Channel Usage
The unique backoff channel is the reference for RU index coding of DL MU PPDU or UHR TB PPDU when both primary channel and anchor channel are covered by the BW of the DL MU PPDU or UHR TB PPDU.
Option 1
  If the BW of the DL MU PPDU or UHR TB PPDU only covers the anchor channel, the RU index is acquired based on the PPDU BW and through treating the anchor channel (non-primary backoff channel) as the primary channel.
  When the primary channel is covered by the PPDU BW, the RU Index will be coded as if no channel switch happens.
Primary channel
Anchor channel
280MHz UHR TB PPDU
160MHz UHR TB PPDU
26-tone RU with PS160 equal to 0, and
RU Allocation equal to 19
26-tone RU with PS160 equal to 1, and
RU Allocation not equal to 19

## Slide 8: RU Index Coding with Secondary Channel Usage
Option2
  the RU index is acquired based on the whole BW of the BSS and the primary channel
Primary channel
Anchor channel
280MHz UHR TB PPDU
160MHz UHR TB PPDU
26-tone RU with PS160 equal to 0, and
RU Allocation equal to 19
26-tone RU with PS160 equal to 1, and
RU Allocation not equal to 19

## Slide 9: Summary
The various aspects related to secondary channel usage are discussed
  Condition to switch to/back primary channel per OBSS PPDU Length.
  The Basic NAV timer resumption with the channel switch per OBSS PPDU Length.
  The RU Index coding clarification.
Compare with the OBSS TXOP based secondary channel usage, the OBSS PPDU based secondary channel usage is simple. If both are allowed, we prefer no to enable them at the same time.