## Slide 1: Control Frame Protection Follow Up
Date: 2024-05-06
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Kiseon Ryu Huizhao Wang Hongyuan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Recap: Control Frame Protection
The following control frame should be protected
  Trigger
  Compressed/Multi-TID BAR
  Multi-STA BA.
The CPTK and CGTK are defined.
This presentation discuss the frame format

## Slide 3: Protected Trigger Frame Format 1---Security Information Before Padding Field
Key ID is carried in Special User Info field or Common Info field.
PN and MIC are carried in Security User Info field.
  The Security User Info field has same length as Special User Info field where the Trigger Dependent User Info field is not used for carrying the PN + MIC.
  Only the Security Info field of the last Security User Info field has reserved bits.
Special User Info
PN
Security User
Info List
Pre-padding
FCS User Info List
4
User Info
……
User Info
Security User Info
Security User Info
……
Security User Info
AID12
0
Trigger Dependent User Info
11
12
39
Pre-Padding FCS User Info field
Bits to carry FCS
FCS Info
MIC
……
Octets:
6
8
MIC
4
Octets:
Pre-Padding User Info
Pre-Padding User Info
Specific AID value, e.g. 2009
AID12
0
Trigger Dependent User Info
11
12
39
Security User Info field
Bits to carry security information, i.e. PN, MIC
Security Info
Specific AID value, e.g. 2006

## Slide 4: Protected Trigger Frame Format 1---Security Information Before Padding Field
Pre-padding FCS is carried in Pre-padding FCS User Info field.
  The Pre-padding FCS User Info field has same length as Special User Info field where the Trigger Dependent User Info field is not used for carrying the FCS.
  Only the FCS Info field of the last Pre-padding FCS User Info User Info field has reserved bits.
Special User Info
PN
Security User
Info List
Pre-padding
FCS User Info List
4
User Info
……
User Info
Security User Info
Security User Info
……
Security User Info
AID12
0
Trigger Dependent User Info
11
12
39
Pre-Padding FCS User Info field
Bits to carry FCS
FCS Info
MIC
……
Octets:
6
8
MIC
4
Octets:
Pre-Padding User Info
Pre-Padding User Info
Specific AID value, e.g. 2009
AID12
0
Trigger Dependent User Info
11
12
39
Security User Info field
Bits to carry security information, i.e. PN, MIC
Security Info
Specific AID value, e.g. 2006

## Slide 5: Protected Trigger Frame Format 2---Security Information in Padding Field
Security Indication, Key Id are carried in Special User Info field or Common Info field.
  Security Indication helps the recipients without control frame protection support to figure out the location of pre-padding FCS.
  The discussion of the Trigger frame addressing to recipients with and without ICF/ICR support will be discussed in the following presentation.
PN and MIC are carried in Padding field after 16-bit all 1s.
It seems option 2 is preferable.
PN
1111111111111111
Sixteen 1s
MIC
6 Octets:
8 Octets:
Pre-Padding FCS
4 octets
Additional Padding
variable

## Slide 6: Protected Compressed/Multi-TID BAR
The Security Indication, Key ID is carried in BAR Control (the current reserved bit of BAR Control) of BAR, BA.
The PN + MIC is before FCS.
  Between PN+MIC and FCS, the padding may be required.
  After PN+MIC. Pre-padding FCS may exist.
PN+MIC
14

## Slide 7: Protected Multi-STA BA (1)
Security Per AID TID Info
Padding Per AID TID List
Padding Per AID TID List
0 or 18
Security Indication, Key Id are carried in BA Control field (the current reserved bits).
PN and MIC are carried in Security Per AID TID Info field.
Per AID TID Info
……
Per AID TID Info
Padding Per AID TID Info
……
Padding Per AID TID Info
Specific AID value, e.g. 2006
2
16
Security Per AID TID Info field
Security Info
Pre-padding FCS Per AID TID Info field

## Slide 8: Protected Multi-STA BA (2)
Security Per AID TID Info
Padding Per AID TID List
Padding Per AID TID List
0 or 18
The Padding Per AID TID Info field is a Per AID TID Info field with specific value in its AID11 field.
Per AID TID Info
……
Per AID TID Info
Padding Per AID TID Info
……
Padding Per AID TID Info
Specific AID value, e.g. 2009
2
32
Padding Per AID TID Info field
Padding Info

## Slide 9: Summary
The control frame protection format is discussed for the protected control frame (Trigger, compressed BAR, Multi-TID BAR, Multi-STA BA):
  The Protection Indication, Key ID are carried in one of the following the current reserved bits of Common Info or Special User Info field, the current reserved bits of BAR Control, the current reserved bits of BA Control.
  The PN + MIC location in various protected control frames.
  The padding (if required by the recipient of the protected control frame) after PN + MIC.

## Slide 10: SP 1
Do you support in 11bn, a STA supports control frame protection announces its padding requirement for the received protected control frame?

## Slide 11: SP 2
Do you support that in protected Trigger frame the following information is carried:
  the Control Frame Protection Indication, Key ID being carried in the current reserved bits of Common Info field or Special User Info field.
  The PN + MIC
  The pre-FCS padding if required

## Slide 12: SP 3
Do you support that in protected Multi-STA Block Ack frame the following information is carried:
  the Control Frame Protection Indication, Key ID being carried in the BA Control field
  The PN + MIC is carried in a Per AID TID Info field with 128 BA Bitmap, special AID value in AID11 field.
  The padding, if exists, is carried in Per AID TID Info field(s) with special AID value in AID11 field.
    The padding is after the Per AID TID Info field carrying PN + MIC

## Slide 13: SP 4
Do you support that in protected Compressed Block Request or Multi-TID Ack Request frame, the following information is carried:
  the Control Frame Protection Indication, Key ID are carried in the BAR Control field
  The PN + MIC is carried right after the BAR Information field.
  The padding, if exists, is carried after PN+MIC.