## Slide 1: Extended 6 GHz channelization
Date: 2024-03-08
Authors:
Name | Affiliations | Address | Phone | Email
Thomas Derham | Broadcom |  |  | thomas.derham@broadcom.com
Ron Porat |  |  |  | 
Chris Szymanski |  |  |  | 

## Slide 2: Overview
UHR PAR defines operation up to 7.250 GHz
  quote:
In current baseline (REVme + 11be), 6 GHz channelization is defined up to 7.125 GHz
  this aligns with the maximum frequency defined by many regulators for upper 6 GHz band operation (e.g. top of U-NII8 subband)
Currently multiple regulators are engaged in active discussions on enabling unlicensed access in 7-8 GHz band
  e.g. see NTIA’s National Spectrum Strategy (Nov 23) https://www.ntia.gov/sites/default/files/publications/national_spectrum_strategy_final.pdf
  e.g. see US Senate Commerce Cte’s proposed legislation “Spectrum and National Security Act of 2024”
  https://www.commerce.senate.gov/services/files/E29CCF6E-C888- 4037-8938-6983261FFF07

## Slide 3: New channelization
Within this band, the 7.125 – 7.250 GHz range seems particularly promising because many of the federal incumbents in the band are similar to those that operate in the 6 GHz band (e.g., Fixed Microwave Service, Fixed Satellite Service)
  It is likely that the UNII-8 rules could be extended to cover this frequency range
The availability of this range for unlicensed operation would enable one additional 160 MHz channel, immediately adjacent to the currently defined 6 GHz channels
  and, therefore, an additional (overlapping) 320 MHz channel

## Slide 4: Example new channelization per Table E-4
237, 241, 245, 249, 253, 257
235, 243, 251
231, 247
231, 247
239
Note: Adding channels to existing OpClasses, vs defining new OpClasses for the new channels, is TBD
223

## Slide 5: Example new channel map
233
257
227
251
215
247
207
239
191
223
20 MHz
40 MHz
80 MHz
160 MHz
320 MHz-1
7125
7245
= newly defined channels
320 MHz-2

## Slide 6: Proposed next steps
(1) Define channelization in 11bn that covers 7.125-7.250 GHz
  Note: This is in accordance with the frequency range specified in the approved UHR PAR, and therefore does not require any PAR modification
(2) Continue to monitor regulatory progress in defining unlicensed operation above 7.250 GHz in 7-8 GHz band
  Consider PAR modification if it seems likely such additional spectrum will be available in 11bn deployment lifecycle