## Slide 1: Requirements and Functionalities for Multi-AP Coordination
Date: 05-01-2024
Authors:

## Slide 2: Abstract
In this contribution, we highlight the requirements and functionalities of multi-AP coordination for 802.11bn

## Slide 3: Introduction
  Multi-AP (MAP) Coordination is one of the key features considered for IEEE 802.11bn.
  By coordinating among overlapping BSSs, MAP coordination technology promises better network efficiency.
  Different forms of MAP coordination have been discussed—
    Coordinated TWT
    Coordinated TDMA
    Coordinated Spatial Reuse
    Coordinated Beamforming
    Joint Transmission
    Coordinated Channel Usage
    …

## Slide 4: MAP Contributions (Camp-1)
There have been many series of contributions on MAP coordination
These can be broadly grouped into two camps—
Camp-1: Discusses the operations and dynamics of a particular mode of MAP coordination
Example- RTWT:
  What level of protection for RTWT SPs would be needed
    Whether the APs-only or both the APs or STAs end the TXOP before the start of an R-TWT SP?
  How a coordinated AP advertises an RTWT SP originated from a coordinating AP’s BSS
  Whether the existing TWT element can be used or a new element would be needed
Example- TDMA:
  How to extend the current TXOP sharing framework to MAP
  Whether a single trigger frame can indicate TXOP allocation to multiple users
  Extension of MU-RTS TXS trigger frame
  NAV protection rules

## Slide 5: MAP Contributions (Camp-2)
Camp-2: Discusses the same materials as in Camp-1, PLUS discusses or acknowledges the work on—
  How the APs discover each other for MAP coordination
  How to negotiate MAP coordination parameters
  How to modify or terminate an existing MAP negotiation

## Slide 6: Assumptions behind Camp-1
Some contributions avoid discussing the MAP discovery and negotiation phases
Often the underlying assumption for Camp-1 is that MAP coordination is only applicable for managed/enterprise networks.
  In such a network, the APs are usually controlled by a central entity, which can dictate the coordination process among the APs it controls. The APs are often from the same vendor
  Accordingly, the participating APs don’t need to go through any MAP discovery/negotiation steps.

## Slide 7: Camp-2 MAP use-cases
MAP coordination can be a major work item for 11bn
Both the enterprise and non-enterprise/residential scenarios can benefit from MAP technologies.
The specification should provide the necessary tools so that even two APs from different vendors can use MAP coordination—
  Tools to discover the participating APs
  Tools to negotiate/maintain coordination terms and conditions
Disregarding the non-enterprise/residential use cases would be quite restrictive for MAP coordination technology.

## Slide 8: Generalized MAP framework
For different MAP coordination mechanisms, there can be some procedures/steps that are reusable for any mode of MAP coordination
  Other steps/procedures can be specific to a particular mode of MAP coordination (C-TWT, C-TDMA, C-SR, JT etc.)
Example-CTWT:

## Slide 9: Summary
MAP coordination in 802.11bn should support non-enterprise along with the enterprise use cases.
The MAP framework can be generalized where some procedures can be common to all modes of MAP coordination (CTWT, CTDMA, CSR, JT, etc.)

## Slide 10: SP1
Do you want to define in 802.11bn a general framework for coordination among multiple APs?
  The framework should support different forms of MAP coordination, e.g., C-TWT, C-TDMA etc.
  The framework should allow two APs, not necessarily centrally managed or in the same ESS, to discover each other and negotiate on the coordination parameters.