## Slide 1: Channel Switching Between Coordinating APs
Date: 2024-03-07
Authors:

## Slide 2: Abstract
Several aspects of Multi-AP coordination has been actively discussed in 11bn.
  Coordinated TDMA [1]
  Coordinated Spatial Reuse [2]
  Coordinated Beamforming [3]
  Coordinated TWT [4]
Clearly, an AP may want to operate in a channel where it can coordinate with co-channel APs, rather than with APs that it cannot.
In this contribution, we discuss enhancements to AP channel switching to enable APs to operate in channels with other cooperative APs.

## Slide 3: Extended Channel Switch
The Extended Channel Switch Announcement element is used by an AP in a BSS or a STA in an IBSS to advertise when it is changing to a new channel and the channel number of the new channel.
The element may be carried in management frames sent by APs, e.g. Beacon Frames
The reason for changing to a new channel can be due to a Hidden Node Interference Problem in the current channel. The extended channel switch element includes
  New Channel Number – The channel number of the new channel
  Channel Switch Count- the number of TBTTs (beacon intervals) before channel switching
The information New Channel Number and Channel Switch Count can also be carried in a standalone frame called Extended Channel Switch Announcement frame

## Slide 4: Motivation
When an AP belonging in a Multi-AP group switches channel (e.g. avoiding congestion on the current channel), it may lose the benefits of Multi-AP coordination.
- e.g. longer range when two APs can perform joint transmission.
While APs may know by receiving beacons of other APs whether the other AP is channel switching, it is not a reliable mechanism (APs not required to parse beacons of other APs).

## Slide 5: Proposal
Define a mechanism for robust notification of channel switch between APs.
  Channel Switch Notification from one AP to another AP
  Channel Switch Request/Response exchange
The new frames may include a list of channels that an AP may want to switch to.
Details of the mechanism is TBD.

## Slide 6: Conclusion
We have presented a proposal to enhance channel switch mechanism between coordinating APs.
With this mechanism, an AP may be able to request another coordinating AP to switch to a channel together and maintain coordination.

## Slide 7: References
[1] https://mentor.ieee.org/802.11/dcn/23/11-23-1895-00-00bn-c-tdma-frame-sequence.pptx
[2] https://mentor.ieee.org/802.11/dcn/23/11-23-1868-00-00bn-coordinated-spatial-reuse-design.pptx
[3] https://mentor.ieee.org/802.11/dcn/24/11-24-0009-00-00bn-coordinated-beamforming-coordinated-beamforming-for-802-11bn.pptx
[4] https://mentor.ieee.org/802.11/dcn/23/11-23-1916-00-00bn-r-twt-coordination-in-multi-bss.pptx