## Slide 1: Multiple AP Transmissions Using DRU
Date: 2024-03-07
Authors:

## Slide 2: Abstract
Distributed spatial reuse (DRU) was recently agreed for addition in the TGbn Specification Document [1].
DRU can provide transmit power boost for devices operating with low power spectral density limitation.
Several contributions have explored various high level DRU aspects including tone plan, DRU bandwidth and puncturing [2-4]
In this contribution, we consider DRU sharing to OBSS STAs (e.g. Shared APs) to improve the spectral efficiency of DRUs.

## Slide 3: Distributed RU in UL OFDMA
DRU is particularly useful in UL-OFDMA
  All STAs transmit at boosted transmit power
  When there are enough STAs to transmit on all available DRUs, spectral efficiency is also maintained.
PSD limitation of LPI devices is mitigated using DRU during UL OFDMA.
AP
STA1
STA2
STA3

## Slide 4: Maximizing Range and Spectral Efficiency
STA 1
STA 2
STA 1
STA 2
484-tone RRU
484-tone DRU
484-tone DRU
Transmit Power Boost = 2.69 dB
RRU Option
DRU Option 1
DRU Option 2
Transmit Power Boost = 11.14 dB
Transmit power boost gained when using DRU instead of RRU can improve range or throughput.
Two options are possible when using DRU
  Option 1 - The AP allocates all available DRUs to the STAs. The transmit power boost may be limited depending on the number of STAs and spreading BW.
  Option 2 - The AP leaves some DRUs unused to enable higher transmit power per tone. In this option, the transmit power boost can be much higher than Option 1. In some cases, Option 2 may result in higher throughput or range than Option 1.
Propose TGbn to support both Options 1 and 2.
STA 1
STA 2
52-tone DRU
52-tone DRU
Unused
484,242,106,tone DRUs

## Slide 5: Proposal: Further improvements for Option 2
Option 2 intentionally leaves some DRU unused. A further improvement is to allow an OBSS STA (e.g. Slave APs) to use the unused DRUs.
- improves spectral efficiency
- reduced contention from OBSS APs reduces access delay and reduces collisions.
AP 1 controls whether another OBSS STA/AP can access the unused DRU
- when AP 1 is part of a coordinating AP set, AP 1 can explicitly indicate which shared AP can use the unused DRU.
- otherwise, any STA/AP are allowed to transmit (conditions/restrictions are TBD).

## Slide 6: Other considerations
Since the preamble is not transmitted using DRU, interference will occur for the non-DRU portion of the transmission. One solution could be
  Non-DRU portion of PPDU transmitted by OBSS STA use PSR based SR type power control.
  DRU portion of PPDU transmitted by OBSS STA may be transmitted at full boosted transmit power.

## Slide 7: Conclusion
  An AP may choose not to allocate all DRUs to uplink STAs in order to maximize the transmit power boost.
  Some of the unused DRUs may be shared to another AP or STA to increase the spectral efficiency.
  We presented a proposal to enable sharing of the unused DRUs to an OBSS AP or STA.

## Slide 8: References
[1] https://mentor.ieee.org/802.11/dcn/24/11-24-0171-03-00bn-tgbn-motions-list-part-1.pptx
[2] https://mentor.ieee.org/802.11/dcn/23/11-23-1919-00-00bn-dru-proposal.pptx
[3] https://mentor.ieee.org/802.11/dcn/23/11-23-1988-00-00bn-considerations-on-dru-design-and-application.pptx
[4] https://mentor.ieee.org/802.11/dcn/23/11-23-2020-00-00bn-high-level-perspective-on-distributed-tone-ru-for-11bn.pptx