## Slide 1
Date: 2024-03-11
Authors:
Coordinated spatial reuse discussion

## Slide 2: Introduction
11bn PAR defines throughput improvement, latency reduction, packet loss reduction in OBSS environment as a scope of project.
Coordinated spatial reuse in multiple AP environment has been discussed a lot as a mean to achieve the scope.
This contribution compares coordinated spatial reuse proposals from the viewpoint of the period during which spatial reuse is performed and identify common and essential parts of them that can be a baseline and direction of detailed discussion of coordinated spatial reuse.

## Slide 3: 11bn PAR
The approved 11bn PAR defines the Scope of Project as follows:
  The Ultra High Reliability capability is defined for both an isolated Basic Service Set (BSS) and overlapping BSSs as:
    at least one mode of operation capable of increasing throughput by 25%, as measured at the MAC data service Access Point, in at least one Signal to Interference and Noise Ratio (SINR) level (Rate-vs-Range), compared to the Extremely High Throughput MAC/PHY operation, and
    at least one mode of operation capable of reducing latency by 25% for the 95th percentile of the latency distribution compared to the Extremely High Throughput MAC/PHY operation and
    at least one mode of operation capable of reducing MAC Protocol Data Unit (MPDU) loss by 25% compared to the Extremely High Throughput MAC/PHY operation for a given scenario, especially for transitions between BSSs.
The point is that throughput improvement, latency reduction, packet loss reduction in OBSS environment are required.

## Slide 4: Coordinated spatial reuse
Coordinated spatial reuse (C-SR) have been proposed and discussed a lot in UHR SG and TGbn. Evaluation results of performance improvement (throughput improvement, latency reduction) by C-SR have been also presented. [2-10]
  C-SR is generally the simultaneous transmission of one or more APs under certain conditions, although there are some operational differences among proposals.
  SR is defined in 11ax as “the transmission of a physical layer (PHY) protocol data unit (PPDU) on the medium under certain conditions when a PPDU has been detected that would otherwise have prevented the transmission.” and it can be said that the proposed C-SR try to extend this beyond the detection of PPDUs.
C-SR is well aligned with the scope of 11bn PAR, and proposals on standardization are active, so C-SR should be considered as one of 11bn features.

## Slide 5: C-SR schemes
Several schemes of C-SR have been proposed, and focusing on the period during which SR is performed, the following two schemes can be mentioned.
TXOP-based Coordinated Spatial Reuse
  An AP (sharing AP) obtains TXOP and negotiate with other APs. (e.g. collecting information of target SINR, Tx power & MCS decision)
  Sharing AP shares TXOP (e.g. by a trigger) with other APs (shared AP) and initiates transmission.
  Shared APs initiate transmission synchronizing with the sharing AP. (e.g. SIFS after the trigger)
Service-Period based Coordinated Spatial Reuse
  R-TWT scheduling AP decides R-TWT SP and advertises parameters (e.g. Service Period, Max interference level)
  R-TWT scheduling AP initiates transmission to certain STAs during the SP.
  Other APs initiate transmission during the same SP while satisfying the criteria by the sharing AP.

## Slide 6: Pros/cons of each scheme
Each scheme has its own pros/cons and should be used appropriately depending on scenarios. In addition, cons should be technically resolved if possible.
TXOP-based Coordinated Spatial Reuse
  This is opportunistic coordination, so it gives flexibility and can utilize available resource. (pros)
  This is based on the most recent measurement, so more appropriate communication parameters (e.g. Tx power, MCS) can be used. (pros)
  There is an overhead of negotiation per TXOP. (cons)
Service-Period based Coordinated Spatial Reuse
  This is pre-deterministic coordination, so it can operate reliably once SP is scheduled. (pros)
  This is long-term basis, so an overhead of negotiation is small. (pros)
  When the propagation of clients or channel is non-static, the communication parameters become inappropriate. (cons)

## Slide 7: Essential part of both schemes (1/3)
This contribution identifies common and essential parts of both schemes.
  The identified common and essential points can be a baseline and direction of C-SR discussion. It is beneficial to proceed to the detailed discussion of each scheme based on these points.
  This does not exclude other (C-)SR schemes or other AP coordination schemes.
Following points are common and essential parts of both schemes.
  Enabling transmission of a PPDU during a period owned by other AP.
  Enabling AP to allow, in advance, transmission of a PPDU by another AP or a non-AP associated with the other AP during a period owned by the AP.
    The period is TXOP or R-TWT SP.
    Both points are enabled under certain conditions.
  Slide 8 & 9 explain details of these points.

## Slide 8: Essential part of both schemes (2/3)
Both scheme intend to enable transmission of a PPDU during a period owned by other AP.
1. TXOP-based C-SR [2]
2. Service-Period based C-SR [10]
An AP obtains TXOP which is the exclusive communication period for the AP. Normally, other APs cannot transmit during this period because NAV is set.
However, this scheme enables transmission from the other AP during this period (TXOP) when certain conditions (TXOP is shared, Tx power not to interfere, etc.) are met.
An AP obtains TXOP (period).
Transmission from other AP
during the period is enabled.
  R-TWT scheduling AP schedules R-TWT SP which is for communication period for the AP’s BSS. Normally, other APs cannot transmit because the SP is not scheduled for the other APs.
However, this scheme enables transmission from the other AP during this period (R-TWT SP) when certain conditions (SP is announced, satisfying the criteria by the sharing AP, etc.) are met.
Transmission from other AP
during this period is enabled.
R-TWT scheduling AP
schedules R-TWT SP (period).

## Slide 9: Essential part of both schemes (3/3)
Both scheme intend to enable AP to allow, in advance, transmission of a PPDU by another AP or a non-AP associated with the other AP during a period owned by the AP.
  An AP that is a TXOP holder sends e.g. a trigger to share TXOP with other APs allow transmission from them in prior to the transmission.
  An AP that is a TXOP holder negotiates with other APs to decide communication parameters (e.g. Tx power) that is one of conditions of the transmission.
  R-TWT scheduling AP advertises SP which is shared with other APs and allow transmission from them in prior to the transmission.
  R-TWT scheduling AP also advertises communication parameters (e.g. Max interference level) that is one of conditions of the transmission.
1. TXOP-based C-SR [2]
2. Service-Period based C-SR [10]
An AP sends a trigger to share TXOP
with other APs and allow transmission.
R-TWT scheduling AP advertises SP which is shared
with other APs and allow transmission.

## Slide 10: Common remaining issues
Interference measurement
  Both schemes require measurement of at least interference from neighboring AP and/or non-AP for parameter decision.
  Overhead may be an issue depending on the frequency, the number of devices, and the type of information to be fed back.
MCS selection
  Both schemes require MCS selection under interference and it must be compatible with existing link adaptation.
  The effects of poor measurement accuracy should also be considered.
Scenario dependency
  Several evaluation results show that the performance improvement of both schemes is scenario dependent.
  It is expected that the scenario dependency will be resolved by choosing an appropriate scheme or combining both schemes or other coordination schemes such as coordinated beamforming.

## Slide 11: Summary
This contribution reviewed C-SR proposals and compared two schemes, TXOP-based Coordinated Spatial Reuse and Service-Period based Coordinated Spatial Reuse.
This contribution also identified common and essential parts of both C-SR schemes.
This contribution proposed the essential parts as a baseline and direction of C-SR discussion to proceed to the detailed discussion of each scheme.

## Slide 12: References
[1] P802.11bn PAR
[2] 11-22/1822r0 “Recap on Coordinated Spatial Reuse Operation”
[3] 11-23/776r1, “Performance of C-BF and C-SR”
[4] 11-23/1023r2, “Coordinated Spatial Reuse in a 4 AP Topology”
[5] 11-23/1037r0, “Performance of Coordinated Spatial Reuse”
[6] 11-23/1832r0 “Multi-AP Coordinated Spatial Reuse”
[7] 11-23/1972r1 “Evaluation of Coordinated Spatial Reuse - Follow Up”
[8] 11-23/1975r0 “Coordinated spatial re-use for UHR”
[9] 11-24/114r1 “Thoughts on Power Control for CSR”
[10] 11-24/120r0 “Thoughts on Coordinated Spatial Reuse (C-SR)”

## Slide 13: Appendix
Definition in IEEE Std 802.11-2020
transmission opportunity (TXOP): An interval of time during which a particular quality-of-service (QoS) station (STA)
has the right to initiate frame exchange sequences onto the wireless medium (WM).
NOTE—A TXOP is defined by a starting time and a maximum duration
Definition in IEEE P802.11 / D5.0
restricted target wake time (R-TWT) service period (SP): [R-TWT SP] A period of time negotiated using R-TWT setup
(35.8.2 (R-TWT membership setup)) during which R-TWT member stations (STAs) prioritize delivery of latency sensitive
traffic.
service period: [SP] A period of time during which one or more downlink individually addressed frames are transmitted to
a quality-of-service (QoS) station (STA) and/or one or more (portions of) transmission opportunities (TXOPs) are granted or
allocated to the same STA. SPs are either scheduled or unscheduled.

## Slide 14: SP #1
Do you agree to add the following text to the TGbn SFD
  11bn supports transmission of a PPDU on the medium under certain conditions when a period owned by other AP has been identified that would otherwise have prevented the transmission.
  Note: The conditions are TBD.

## Slide 15: SP #2
Do you agree to add the following text to the TGbn SFD
11bn supports a mechanism that enables an AP to allow, in advance, transmission of a PPDU by another AP or a non-AP associated with the other AP on the medium under certain conditions during a period owned by the AP under certain conditions.
  Note: The conditions are TBD.