## Slide 1: Thoughts on low latency traffic transmission
Date: 2024-04-12
Authors:

## Slide 2: Introduction-1
According to PAR [1], one of the goals is to improve low latency and reliability.
In the Scope of the project, related KPIs are described.
  “at least one mode of operation capable of reducing latency by 25% for the 95th percentile of the latency distribution compared to the Extremely High Throughput MAC/PHY operation”
  “at least one mode of operation capable of reducing MAC Protocol Data Unit (MPDU) loss by 25% compared to the Extremely High Throughput MAC/PHY operation for a given scenario, especially for transitions between BSSs.”
In the Need for the Project, applications with higher requirements are described.
  “More stringent requirements are needed to meet the demands of new applications (including metaverse, augmented and virtual reality, robotics, industrial automation for industrial IoT, logistics and smart agriculture).”

## Slide 3: Introduction-2
In applications indicated in PAR (e.g., robotics, industrial automation for industrial IoT, logistics, etc.), there are many STAs and these STAs need low-latency communication.
STAs (STA group) working in the same location or performing the same task need to exchange information (e.g., sensing data, location info., moving route, etc.) at the same timing.
  There may be multiple STA groups
Although it is possible to transmit each STA group using OFDMA/MU-MIMO, all STAs may not multiplex at the same timing.
STA group1
STA group2
AP
STAs require low-latency transmission at the same timing

## Slide 4: Restricted TWT (11be)
Restricted TWT (R-TWT) allows low latency traffic from STAs that are members of the R-TWT membership to be transmitted with higher priority within the scheduled Service Period (SP) [2].
For many STAs to satisfy low latency, it is desirable that the STAs transmit within the R-TWT SP.
Efficient use of R-TWT SP is necessary [3].
  In the current 11be, since AP can control each STA's transmission by trigger frame, priority control of low-latency traffic can be efficiently performed.
  For many STAs to transmit, it is necessary to transmit TB PPDUs at multiple timing, and a trigger frame is required before transmitting a TB PPDU.
  Multiple trigger frame transmissions become overhead and reduce efficiency [4].

## Slide 5: Existing procedure
Trigger frame1
TB PPDU1
Trigger frame2
TB PPDU2
R-TWT SP
AP
STA group1
STA group2
BA
BA
STA group3
Trigger frame3
TB PPDU3
BA
One TB PPDU is transmitted with a trigger frame transmission
  Each TB PPDU may be multiplexed with a STA group.
Trigger frame transmission is required to transmit each TB PPDU
R-TWT SP efficiency degrades as trigger frame transmission increases in the R-TWT SP

## Slide 6: Multiple TB PPDUs transmission in an R-TWT SP
Allow multiple TB PPDUs duration to be transmitted in a trigger-based transmission.
  R-TWT SP is divided into multiple sub-SPs.
    Sub-SPs are set and announced in advance.
  Trigger frame indicates the allocated sub-SP to the STAs.
    On receiving the trigger frame, the STA transmits a TB PPDU in the sub-SP.
Overhead is reduced and R-TWT SP can be used efficiently.
Trigger frame
TB PPDU1
TB PPDU2
R-TWT SP
AP
STA group1
STA group2
BA
BA
Sub-SP1
Sub-SP2
TB PPDU3
BA
Sub-SP3
STA group3

## Slide 7: Multi-Link scenario
In multi-link scenario, when R-TWT SPs among links are aligned, the number of sub-SPs within the aligned R-TWT SP increases and the transmission chance for each STA increase.
Trigger frame1
TB PPDU1-1
R-TWT SP1
AP1
STAs1
BA
BA
Sub-SP1
Sub-SP2
BA
Sub-SP3
Trigger frame2
TB PPDU2-1
AP2
STAs2
BA
BA
BA
TB PPDU2-2
TB PPDU1-2
R-TWT SP2
Sub-SP1
Sub-SP2
Sub-SP3
TB PPDU2-3
TB PPDU1-3
Link1
Link2

## Slide 8: Summary
In this contribution, we shared our thoughts on low latency transmission.
We discussed multiple TB PPDUs transmission in an R-TWT SP when there are many STAs in applications such as robotics, industrial automation for industrial IoT, logistics, etc.
  Multiple TB PPDUs transmission allows multiple TB PPDUs duration (sub-SPs) to be transmitted in a trigger-based transmission.
  Sub-SP is part of R-TWT SP, and one trigger frame indicates the sub-SP to be transmitted for each STA.
  R-TWT SP can be used efficiently by reducing the overhead of trigger frame transmission.
R-TWT SP alignment in multi-link scenario is also effective because it increases the number of sub-SP within the aligned R-TWT SP, resulting in more transmission chances for STAs.

## Slide 9: References
[1] 11-23-0480r3 UHR proposed PAR
[2] IEEE P802.11be/D5.0
[3] 11-23/2022r1 R-TWT for Multi-AP
[4] 11-22/1923r1 Enhanced Trigger-Based Uplink Transmission