## Slide 1: Consideration on C-SR Types
Date: 2024-5-10
Authors:

## Slide 2: Introduction
Coordinated Spatial Reuse (C-SR) is one of the Multi-AP coordination schemes for TGbn
C-SR can improve system throughput with lower complexity in multiple BSS environment
Transmit power control method of C-SR is considered
In this contribution, we considered control information required for each C-SR type and evaluated the throughput and fairness of each C-SR type

## Slide 3: Recap of C-SR
AP which obtains a TXOP and initiates the multi-AP coordination is the sharing AP. AP which is coordinated for multi-AP transmission by the sharing AP is the shared AP[1]
Following two C-SR types are considered
  Optimal coordination[2][3]
    Sharing AP determines Tx power for each AP by using measurement information of OBSS transmitted from associated STA and OBSS AP
    Prerequisites for maximizing throughput need to be considered
  One-way coordination[4]
    Sharing AP determines own Tx power without using measurement information transmitted from OBSS AP
    Shared AP determines own Tx power based on the transmit parameter of sharing AP
    Low overhead compared to optimal coordination
Optimal
coordination
One-way
coordination

## Slide 4: C-SR sequence
Measurement phase
  Each STA measures RSSI from OBSS AP by using beacon signal
  AP requests STAs in its BSS to transmit measurement report including RSSI from OBSS AP
  AP calculates pathloss a), b) based on the Tx power and RSSI of the measurement report received from the associated STAs
  The role of each AP (sharing AP/shared AP) is not decided in this phase
AP1
AP2
STA
1
STA
2
a)
b)
c)
d)
RSSI of d)
RSSI of c)
Calculate pathloss of a)
Calculate pathloss of b)

## Slide 5: C-SR sequence
Multi-AP Request
  AP1 that has acquired TXOP becomes a sharing AP and notifies shared AP of Multi-AP coordination method (JT, C-BF, C-SR etc.) by using Multi-AP request frame
  If two C-SR control types are defined, the frame requesting C-SR indicates one of the C-SR control types (optimal or one-way).
  The Multi-AP request frame has the following additional information depending on C-SR type
    Optimal coordination: no additional information
    One-way coordination: Acceptable Tx power of AP2 (maximum Tx power of AP2)
AP1
AP2
STA
1
STA
2
a)
b)
c)
d)

## Slide 6: C-SR sequence
Multi-AP Response
  Shared AP notifies whether it can participate in notified Multi-AP coordination method by using Multi-AP response frame
  If shared AP can participate in notified Multi-AP coordination method, Multi-AP response frame has the following additional information depending on C-SR type
    Optimal coordination: Acceptable Receiver Interference Level (ARIL) of STA2 and pathloss of b), c)
    One-way coordination: no additional information
AP1
AP2
STA
1
STA
2
a)
b)
c)
d)

## Slide 7: C-SR sequence
Multi-AP Trigger
  Sharing AP receives the multi-AP response frame and, if the shared AP can cooperate, notifies scheduling information (transmission timing, frequency resources) necessary for Multi-AP coordination by Multi-AP trigger frame
  In optimal coordination, sharing AP notifies destination STA ID and Tx power for each shared AP
  In one-way coordination, sharing AP may notify acceptable Tx power of AP2 by Multi-AP trigger frame

## Slide 8: Simulation Setup
  Parameter
  Eq(1): Pathloss =
    𝑑 = max(2D distance[m], 1)
    = 5[GHz]
    𝑊 = number of walls traversed
Simulation Environment
  Layout
    One AP and one STA are placed in each 15[m] x 10[m] room
    STAs are deployed with a granularity of 1[m]
Frequency, Bandwidth | 5[GHz], 80[MHz]
Tx Power | -10 ~ 20[dBm]
Tx/Rx Antenna | (AP, STA) = (4, 2)
Stream | 2 per STA
Precoding | SVD
MCS index | 0 ~ 11
Fading Model | Model-D
Noise Figure | 7 [dB]
Path loss model | Eq.(1)
AP2
AP1
STA1
STA2
15[m]
10[m]
1
2
3
4
5
6
7
8
9
10
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
0
0
x[m]
y[m]
16[m]

## Slide 9: Comparison Methods
TDMA
  Sharing AP transmits maximum Tx power and MCS
  Shared AP doesn’t transmit
Optimal coordination
  Sharing AP determines Tx power and MCS of each AP to maximize system throughput
Optimal coordination, MaxMCS
  Sharing AP uses same MCS as TDMA
  Tx power of each AP determined based on pathloss between each AP and STA and ARIL of STA

## Slide 10: Comparison Methods
One-way coordination
  Sharing AP determines own Tx power that satisfies SINR of the target MCS based on pathloss between sharing AP and destination STA as following
    TxPowerSharing AP = INDestination STA,max + SINRrequired + PathlossSharing AP, Destination STA
    INDestination STA,max = RSSIShared AP beacon
  Sharing AP also determines acceptable Tx power of shared AP as following
    AcceptableTxPowerShared AP = ARILDestination STA + PathlossShared AP, Destination STA
  Shared AP determines Tx power less than or equal to AcceptableTxPowerShared AP based on ARIL of destination STA of shared AP

## Slide 11: Simulation Result
Comparing the throughput CDF of each C-SR type
Optimal coordination can achieve maximum throughput but will be less fairness
One-way coordination can achieve throughput and fairness equivalent to optimal coordination_MaxMCS
5%-tile throughput

## Slide 12: Summary
We considered control information used in C-SR and evaluated the throughput for each C-SR type
Optimal coordination showed high throughput with large overhead
One-way coordination showed throughput higher than TDMA and lower than optimal coordination with less overhead while guaranteeing fairness

## Slide 13: References
[1] Edward Au (Huawei), “Compendium of straw polls and potential changes to the Specification Framework Document Part 2,” 20/1935r66, May, 2022
[2] Kanke Wu (Qualcomm), “Performance of Coordinated Spatial Reuse,” 23/1037r0, June, 2023
[3] Kosuke Aio (Sony), “Evaluation of Coordinated Spatial Reuse - Follow Up,” 23/1972r1, November, 2023
[4] Jonghun Han (Samsung), “Coordinated Spatial Reuse: Focus on Downlink,” 20/590r5, May, 2020