## Slide 1: In-Device Coex and P2P—Follow-up
Date: 07-01-2024
Authors:

## Slide 2: Abstract
In this contribution, we provide some of the potential enhancements to 802.11 to better support aperiodic/unscheduled/urgent in-device coexistence for WLAN devices.

## Slide 3: Introduction
Improving the in-device coexistence (co-ex) for WLAN STAs is important to enhance the performance and reliability of the overall network [1-5].
Co-ex event may occur due to interaction with—
  Other Wi-Fi devices: E.g., peer-to-peer (P2P) communication
  Non-Wi-Fi devices: E.g., Bluetooth, Ultra-wideband (UWB)
During the co-ex event, a STA may not be able to communicate with another STA (/AP) using the agreed-upon parameters. New co-ex constraints can be on--
  Period of operation: co-ex event overlapping with existing expected transmissions/reception time
  Frequency: co-ex event happening on a specific frequency
  Spatial streams: co-ex event reducing the receive NSS capability
Better addressing the in-device coexistence issues should be one of the critical goals for the TGbn group.

## Slide 4: Handling In-Device Co-existence Issues
In general, for predictable/periodic and non-urgent co-ex events, the STA (/AP) can notify the other AP(/STA) ahead of time about the upcoming unavailability for operation
  Existing technologies defined in 802.11, such as peer-to-peer TWT, can be used or enhanced to support these co-ex events
For unschedule/urgent co-ex events, a TXOP-level intervention is needed
  The STA(/AP) can indicate within a TXOP the reduced capability of operation due to the co-ex events
  Control frames can be used to make such indications—
    Timing information indication
    Truncated TXOP
    Reduced BW
    Reduced RX NSS etc.
    Other parameters?
This contribution is focused on unscheduled/urgent coex handling without detailing the exact frame format.

## Slide 5: Same Co-Ex Event for a Peer STA
Co-ex events for a STA (the “Co-ex STA”) often involve Wi-Fi or Non-Wi-Fi operation with another STA
  The other STA can be referred to as a “Co-ex Peer STA”
The constraints that are applicable for the Co-ex STA are often also applicable for the Co-ex Peer STA.
  Both STAs can be associated with the same AP
The Co-ex Peer STA also needs to handle the joint co-ex events
  As a co-ex event responder, in comparison with the co-ex event initiator, the Co-ex Peer STA may have even less opportunity to handle the co-ex events in time (e.g. with the AP)

## Slide 6: Proxy Co-Ex Indication (PCI)
The Co-ex STA, as a TXOP holder or TXOP responder, should be able to identify the Co-ex Peer STA when informing the AP about the co-ex events.
The AP can operate with both STAs with the knowledge that both STAs have the same co-ex events and, as a result, similar constraints.
  For example, due to non-responsiveness to transmissions during the co-ex event, the AP may not take any punitive action (e.g. reducing MCS) against either of the STAs

## Slide 7: Example: Proxy Co-Ex Indication (PCI)
In the figure, instead of RTS/CTS, other control/control response frames can also be used
In the figure, CTS/Response frame contains the time information beyond which both STA1 and STA2 will be unavailable due to co-ex events.

## Slide 8: TXOP Request for handling coex (1)
The STA that has the coex event may also have active P2P links.
For urgent coex event, the STA under the coex constraint, as a TXOP responder, won’t get a chance to inform its impending unavailability to its peer STAs or P2P groups.

## Slide 9: TXOP Request for handling coex (2)
When the STA with coex event indicates its coex constraints to the TXOP holder, it can also indicate a request for a portion of TXOP from the TXOP holder.
The TXOP holder can allocate a portion of its TXOP to the STA so that the STA can use the received TXOP to inform its peer STAs/P2P groups about its impending unavailability.
11be TXOP sharing procedure can be used for TXOP allocation.

## Slide 10: TXOP Request for handling coex (3)
The TXOP holder might have initiated the frame exchange sequence with ICR-ICF exchange [Not shown in the figure]
If ICR-ICF used, the TXOP responder could also indicate its TXOP request in the ICF (e.g. CTS+)

## Slide 11: Summary
Better handling of the in-device coexistence is important for efficient and reliable UHR operation.
While informing the AP about a co-ex event, the STA, along with other reduced capability parameters, can also include information about the Co-ex Peer STA for fast co-ex signaling for the peer STA.
To inform peer STA or P2P groups about the impending unavailability due to coex constraints, the STA can request the TXOP holder for TXOP sharing.

## Slide 12: References
[1] Liwen Chu, et.al., IEEE 802.11-23/1934r0, “In-device interference mitigation follow up”.
[2] Alfred Asterjadhi, et.al., IEEE 802.11-23/1964r0, “Coexistence Protocols for UHR”.
[3] Laurent Cariou, et.al., IEEE 802.11-23/2002r1, “In-device coexistence and interference follow – up”.
[4] Brian Hart, et.al., IEEE 802.11-23/2026r0, “Balanced In-Device Coexistence”.
[5] Rubayet Shafin, et.al., IEEE 802.11-24/509r1, “Thoughts on in-device coexistence and P2P for 11bn”

## Slide 13: Straw Poll-1
SP: Do you support defining a mechanism so that a STA that is a TXOP responder or a TXOP holder can indicate in a frame the following—
  - How long the STA will be available
  - Whether the STA will be unavailable after a specific point in time and for how long it will remain unavailable
  - Identification of a peer STA for which the unavailability indication also applies
  - Whether the STA requests for a TXOP from the TXOP holder, if the STA is the TXOP responder.