## Slide 1: Peer-to-Peer TWT for Handling Coex and P2P
Date: 07-01-2024
Authors:

## Slide 2: Abstract
In this contribution, we provide some of the potential enhancements to 802.11 to better support in-device coexistence for WLAN devices.

## Slide 3: Introduction
Improving the in-device coexistence (co-ex) for WLAN STAs is important to enhance the performance and reliability of the overall network [1-4].
Co-ex event may occur due to interaction with—
  Other Wi-Fi devices: E.g., peer-to-peer (P2P) communication
  Non-Wi-Fi devices: E.g., Bluetooth, Ultra-wideband (UWB)
During the co-ex event, a STA may not be able to communicate with another STA (/AP) using the agreed-upon parameters. New co-ex constraints can be on--
  Period of operation: co-ex event overlapping with existing expected transmissions/reception time
  Frequency: co-ex event happening on a specific frequency
  Spatial streams: co-ex event reducing the receive NSS capability
Better addressing the in-device coexistence issues should be one of the critical goals for the TGbn group.

## Slide 4: Handling In-Device Co-existence Issues
In general, for predictable and non-urgent co-ex events, the STA (/AP) can notify the other AP(/STA) ahead of time about the upcoming unavailability for operation
  Existing technologies defined in 802.11, such as peer-to-peer TWT, can be used or enhanced to support these co-ex events
For urgent co-ex events, a TXOP-level intervention is needed
  The STA(/AP) can indicate within a TXOP the reduced capability of operation due to the co-ex events
  Control frames can be used to make such indications—
    Truncated TXOP
    Reduced BW
    Reduced RX NSS etc.

## Slide 5: Background: Peer-to-Peer TWT
Peer-to-peer TWT was introduced in the baseline to indicate to the AP the periodic unavailability of the STA due to coex/P2P communication.
The baseline channel usage procedure was extended to facilitate peer-to-peer TWT.
  Instead of TWT Setup frame, the non-AP STA sends a Channel Usage Request frame and include a TWT element to request to set up a peer-to-peer TWT schedule with the AP
Once, a peer-to-peer TWT schedule is set up with the non-AP STA, the AP does not send any downlink frame to the non-AP STA and does not solicit uplink frame from the non-AP STA.

## Slide 6: Need for Enhancements
For TWT operation--due to the lack of granularity in the TWT interval units, once the TWT has been setup, it is expected that there would be a mismatch between traffic arrival time and the TWT SP start time.
Also, if the AP has a P2P link, the AP clock and the P2P group’s clock may get unsynchronized over time, we may need to re-align the TWT SP start time.
For Peer-to-peer TWT, there needs to be a mechanism to update/revise the peer-to-peer TWT SP start time so that it is aligned with the coex/P2P start time

## Slide 7: Flexible Peer-to-peer TWT
We need a mechanism to flexibly change the subsequent peer-to-peer TWT SP start time

## Slide 8: Flexible Peer-to-peer TWT: Example

## Slide 9: Summary
Peer-to-peer TWT is important for handling coex events
For effective unavailability indication using peer-to-peer TWT, it would be essential to devise a mechanism to update the start time of the subsequent SPs in a sequence of peer-to-peer TWT SPs.

## Slide 10: References
[1] Liwen Chu, et.al., IEEE 802.11-23/1934r0, “In-device interference mitigation follow up”.
[2] Alfred Asterjadhi, et.al., IEEE 802.11-23/1964r0, “Coexistence Protocols for UHR”.
[3] Laurent Cariou, et.al., IEEE 802.11-23/2002r1, “In-device coexistence and interference follow – up”.
[4] Brian Hart, et.al., IEEE 802.11-23/2026r0, “Balanced In-Device Coexistence”.
[5] Rubayet Shafin, et.al., IEEE 802.11-24/509r1, “Thoughts on in-device coexistence and P2P for 11bn”