## Slide 1: Further considerations on coordinated TWT
Date: 01-18-2024
Authors:

## Slide 2: Abstract
  Multi-AP (MAP) Coordination is one of the key features considered for UHR SG and IEEE 802.11bn.
    TWT-based multi-AP coordination is considered one of the candidate technologies for UHR[1-9].
    Different modes of TWT coordination were discussed.
    In this contribution, we follow up specifically on the R-TWT version of the TWT-based MAP coordination.

## Slide 3: Coordinated R-TWT (C-R-TWT)
  In the end-to-end C-R-TWT operation, some phases can be part of the generalized MAP framework, while others would be R-TWT-specific procedures.
  For the generalized segments (Discovery and Param neogitation), all the MAP coordination techniques can use the same vehicle/ information container.

## Slide 4: MAP Discovery for C-R-TWT
  Discovery for C-RTWT:
    In this phase, the C-R-TWT initiating AP advertises/announces its intent for R-TWT-based MAP coordination to other APs.
      Basic C-R-TWT-related capabilities and other coordination information can be included in the advertisement
      Schedule information can optionally be shared during the discovery phase.
    An AP that receives the C-R-TWT announcement from the initiating AP and is willing to participate in the C-R-TWT coordination should respond to the announcement.
      The responder AP should include its C-R-TWT capability information in its response.
    Capability information may include support for different modes of C-R-TWT

## Slide 5: MAP Negotiation for C-R-TWT
  Negotiation for C-RTWT:
    In this phase, the C-R-TWT initiating AP gets into explicit parameter negotiation with an AP that responded to the initiating AP’s C-R-TWT advertisement.
      1-to-1 Request-response based approach
      Responding AP also suggest alternative param set it can support
      The responding AP can also be referred to as a coordinated AP.
    Negotiating parameters (minimum set):
      Schedule timing information: TWT, wake duration, and interval mantissa and exponent
      Schedule persistence
      Mode of C-R-TWT (see slide 7)
      Schedule identifier (can be different than B-TWT ID used for intra-BSS operation)
    Can either repurpose the existing TWT element or come up with a new container

## Slide 6: Example frame exchange for Disc. and Negotiation
  For C-R-TWT
    The MAP Announcement and MAP Preparedness frame can include an indication of R-TWT-based coordination and the corresponding capability information.
    The MAP Request and Response frames may include exact C-R-TWT negotiation parameters.

## Slide 7: SP1
Do you agree to define in 11bn a multiple AP coordination mechanism based on target wake time (TWT) information exchanged between the participating APs?
Such a mechanism would be referred to as coordinated TWT (C-TWT)

## Slide 8: SP2
Do you agree to define in 11bn a variant of TWT-based multi-AP coordination where the participating APs coordinate with each other exchanging restricted TWT schedule information?
Such a mechanism would be referred to as coordinated restricted TWT (C-R-TWT)

## Slide 9: SP3
Do you agree to define in 11bn different modes of coordinated R-T-TWT schedule?
Different modes can correspond to different levels of protection offered by the C-R-TWT coordinated AP for the C-R-TWT initiating AP.

## Slide 10: SP4
Do you agree to define in 11bn a mechanism to allow a C-R-TWT coordinated AP to make a distinction, during the intra-BSS schedule advertisement, between a schedule originated in the C-R-TWT coordinated AP’s BSS and a schedule originated in the C-R-TWT initiating AP’s BSS?

## Slide 11: References
[1] IEEE 802.11-21/1046r0, “Multi-AP: TWT Information Sharing”, Rubayet Shafin, et.al., July 2021.
[2] IEEE 802.11-22/1530r1, “Multi-AP coordination for next-generation Wi-Fi”, Rubayet Shafin, et.al., Sept 2022.
[3] IEEE 802.11-23/932r0, “Follow-up on TWT-based Multi-AP Coordination”, Rubayet Shafin, et.al., May 2023.
[4] IEEE 802.11-23/226r1, “Coordination of R-TWT for Multi-AP Deployment”, Abdel Karim Ajami, et.al., April 2023
[5] IEEE 802.11-23/250r0, “AP coordination with R-TWT”, Liwen Chu, et.al., April 2023
[6] IEEE 802.11-23/291r0, “R-TWT Multi-AP Coordination”, Muhammad Kumail Haider, et.al., May 2023.
[7] IEEE 802.11-23/297r0, “r-TWT for Multi-AP”, Laurent Cariou, et.al., April 2023
[8] IEEE 802.11-23/355r0, “Enhanced rTWT and MAP operation”, Hanqing Lou, et.al., May 2023
[9] IEEE 802.11-23/771r0, “Coordinated R-TWT Protection in Multi-BSS”, SunHee Baek, et.al., June 2023.