## Slide 1
MAP Set Operation

## Slide 2: Introduction
Several contributions discussed the uniform MAP coordination framework.
e.g. a general MAP coordination procedure in [2]:
Also, several contributions[3]--[7] agree that one AP(Sharing AP) shares its partial TXOP to another AP(Shared AP) via a Trigger frame in C-TDMA scheme.
In this contribution, we will discuss the MAP coordination framework in MBSSID set and co-hosted BSSID set scenario

## Slide 3: Recap MBSSID set and co-hosted BSSID set feature
Characteristic for both:
  Share the same operating class, channel, receive antenna connector, and transmit antenna connector
  The maximum number of BSSIDs can up to 28 =256 in one co-hosted or MBSSID set(Set)
  All BSSIDs in the Set compete the channel and transmit DL traffics in TDMA manner
2.4GHz radio
AP11 SP
Period=100ms
AP12 SP
AP13 SP
AP14 SP

## Slide 4: The problem in the proposed uniformed MAP coordination framework
Overhead issue
  Assume each AP in one Set need to set up agreement with another AP in the second Set before MAP coordination transmission, there will be CM1 * CN1= M*N times agreement frames exchange in the air.
AP11
AP12
AP13
AP14
CH36/5GHz
Router1
AP21
AP22
AP23
AP28
Router2
...............................................
CH36/5GHz
Complex issue
  Considering each radio may add or delete BSSIDs from Set at any time, AP level agreement will become more complicated.
    Adding or deleting AP(s) from AP set(e.g via ML reconfiguration) may cause new signaling(set-up new agreement, agreement break down etc.) sending to its peer AP.

## Slide 5: Motivation
We propose a uniformed MAP Set coordination framework
  All APs including either or both MBSSID set and co-hosted BSSID set on one radio consists an AP Set
  The MAP coordination framework like Discovery, Agreement,etc. should be MAP Set level
  AP Set may have it own EDCA parameter to compete the channel
  MAP Trigger frame should include the identifier of its peer AP Set, and the peer AP Set decide how to allocate the granted TXOP to it APs internally. e.g. which AP makes the response.

## Slide 6: The following figure depicts an example of MAP Set agreement
AP11
AP12
AP13
AP14
router1
AP21
AP22
AP23
AP28
router2
...............................................
CH36/5GHz
CH36/5GHz
AP Set1
AP Set2
MAP Set
agreement
request
MAP Set
agreement
response

## Slide 7: The following figure depicts an example of the MAP Set transmission under the proposed C-TDMA scheme
AP Set1
(AP11,AP12.. AP1X)
AP Set2
(AP21,AP22..AP2Y)
In-BSS
AP21 In-BSS
Time shared to AP Set2
In-BSS
t
t
AP12 In-BSS
Time shared to AP Set1
T1
T2
T3
T4
TF
TF
T3

## Slide 8: Summary
Analysis the potential issues on MAP coordination framework in co-hosted BSSID and MBSSID scenario
Propose MAP Set coordination framework to address the overhead issue

## Slide 9
THANK YOU 

## Slide 10: Reference
[1]802.11bn PAR
[2]23/1871r2 M-AP Coordinated Transmission framework
[3]24/0093 C-TDMA NAV setting
[4]24/0227 TXOP Protection in C-TDMA
[5]24/0375 NAV protection for C-TDMA
[6]24/0382 Further Considerations on Coordinated TDMA
[7]24/0411 TXOP Return in C-TDMA

## Slide 11: SP1
Do you agree 11bn SFD should have the following definition of AP set under MAP coordination scheme.
    AP set: A set of all the affiliated APs including either or both of MBSSID set and co-hosted BSSID set on one radio

## Slide 12: SP2
Do you agree 11bn SFD should define a uniformed MAP set operation?
Note: MAP set operation includes MAP set discovery, agreement, co-ordination transmission etc.