## Slide 1: Considerations for Low Latency Application Support in Next Generation WLANs
Date: 2024-07-24
Authors:

## Slide 2: Abstract
EDCA continues to serve as the primary channel access method for Wi-Fi networks and will likely maintain this status well into the future.
Channel access delay plays a crucial role in determining the achievable latency performance.
In this contribution, we explore ways to enhance low latency application support via
  TXOP limit reduction
  Enhanced EDCA based operation
  These methods hold potential for enhancing support for low-latency applications [1-3]

## Slide 3: Support for New LL Applications in Wi-Fi
There has been a growing interest to provide enhanced support in Wi-Fi for a number of emerging applications.
  Cloud gaming, AR VR, industrial automation[4-6], etc.
A number of these applications typically have low throughput but extremely tight latency requirements [7-10]
  E.g., inter-packet/burst arrival period of 100+ millseconds but packets need to be sent with a few milliseconds upon enqueue.

## Slide 4: Channel Access Delays – The Next Frontier!
A key bottleneck that determines achievable latency is the channel access delay.
Factors such as amount of time spent deferring to other transmissions, backoff counters, etc. contribute to tail latency in Wi-Fi.
Reducing the time taken by such factors can enhance support for low latency applications.
Which factor to address in the solution depends on the range in which the application latency requirement falls.
STA 1
5 ms
Defer to STA2’s transmission
Defer to STA3’s transmission
Defer to STA4’s transmission
LL packet arrival
BO: 12
End of successful transmission
36μs
DIFS + 27μs
DIFS + 27μs
DIFS + 18μs
5 ms
5 ms
STA1
STA2
STA3
STA10
…
Channel access delay

## Slide 5: No One-Size-Fits-All Solution
 | Range for delay tolerance d = delay tolerance, CA = legacy channel access delay | Example values of d | Example applications | Feature requirements
1. | d ≤ TXOP limit | Few milliseconds | Real time gaming, AR/VR | Enable packet transmission before the end of the TXOP. E.g., preemption (Not addressed in this contribution)
2. | TXOP limit < d ≤ CA | Close to 10 milliseconds | Real time gaming, AR/VR, cloud gaming, some real time video applications, robotics, industrial automation, etc. | Traffic may survive not being served in the same TXOP where it arrives but cannot incur a long channel access delay. Solution that can enable channel access faster than legacy channel access are needed
3. | CA delay << d | Few 10s of milliseconds | Video call, audio call, non-real time services such as streaming, web browsing, file downloads, etc. | Legacy channel access (Not address in this contribution)
Analysis of feature requirement for LL applications

## Slide 6: Problem Illustration
STA 1
5 ms
Defer: STA2 TX/RX
LL packet arrival
BO: 12
36μs
DIFS + 27μs
DIFS + 27μs
DIFS + 18μs
5 ms
5 ms
STA2
App 2: 40 ms latency
STA3
App 3: 50 ms latency
…
Time when STA1 can get channel access
Packet expiration
STA1
App 1: 10 ms latency
STA10
Defer: STA3 TX/RX
Defer: STA4 TX/RX
Application in case 2 cannot incur a long channel access delay.
Solutions that can enable channel access faster than legacy channel access are needed

## Slide 7: Solution Approach
In this contribution, we explore two approaches that can be used jointly to solving this problem:
  1. Reduction of TXOP limits: controlling amount of defer time to other devices.
  2. Enhanced EDCA: authorize device running case 2 LL application with an EDCA parameter set that enables it to access channel faster than legacy channel access.
STA 1
2 ms
LL packet arrival
BO: 7
36μs
DIFS + 18μs
2 ms
DIFS +
9μs
Time when STA1 can get channel access
Packet expiration
…
STA2
App 2: 40 ms latency
STA3
App 3: 50 ms latency
STA1
App1: 10ms latency
STA2 TX/RX
STA3 TX/RX
Auth. for Enhanced EDCA

## Slide 8: High Level Procedure
High Level Procedure:
  STA can inform the AP about its LL requirements. E.g., via SCS setup
  If STA fits in case 2, AP can authorize the STA for enhanced EDCA and provide the STA with an EDCA parameter set that results in higher priority to the wireless medium.
  AP can further reduce TXOP limits for other STAs in the network.
  AP/STA can terminate the authorization for the STA when necessary. E.g., when case 2 LL app session ends.
STA
AP
LL session setup
Auth. for enhanced EDCA.
AP shares a new EDCA parameter set
Channel access with enhanced EDCA parameter set
Authorization termination
STA returns to normal EDCA parameters
AP can reduce TXOP limits if necessary

## Slide 9: Discussion on TXOP Limit Reduction
There can be some challenges with TXOP limit reduction
  It can limit the throughput of high throughput applications.
  Some 11ac and prior implementations are known to ignore TXOP limits advertised by the AP [4].
But…
  Its under AP’s control. AP can tune it based on the requirements of different devices.
  Also, bulk bytes are transmitted on the downlink. AP limiting the TXOP for the downlink can already handle a lot of cases.

## Slide 10: Discussion About Enhanced EDCA Parameter Set
The design principle is already used in Wi-Fi 7 for EPCS to achieve a similar objective. How can this jointly work with EPCS?
  The proposed framework operates under AP’s guidance.
  AP is also involved in EPCS authorization.
  AP can take steps to ensure no harm occurs to EPCS operation. E.g., de-authorize LL device for enhanced EDCA parameter set.
  But this is expected to be a rare occurrence.

## Slide 11: Conclusion
11bn should consider enhancements for EDCA for better support of even lower latency applications.
In this contribution, we discuss requirements for LL applications based on the delay requirement range.
We propose solutions based on extension of legacy procedures:
  TXOP limit reduction coupled with
  Enhanced EDCA operation

## Slide 12: Straw Poll 1
Do you agree to improve EDCA to reduce tail access delay of low latency traffic? Note: The solution can operate under the guidance/supervision of the AP to limit impact to legacy use cases.
  Yes
  No
  Abstain

## Slide 13: Straw Poll 2
Do you agree that the AP can authorize select STAs to use an enhanced EDCA parameter set to reduce channel access delays?
  Yes
  No
  Abstain

## Slide 14: References
[1] Szott, Szymon, et al. "Impact of contention window cheating on single-hop IEEE 802.11 e MANETs." IEEE WCNC, 2008.
[2] Szott, Szymon, Marek Natkaniec, and AndrzejR Pach. "An IEEE 802.11 EDCA model with support for analysing networks with misbehaving nodes." EURASIP Journal, 2010.
[3] Z. Lu, W. Wang and C. Wang, "On Order Gain of Backoff Misbehaving Nodes in CSMA/CA-based Wireless Networks," 2010 Proceedings IEEE INFOCOM, 2010
[4] Consideration of Industrial Automation Scenarios, IEEE 802.11-23/0815
[5] Discussion on bounded delay in Industrial Scenarios, IEEE 802.11-24,0443
[6] Cloud VR Use Case and Requirements, IEEE 802.11-22/0952
[7] Polupanova, Marina. "VR Traffic Dataset on Broad Range of End-User Activities." Data 8.8 (2023): 132.
[8] Salehi, S.; Alnajim, A.; Zhu, X.; Smith, M.; Shen, C.C.; Cimini, L. Traffic Characteristics of Virtual Reality over Edge-enabled Wi-Fi Networks. 2020.
[9] Cheng, Ruizhi, et al. "Are we ready for metaverse? A measurement study of social virtual reality platforms." ACM IMC 2022.
[10] STA TXOP Frame Bursting Testing, WFA, 2020
[11] A Custura, R Secchi, and G Fairhurst. "Exploring DSCP modification pathologies in the internet." Computer Communications 127 (2018): 86-94

## Slide 15: Appendix

## Slide 16: Issues with STA-side Internal Reassignment
Typical case 2 traffic such as gaming traffic is usually marked for BE.
There are multiple user side hacks which can enable an internal reassignment of the packets. E.g., DSCP remarking, bleaching, etc.
Such solutions when employed by the user from the STA side often worsen the end to end situation instead of improving it
  Priority inversions on the backbone. See [11] as an example.
  Breaks application layer closed control mechanisms to determine priority levels.
  Negative treatment from backbone components resulting in increased end to end packet loss…