## Slide 1: Time-domain A-PPDU for Collision Reduction and Priority Access
Date: 2024-04-25
Authors:
Name | Affiliation | Address | Phone | Email
Ning Gao | OPPO |  |  | gaoning1@oppo.com
Chaoming Luo |  |  |  | luochaoming@oppo.com
Liuming Lu |  |  |  | luliuming@oppo.com
Yapu li |  |  |  | liyapu1@oppo.com
Liangxiao Xin |  |  |  | v-xinliangxiao@oppo.com
Dong Wei |  |  |  | v-dong.wei@oppo.com

## Slide 2: Introduction
Compared with EHT, UHR aims at increasing throughput by 25%, reducing MPDU loss by 25% as well as reducing the latency by 25% for the 95th percentile of the latency distribution.
However, collisions will result in a waste of channel, retransmission as well as a large delay or jitter due to the double backoff mechanism, so collision reduction could help UHR with all three goals. [1,4,5]
Meanwhile, there is a strong demand for priority channel access of UHR STAs which have low latency traffic. [2,3]
In this contribution, we intend to introduce a Time-domain A-PPDU to achieve the collision reduction and the priority access at the same time.

## Slide 3: Proposed: Time-domain A-PPDU
Compared with EDMG A-PPDU, the proposed Time-domain A-PPDU is a concatenation of two independent and complete PPDUs (i.e. a First PPDU and a Second PPDU).
  The two PPDUs can use different PPDU formats (e.g. a non-HT PPDU & an UHR PPDU).
  The two PPDUs are able to carry distinct frames (e.g. a Data frame & a Control frame).
The purpose of the First PPDU is to create a guard interval to protect the Second PPDU from overlapping with other PPDUs.
  A longer First PPDU provides better protection but leads to more overhead.
  The available length of the First PPDU within a single BSS should be announced by the AP which is the same as EDCA Parameters Set.
Time-domain A-PPDU format:

## Slide 4: How to use the Time-domain A-PPDU
A UHR STA with low latency traffic (i.e. STA 1 in figure bellow) could contend for the channel by transmitting a Time-domain A-PPDU while following the EDCA rule.
If a collision happens, due to the existence of the First PPDU, the Second PPDU is able to present on the medium later than other PPDUs.
Therefore, the TXOP responder (i.e. AP in figure bellow) could detect and receive the Second PPDU successfully which includes a RTS frame and then response a CTS frame to STA 1.
In this way, STA 1 obtains the channel with priority and this collision is avoided.

## Slide 5: Analysis
Advantages
  Reduce collision and double backoff
  Priority Access for LL UHR STA
  Limited influence on the fairness
    EDCA is still there
    Improved tail latency at the cost of worse minimum latency, a trade-off.
Disadvantages
  Extra constant latency overhead due to the duration of the First PPDU
    Maybe 1~2ms, but it is negligible when compared with overall latency(10~100ms).
    Also, the First PPDU could be used to transmit low QoS requirement traffics.
  Collisions may still happen
    Collison is inevitable in a distributed system, can be reduced but never eliminated.
    In this scheme, an A-PPDU may conflict with another A-PPDU or a long single PPDU. But these collisions are reasonable and can be solved by double backoff.
  Hidden Node Problem
    The First PPDU is without protection as it is transmitted before a RTS/CTS exchange.

## Slide 6: An Alternate of Time-domain A-PPDU
Alternate
The proposed time-domain A-PPDU also can be achieved by transmitting the First PPDU and the Second PPDU with a SIFS interval, which is already supported by the 802.11.
The way to use this alternate is the same as the Time-domain A-PPDU.
This alternative method is easier for implementation compared with A-PPDU.

## Slide 7: Summary
A Time-domain A-PPDU is proposed in this contribution to achieve collision reduction as well as priority access at the same time.
The Time-domain A-PPDU is composed of a First PPDU and a Second PPDU
  The First PPDU is used to create a guard interval to protect the Second PPDU from overlapping with other PPDUs.
  The Second PPDU is carrying the intended frame.
The format or length of the First PPDU can be seen as another kind of EDCA parameter.
An alternate of the Time-domain A-PPDU is also supplied.

## Slide 8: Reference
[1] 11-22-1519-00-0uhr-requirements-of-low-latency-in-uhr
[2] 11-23-1065-00-0uhr-low-latency-channel-access
[3] 11-23-2126-00-00bn-low-latency-channel-access-follow-up
[4] 11-24-0284-01-00bn-low-latency-low-collision-low-power-uhr-medium-access
[5] 11-24-0031-00-00bn-deterministic-backoff

## Slide 9: Appendix: EDMG A-PPDU
The EDMG A-PPDU defined in 11ay is a concatenation of EDMG PPDUs shown as bellow.
The first PPDU of an EDMG A-PPDU includes L-STF, L-CEF, L-Header, EDMG-Header-A, EDMG-STF, EDMG-CEF, and Data fields, and each subsequent PPDU includes EDMG-Header-A and Data fields only.