## Slide 1: Thoughts on STF Design for DRU
Date: 2024-05-10
Authors:
Name | Affiliations | Address | Phone | Email
Bo Gong | Huawei |  |  | gongbo8@huawei.com
Chenchen Liu |  |  |  | liuchenchen1@huawei.com
Jian Yu (Ross) |  |  |  | ross.yujian@huawei.com
Ming Gan |  |  |  | ming.gan@huawei.com

## Slide 2: Introduction
For DRU design, we have lots of discussion on transmission mode [1], tone plan [2]-[3] and pilot designs [4]-[5].
In this proposal, we give some thoughts on STF design for DRU.
May 2024

## Slide 3: If inheriting STF transmission for rRU
For rRU, the part of STF sequence which falls within the selected rRU is transmitted. Taking STF for TB PPDU in 20MHz as an example, if 26-tone RU6 with tone indexes 17:42 is selected, STF sequence part in the red circle will be transmitted.
Consider that the way of STF transmission for rRU is inherited directly for DRU, which means the part of STF sequence overlapped with DRU is transmitted. Taking STF for TB PPDU in 20MHz as an example, for half of 26-tone DRU with positive tone indexes, STF sequence part in the red circle with tone indexes 48 and 104 will be transmitted.

## Slide 4
If inheriting STF transmission for rRU
If the way of STF transmission for rRU is inherited directly for DRU, there exists the following issues.
  For the same size DRUs, the number of tones in STF is not fixed, which increases the implementation complexity;
  For some DRUs, the number of tones in STF is too small, which cannot guarantee the power measurement accuracy;
  For some DRUs, the intersection of the non-zero tones in STF and Data is null.
Taking 26-tone DRUs in 40M as an example.
26-tone DRU1: [-233 -208 -194 -181 -156 -142 -129 -104 -90 -77 -52 -37 -23 18 33 47 74 89 103 130 145 159 186 201 215 242 ]
26-tone DRU2 : [-232 -206 -180 -154 -128 -50 -36 -22 -8 6 20 34 48 62 76 90 104 118 132 146 160 174 188 202 216 230 ]
26-tone DRU3 : [-219 -193 -167 -141 -115 -49 -35 -21 -7 7 21 35 49 63 77 91 105 119 133 147 161 175 189 203 217 231 ]
Intersection with Nonzero tone indexes of STF for TB PPDU -240:8:240
[-208 -104 ]
[-232 -128 -8 48 104 160 216]
Null

## Slide 5: Principles of STF Design for DRU
Guarantee the power measurement accuracy.
  Transmit STF in the whole distribution bandwidth.
  Apply CSD on per stream of per user to avoid unintended beamforming.
May 2024
Simplify the implementation as much as possible.
  Reuse the current STF sequence, e.g. STF for TB PPDU or STF for MU PPDU.
  Reuse the current CSD values.

## Slide 6: Principles of CSD Design for DRU
Conduct global CSD assignment.
  For high correlated scenarios, e.g. collocated users and LOS path and so on, it is more safer than local CSD.
May 2024
Avoid CSD collision as much as possible, e.g., if the number of the required CSD values is smaller than the total number of CSD values, no collision is permitted.
  Example-1: Indicate CSD values in trigger frame.
  Example-2: Establish a mapping between CSD indexes and DRU user indexes.

## Slide 7: Summary
In this proposal, we share our thoughts on STF design for DRU. On the one hand, whole bandwidth STF transmission and global CSD assignment are proposed to guarantee the accuracy of the power measurement; on the other hand, reusing the current STF sequence and CSD values are considered for simplify the implementation.
May 2024

## Slide 8: References
[1] 11-23-2020-01-00bn-high-level-perspective-on-distributed-tone-ru-for-11bn
[2] 11-23-2021-00-00bn-principle-and-methodology-for-dru-tone-plan-design
[3] 11-24-0468-01-00bn-DRU tone plan for 11bn
[4] 11-24-0501-01-00bn-pilot design considerations for DRU
[5] 11-24-0402-01-00bn-20MHz tone plan and pilot design for DRU
May 2024

## Slide 9: Straw Poll #1
May 2024
Do you agree to add the following text to the TGbn SFD?
- In UHR-STF for DRU, the current STF tone plan and sequence of 11ax/11be are reused.
Y/N/A: //
Note: Some harmonization based on [24/0749r1, 24/0753r1]

## Slide 10: Straw Poll #2
May 2024
Do you agree to add the following text to the TGbn SFD?
-In UHR-STF for DRU,
- STF sequence depends on PPDU BW.
- Occupied STF tones are the same as that of the largest RRU corresponding to the distribution BW within PPDU BW.
Y/N/A: //
Note: Some harmonization based on [24/0749r1, 24/0753r1]

## Slide 11
Straw Poll #3
May 2024
Do you agree to add the following text to the TGbn SFD?
  - In UHR-STF for DRU, CSD is applied to per stream of per user.
Y/N/A: //

## Slide 12
Straw Poll #4
May 2024
Do you agree to add the following text to the TGbn SFD?
  - In UHR-STF for DRU, CSD is assigned to each user globally.
Y/N/A: //

## Slide 13
Straw Poll #5
May 2024
Do you agree to add the following text to the TGbn SFD?
  - In UHR-STF for DRU, current CSD values of 11ac/11ax/11be are reused.
Y/N/A: //

## Slide 14
Straw Poll #6
May 2024
Do you agree to add the following text to the TGbn SFD?
  - In UHR-STF for DRU, if the number of the required CSD values is smaller than the total number of the CSD values, no collision is permitted.
Y/N/A: //